# Configuration guide
A JPPF grid is composed of many distributed components interacting with each other, often in different environments. While JPPF will work in most environments, the default behavior may not be appropriate or adapted to some situations. Much of the behavior in JPPF components can thus be modified, fine-tuned or sometimes even disabled, via numerous configuration properties. These properties apply to many mechanisms and behaviors in JPPF, including:

- network communication
- management and monitoring
- performance / load-balancing
- failover and recovery

Any configuration property has a default value that is used when the property is not specified, and which should work in most environments. In practice, this means that JPPF can work without any explicitely specified configuration at all.

For a full list of the JPPF configuration properties, do not hesitate to read the chapter Appendix A: configuration properties reference of this manual.
## Configuration file specification and lookup
All JPPF components work with a set of configuration properties. The format of these propertiesis as specified in the Java Properties class. To enable a JPPF component to retrieve thiese properties file, their source must be specified using one of the two, mutually exclusive, system properties:

- jppf.config.plugin = class_name, where class_name is the fully qualified name of a class implementing either the interface JPPFConfiguration.ConfigurationSource, or the interface JPPFConfiguration.ConfigurationSourceReader, enabling a configuration source from any origin, such as a URL, a distributed file system, a remote storage facility, a database, etc.
- jppf.config = path, where path is the location of the configuration file, either on the file system, or relative to the JVM's classpath root. If this system property is not specified, JPPF will look for a default file named "jppf.properties" in the current directory or in the classpath root.

Example use:

java -Djppf.config.plugin=my.own.Configuration ...

or

java -Djppf.config=my/folder/myFile.properties ...

The configuration file lookup mechanism is as follows:

1. if jppf.plugin.config is specified
  a) instantiate an object of the specified class name and read the properties via the stream provided by this object's getPropertyStream() or getPropertyReader() method, depending on which interface it implements.
  b) if, for any reason, the stream cannot be obtained or reading the properties from it fails, go to 3.
2. else if jppf.config is specified
  1. look for the file in the file system
  2. if not found in the file system, look in the classpath
  3. if not found in the classpath use default configuration values
3. if jppf.config is not specified
  1. use default file "jppf.properties"
  2. look for "jppf.properties" in the file system
  3. if not found in the file system, look for it in the classpath
  4. if not found in the classpath use default configuration values

A practical side effect of this mechanism is that it allows us to place a configuration file in the classpath, for instance packaged in a jar file, and override it if needed with an external file, since the the file system is always looked up first.

## Includes, substitutions and scripted values in the configuration
### Includes
A JPPF configuration source, whether as a file or as a plugin, can include other configuration sources by adding one or more “#!include” statements in the following format:

#!include source_type source_path

The possible values for source_type are “file”, “url” or “class”. For each of these values, source_path has a different meaning:

- when source_type is “file”, source_path is the path to a file on the file_system or in the JVM's classpath. If the file exists in both classpath and file system, the file system will have priority over the classpath. Relative paths are interpeted as relative to the JVM's current user directory, as determined by System.getProperty(“user.dir”).

- when source_type is “url”, source_path is a URL pointing to a configuration file. It must be a URL such that the JVM can open a stream from it.

- when source_type is “class”, source_path is the fully qualified class name of a configuration plugin, i.e. an implementation of either JPPFConfiguration.ConfigurationSource or JPPFConfiguration.ConfigurationSourceReader.

Examples:

# a config file in the file system
#!include file /home/me/jppf/jppf.properties

# a config file in the classpath
#!include file META-INF/jppf.properties

# a config file obtained from a url
#!include url http://www.myhost.com/jppf/jppf.properties

# a config file obtained from a configuration plugin
#!include class myPackage.MyConfigurationSourceReader

Includes can be nested without any limit on the nesting level. Thus, you need to be careful not to introduce cycles in your includes. If that happens, JPPF will catch the resulting StackOverflowException and display an error message in the console output and in the log.
### Substitutions in the values of configuration properties
The JPPF configuration can handle a syntax of the form “propertyName = prefix${otherPropertyName}suffix”, where prefix and suffix are arbitrary strings and ${otherPropertyName} is a placeholder referencing another property, whose value will be substituted to the placeholder. If you have experience with Apache Ant, this syntax is very similar to the way Ant properties are used in a build script.

Let's take an example illustrating how this works. The following property definitions:

prop.1 = value1
prop.2 = ${prop.1}
prop.3 = value3 ${prop.2}
prop.4 = value4 ${prop.2} + ${prop.3}

will be resolved into:

prop.1 = value1
prop.2 = value1
prop.3 = value3 value1
prop.4 = value4 value1 + value3 value1

Note 1: the order in which the properties are defined has no impact on the resolution of substitutions.

Note 2: substitutions are resolved after all includes are fully resolved and loaded.

Unresolved substitutions

A referenced property is unresolvable if, and only if, it refers to a property that is not defined or it is involved in a resolution cycle. In this case, the value of the unresolved value will be the literal syntax in its initial definition, that is in the literal form “${otherPropertyName}”. Let's illustrate this with examples.

In the following configuration:

prop.1 = ${prop.2}

the value of “prop.1” will remain “${prop.2}”, since the property “prop.2” is not defined.

In this configuration:

prop.1 = ${prop.2}
prop.2 = ${prop.3} ${prop.1}
prop.3 = value3

“prop.1” and “prop.2” introduce an unresolvable cycle, and only the reference to “prop.3” can be fully resolved. According to this, the final values will be:

prop.1 = ${prop.2}
prop.2 = value3 ${prop.1}
prop.3 = value3

Environment variable substitutions

Any reference to a property name in the form “env.variableName” will be substituted with the value of the environment variable whose name is “variableName”. For example, if the environment variable JAVA_HOME is defined as “/opt/java/jdk1.7.0”, then the following configuration:

prop.1 = ${env.JAVA_HOME}/bin/java

will be resolved into:

prop.1 = /opt/java/jdk1.7.0/bin/java

If the value of a property refers to an undefined environment variable, then the reference will be replaced with the literal syntax in its initial definition, that is in the literal form “${env.<UndefinedVariable>}”.

System properties substtutions

References to system properties work in exactly the same way as for environment variables, except that the prefix for a system property reference is "sys." instead of "env.". The syntax for the reference is then "${sys.systemPropertyName}".

For example, if the Java command includes an option "-DTest.property=some.test.value", then the following configuration property:

prop.1 = ${sys.Test.property}

will be resolved into:

prop.1 = some.test.value

### Scripted property values
The values of configuration properties can be partially or complety computed as expressions written in any JSR 223-compliant dynamic script language. Such properties contain one or more expressions of the form:

my.property = $script:language:source_type{script_source}$

Where:

- language is the script language to use, such as provided by the javax.script APIs. It defaults to "javascript"
- source_type determines how to find the script, with possible values "inline", "file" or "url". It defaults to "inline"
- script_source is either the script expression, or its location, depending on the value of source_type:
- if source_type = inline, then script_source is the script itself.
  For example: my.prop = $script:javascript:inline{"hello " + "world"}$
- if source_type = file, then script_source is a script file, looked up first in the file system, then in the classpath.
  For example: my.prop = $script:javascript:file{/home/me/myscript.js}$
- if source_type = url, then script_source is a script loaded from a URL.
  For example: my.prop = $script:javascript:url{file:///home/me/myscript.js}$

If the language or source type are left unspecified, they will be assigned their default value. For instance the following patterns will all resolve in language = 'javascript' and source_type = 'inline' :

$script{ 2 + 3 }$
$script:{ 2 + 3 }$
$script::{ 2 + 3 }$
$script::inline{ 2 + 3 }$
$script:javascript{ 2 + 3 }$
$script:javascript:{ 2 + 3 }$

The default script language can be specified with the property 'jppf.script.default.language'. This property is always evaluated first, in case it is also expressed with script expressions (which can only be in javascript). If it is not specified explicitely, it will default to 'javascript'. For example, in the following:

# using javascript expression to set the default language to groovy
jppf.script.default.language = $script{ 'groo' + 'vy' }$
# inline expression using default language 'groovy'
my.property = $script{ return 2 + 3 }$

The value of 'my.property' will evaluate to 5, resulting from the inline groovy expression 'return 2 + 3'.

The scripts are evaluated after all includes and variable substitutions have been resolved. This will allow the scripts to use a variable binding for the Properties (or TypedProperties object) being loaded, with the best possible accuracy. For example, in the following:

prop.1 = hello world
prop.2 = $script:javascript{ thisProperties.getString('prop.1') + ' of scripting' }$

the value of 'prop.2' will evaluate to 'hello world of scripting', which is the value of 'prop.1' to which another string is concatenated. The predefined variable thisProperty is bound to the properties object being evaluated. Note that the same result can be achieved with a property substitution:

prop.1 = hello world
prop.2 = $script:javascript{ '${prop.1}' + ' of scripting' }$

Here, the substitution of ${prop.1} is performed before the script evaluation, and must be enclosed within quotes to be parsed as a string literal inside the script.

Finally, property values can contain any number of script expressions, which can be written in different script languages and loaded from different sources. For example, the value of the following property:

prop.1 = hello $script:javascript{'my ' + 'world'}$ number $script:groovy{return 2 + 3}$

will evaluate to 'hello my world number 5'.
## Reminder: JPPF topology
Before reviewing the details of each configuration property, it is useful to have the big picture of what we are configuring exactly. In a few words, a JPPF grid is made of clients (instances of your applications), servers and nodes. An application submits jobs to a server, and a server distributes the tasks in each job to its attached nodes. The simplest configuration you can have would be as illustrated in this picture:

We can see here that we have a single client communicating with one server, to which a single node is attached. In practice, there will be many nodes attached to the server, and many clients will be able to communicate with the server concurrently. It is also possible to link servers together, forming a peer-to-peer network of JPPF servers, allowing servers to delegate a part of their workload to other servers.
We could effectively build a much more complex JPPF network, such as the one in this picture:

The role of the configuration will be essentially to determine where each component can find the others, and how their interactions will be processed.
## Configuring a JPPF server
### Basic network configuration
The server network communication mechanism uses TCP/IP. To do its basic work of receiving jobs and dispatching them for execution, one TCP port is required:

In the configuration file, this property would be defined as follows, with its default value:

# JPPF server port
jppf.server.port = 11111

Notes:
- not defining this property is equivalent to assigning it its default value.
- dynamic port allocation: when the port number is set to 0, JPPF will dynamically allocate a valid port number. Note that this feature is mostly useful when server discovery is enabled.
### Server discovery
By default, JPPF nodes and clients are configured to automatically discover active servers on the network. This is made possible because, by default, a JPPF server will broadcast the required information (i.e. host address and port numbers) using the UDP multicast mechanism. This mechanism itself is configurable, by setting the following properties:

# Enable or disable automatic discovery of JPPF drivers
jppf.discovery.enabled = true
# UDP multicast group to which drivers broadcast their connection parameters
jppf.discovery.group = 230.0.0.1
# UDP multicast port to which drivers broadcast their connection parameters
jppf.discovery.port = 11111
# How long a driver should wait between 2 broadcasts, in milliseconds
jppf.discovery.broadcast.interval = 1000

# IPv4 address inclusion patterns
jppf.discovery.broadcast.include.ipv4 =
# IPv4 address exclusion patterns
jppf.discovery.broadcast.exclude.ipv4 =
# IPv6 address inclusion patterns
jppf.discovery.broadcast.include.ipv6 =
# IPv6 address exclusion patterns
jppf.discovery.broadcast.exclude.ipv6 =

The values indicated above are the default values. Note that, given the nature of the UDP protocol, the broadcast data is transient, and has to be re-sent at regular intervals to allow new nodes or clients to find the information. The broadcast interval property allows some control over the level of network traffic ("chattyness") thus generated.

The last four properties define inclusion and exclusion patterns for IPv4 and IPv6 addresses. Each of them defines a list of comma- or semicolumn- separated patterns. The IPv4 patterns can be exppressed in either CIDR notation, or in a syntax defined in the Javadoc for the class IPv4AddressPattern. Similarly, IPv6 patterns can be expressd in CIDR notation or in a syntax defined in IPv6AddressPattern. This allows restricting the network interfaces on which to broadcast the server information: the server will only broadcast from the host's addresses that are included and not excluded.
### Connecting to other servers
We have seen in the "reminder" section that servers can connect to each other, up to a full-fledged peer-to-peer topology. When a server A connects to another server B, A will act as a node attached to B (from B's perspective). Based on this, there are 4 possible kinds of connectivity between 2 servers:

- A and B are not connected at all
- A is connected to B (i.e. A acts as a node attached to B)
- B is connected to A (i.e. B acts as a node attached to A)
- A and B are connected to each other
#### Orphan servers
As of JPPF 5.1, the default behavior when a server doesn't have any attached node (i.e.orphan server) is, for the peer servers it is connected to, to not send any job to this server. Servers are automatically notified of the number of nodes attached to their peers, and will start sending jobs their way as soon as they have at least one node.
To force a server to send jobs to their peers even when they don't have any node, for instance if you wish to set a server as a router to other servers, you can set the following property in its configuration:

# ingore the fact that peer servers may not have any node; default to false
jppf.peer.allow.orphans = true
#### Configuring peer connections
There are 2 ways to define a connection from a server to other servers on the network:

Using automatic discovery

In this scenario, we must enable the discovery of peer servers:

# Enable or disable auto-discovery of other peer servers (defaults to false)
jppf.peer.discovery.enabled = true

For this to work, the server broadcast must be enabled on the peer server(s), and the properties defined in the previous "server discovery" section will be used, hence they must be set to the same values on the other server(s). A server can discover other servers without having to broadcast its own connection information (i.e. without being "discoverable").

Please note that the default value for the above property is "false". Setting the default to "true" would imply that each server would connect to all other servers accessible on the network, with a high risk of unwanted side effects.

Manual connection to peer servers

This will be best illustrated with an example configuration:

# define a space-separated list of peers to connect to
jppf.peers = server_1 server_2
# connection to server_1
jppf.peer.server_1.server.host = host_1
jppf.peer.server_1.server.port = 11111
# connection to server_2
jppf.peer.server_2.server.host = host_2
jppf.peer.server_2.server.port = 11111

To connect to each peer, we must define its IP address or host name as well as a port number. Please note that the value we have defined for "jppf.peer.server_1.server.port" must be the same as the one defined for "jppf.server.port" in server_1's configuration, and the value for "jppf.peer.server_1.server.port" must be equal to that of "jppf.server.port" in server_1's configuration.

Using manual configuration and server discovery together

It is possible to use the manual configuration simultaneously with the discovery, by adding a special driver name, “jppf_discovery”, to the list of manually configured peers:

# enable auto-discovery of other peer servers
jppf.peer.discovery.enabled = true
# specifiy both discovery and manually configured drivers
jppf.peerss = jppf_discovery server_1
# connection to server_1
jppf.peer.server_1.server.host = host_1
jppf.peer.server_1.server.port = 11111
### JMX management configuration
JPPF uses JMX to provide remote management capabilities for the servers, and uses the default JMXMP connector for communication.

The management features are enabled by default; this behavior can be changed by setting the following property:

# Enable or disable management of this server
jppf.management.enabled = true

When management is enabled, the following properties must be defined:

# JMX management host IP address. If not specified (recommended), the first non-local
# IP address (i.e. neither 127.0.0.1 nor localhost) on this machine will be used.
# If no non-local IP is found, localhost will be used.
jppf.management.host = localhost
# JMX management port, used by the remote JMX connector
jppf.management.port = 11198

Let's see in more details the usage of each of these properties:

- jppf.management.host: defines the host name or IP address for the remote management and monitoring of the servers and nodes. It represents the host where an RMI registry is running. When this property is not defined explicitely, JPPF will automatically fetch the first non-local IP address (meaning not the loopback address) it can find on the current host. If none is found, ''localhost'' will be used. This provides a way to use an identical configuration for all the servers on a network.
- jppf.management.port: defines the port number for connecting to the remote Mbean server. The default value for this property is '''11198'''. If 2 nodes, 2 drivers or a driver and a node run on the same host, they must have a different value for this property.

Note: if a management port is already in use by another JPPF component or application, JPPF will automatically increment it, until it finds an available port number. This means that you can in fact leave the port numbers to their default values (or not specify them at all), as JPPF will automatically ensure that valid unique port numbers are used.
### Load-balancing
The distribution of the tasks to the nodes is performed by the JPPF driver. This work is actually the main factor of the observed performance of the framework. It consists essentially in determining how many tasks will go to each node for execution, out of a set of tasks sent by the client application. Each set of tasks sent to a node is called a "bundle", and the role of the load balancing (or task scheduling) algorithm is to optimize the performance by adjusting the number of task sent to each node.

The algorithm to use is configured with the following property:

jppf.load.balancing.algorithm = <algorithm_name>

The algorithm name can be one of those prefefined in JPPF, or a user-defined one. We will see how to define a custom alogrithm in the Extending and Customizing JPPF section of this manual. JPPF has predefined load-balancing algorithms to compute the distribution of tasks to the nodes, each with its own configuration parameters:

- “manual” : each bundle has a fixed number of tasks, meaning that each will receive at most this number of tasks
- “autotuned” : adaptive heuristic algorithm based on a simulated annealing technique
- “proportional” : an adaptive deterministic algorithm based on the contribution of each node to the overall mean task execution time
- “rl” : adaptive algorithm based on an artificial intelligence technique called “reinforcement learning”
- “nodethreads” : each bundle will have at most n * m tasks, where n is the number of threads in the node to which the bundle is sent is sent, and m is a user-defined parameter

For a detailed explanation of the load-balancing, its APIs and the predefined algorithms, please refer to the Load Balancing section of this manual.

The predefined possible values for the property jppf.load.balancing.algorithm are thus: manual, autotuned, proportional, rl and nodethreads. If not specified, the algorithm defaults to manual. For example:

jppf.load.balancing.algorithm = proportional

Each algorithm uses its own set of parameters, which define together a strategy for the algorithm, It is also called a performance profile or simply profile, and we will use these terms interchangeably. A strategy has a name that serves to identify a group of parameters and their values, using the following pattern:

jppf.load.balancing.profile = <profile_name>

jppf.load.balancing.profile.<profile_name>.<parameter_1> = <value_1>
...
jppf.load.balancing.profile.<profile_name>.<parameter_n> = <value_n>

Using this, you can define multiple profiles and easily switch from one to the other, by simple changing the value of jppf.load.balancing.profile. It is also possible to mix, in a single profile, the parameters for multiple algorithms, however it is not recommended, as there may be name collisions.

To illustrate this, we will give a sample profile for each of the predefined algorithms:

“manual” algorithm

# algorithm name
jppf.load.balancing.algorithm = manual
# name of the set of parameter values or profile for the algorithm
jppf.load.balancing.profile = manual_profile
# "manual" profile
strategy.manual_profile.size = 1

“autotuned” algorithm

# algorithm name
jppf.load.balancing.algorithm = autotuned
# name of the set of parameter values or profile for the algorithm
jppf.load.balancing.profile = autotuned_profile
# "autotuned" profile
jppf.load.balancing.profile.autotuned_profile.size = 5
jppf.load.balancing.profile.autotuned_profile.minSamplesToAnalyse = 100
jppf.load.balancing.profile.autotuned_profile.minSamplesToCheckConvergence = 50
jppf.load.balancing.profile.autotuned_profile.maxDeviation = 0.2
jppf.load.balancing.profile.autotuned_profile.maxGuessToStable = 50
jppf.load.balancing.profile.autotuned_profile.sizeRatioDeviation = 1.5
jppf.load.balancing.profile.autotuned_profile.decreaseRatio = 0.2

“proportional” algorithm

# algorithm name
jppf.load.balancing.algorithm = proportional
# name of the set of parameter values or profile for the algorithm
jppf.load.balancing.profile = proportional_profile
# "proportional" profile
jppf.load.balancing.profile.proportional_profile.initialSize = 5
jppf.load.balancing.profile.proportional_profile.performanceCacheSize = 1000
jppf.load.balancing.profile.proportional_profile.proportionalityFactor = 1

“rl” algorithm

# algorithm name
jppf.load.balancing.algorithm = rl
# name of the set of parameter values or profile for the algorithm
jppf.load.balancing.profile = rl_profile
# "rl" profile
jppf.load.balancing.profile.rl_profile.performanceCacheSize = 3000
jppf.load.balancing.profile.rl_profile.performanceVariationThreshold = 0.001

“nodethreads” algorithm

# algorithm name
jppf.load.balancing.algorithm = nodethreads
# name of the set of parameter values or profile for the algorithm
jppf.load.balancing.profile = nodethreads_profile
# means that multiplicator * nbThreads tasks will be sent to each node
jppf.load.balancing.profile.nodethreads_profile.multiplicator = 1

### Server process configuration
A JPPF server is in fact made of two processes: a “controller” process and a “server” process. The controller launches the server as a separate process and watches its exit code. If the exit code has a pre-defined value of 2, then it will restart the server process, otherwise it will simply terminate. This mechanism allows the remote (eventually delayed) restart of a server using the management APIs or the management console. It is also made such that, if any of the two processes dies unexpectedly, then the other process will die as well, leaving no lingering Java process in the OS.

The server process inherits the following parameters from the controller process:

- location of jppf configuration (-Djppf.config or -Djppf.config.plugin)
- current directory
- environment variables
- Java class path

It is possible to specify additional JVM parameters for the server process, using the configuration property jppf.jvm.options, as in this example:

jppf.jvm.options = -Xms64m -Xmx512m

Here is another example with remote debugging options:

jppf.jvm.options = -server -Xmx512m \
 -Xrunjdwp:transport=dt_socket,address=localhost:8000,server=y,suspend=n

It is possible to specify additional class path elements through this property, by adding one or more “-cp” or “-classpath” options (unlike the Java command which only accepts one). For example:

jppf.jvm.options = -cp lib/myJar1.jar:lib/myJar1.jar -Xmx512m \
  -classpath lib/external/externalJar.jar

If a classpath element contains one or more spaces, the path(s) if defines must be surrounded with double quotes:

jppf.jvm.options = -Xmx512m -cp "dir with spaces/myJar1.jar" -cp NoSpaces/myJar2.jar
### Configuring a local node
Each JPPF driver is able to run a single node in its own JVM, called ”local node”. The main advantage is that the communication between server and node is much faster, since the network overhead is removed. This is particularly useful if you intend to create a pure P2P topology, where all servers communicate with each other and only one node is attached to each server.

To enable a local node in the driver, use the following configuration propoerty, which defaults to “false”:

jppf.local.node.enabled = true

Please note:

- the local node can be configured using the same properties as described in the Node Configuration section, except for the network-related properties, since no network is involved between driver and local node
- for the same reason, the SSL configuration does not apply to a local node
### Recovery from hardware failures of nodes
Network disconnections due to hardware failures are notoriously difficult to detect, let alone recover from. JPPF implements a configurable mechanism that enables detecting such failures, and recover from them, in a reasonable time frame. This mechanism works as follows:

- the node establishes a specific connection to the server, dedicated to failure detection
- at connection time, a handshake protocol takes place, where the node communicates a unique id (UUID) to the server, that can be correlated to other connections for this node (i.e. job server and distributed class loader)
- at regular intervals (heartbeats), the server will send a very short message to the node, which it expects the node to acknowledge by sending a short response of its own
- if the node's response is not received in a specified time frame, and this, a specified number of times in a row, the server will consider the connection to the node broken, will close it cleanly, close the associated connections, and handle the recovery, such as requeing tasks that were being executed by the node for execution on another node

In practice, the polling of the nodes is performed by a “reaper” object that will handle the querying of the nodes, using a pool of dedicated threads rather than one thread per node. This enables a higher scalability with a large number of nodes.
The ability to specify multiple attempts at getting a response from the node is useful to handle situations where the network is slow, or when the node or server is busy with a high CPU utilization level.On the server side, the parameters of this mechanism are configurable via the following properties:

# Enable recovery from hardware failures on the nodes. Defaults to false (disabled).
jppf.recovery.enabled = false
# Maximum number of attempts to get a response form the node before the
# connection is considered broken. Default value is 3.
jppf.recovery.max.retries = 3
# Maximum time in milliseconds allowed for each attempt to get a response
# from the node. Default value is 6000 (6 seconds).
jppf.recovery.read.timeout = 3000
# Dedicated port number for the detection of node failure. Defaults to 22222.
jppf.recovery.server.port = 22222
# Interval in milliseconds between two runs of the connection reaper.
# Defaults to 60000 (1 minute).
jppf.recovery.reaper.run.interval = 60000
# Number of threads allocated to the reaper.
# Default value is the number of available CPUs.
jppf.recovery.reaper.pool.size = 8

Important note: given the implementation of this mechanism, you must be careful to keep some consistency between the server and node settings. As a general rule of thumb, the settings should always satisfy the following constraint:
serverReaperInterval < nodeMaxRetries * nodeTimeout
This rule applies between any server and node, as well as between any two servers if you enabled communication between servers in your configuration.

Note: if server discovery is active for a node, then the port number specified for the driver will override the one specified in the node's configuration.
### Parallel I/O
The JPPF driver uses several pools of threads to perform network I/O with the nodes, clients and other drivers in parallel. There is a single configuration property that specifies the size of each of these pools:

  jppf.transition.thread.pool.size = <number_of_io_threads>

When left unspecified, this property will take a default value equal to the number of processors available to the JVM (equivalent to Runtime.getRuntime().availableProcessors()).
### Redirecting the console output
In some situations, it might be desirable to redirect the standard and error output of the driver, that is, the output of System.out and System.err, to files. This can be accomplished with the following properties:

# file on the file system where System.out is redirected
jppf.redirect.out = /some/path/someFile.out.log
# whether to append to an existing file or to create a new one
jppf.redirect.out.append = false

# file on the file system where System.err is redirected
jppf.redirect.err = /some/path/someFile.err.log
# whether to append to an existing file or to create a new one
jppf.redirect.err.append = false

By default, a new file is created each time the driver is started, unless “jppf.redirect.out.append = true” or “jppf.redirect.err.append = true” are specified. If a file path is not specified, then the corresponding output is not redirected.
### Resolution of the nodes IP addresses
You can switch on or off the DNS name resolution for the nodes connecting to this driver, with the following property:

# whether to resolve the nodes' ip addresses into host names
# defaults to true (resolve the addresses)
org.jppf.resolve.addresses = true

## Node configuration
### Server discovery
By default, JPPF nodes are configured to automatically discover active servers on the network. As we have seen in 5.4.2, this is possible thanks to the UDP broadcast mechanism of the server. On the other end, the node needs to join the same UDP group to subscribe to the bradcasts from the server, which is done by configuring the following properties:

# Enable or disable automatic discovery of JPPF drivers
jppf.discovery.enabled = true

# UDP multicast group to which drivers broadcast their connection parameters
jppf.discovery.group = 230.0.0.1
# UDP multicast port to which drivers broadcast their connection parameters
jppf.discovery.port = 11111

# How long in milliseconds the node will attempt to automatically discover a driver
# before falling back to the manual configuration parameters
jppf.discovery.timeout = 5000
# IPv4 address inclusion patterns
jppf.discovery.include.ipv4 =
# IPv4 address exclusion patterns
jppf.discovery.exclude.ipv4 =
# IPv6 address inclusion patterns
jppf.discovery.include.ipv6 =
# IPv6 address exclusion patterns
jppf.discovery.exclude.ipv6 =

For the node to actually find a server on the network, the values for the group and port must be the same for a node and at least one server. If multiple servers are found on the network, the node will arbitrarily pick one.

Note the property jppf.discovery.timeout: if defines a fall back strategy that wil cause the node to connect to the server defined in the manual configuration parameters (see manual configuration) after the specified time.

The last four properties define inclusion and exclusion patterns for IPv4 and IPv6 addresses. Each of them defines a list of comma- or semicolumn- separated patterns. The IPv4 patterns can be exppressed in either CIDR notation, or in a syntax defined in the Javadoc for the class IPv4AddressPattern. Similarly, IPv6 patterns can be expressd in CIDR notation or in a syntax defined in IPv6AddressPattern. This enables filtering out unwanted IP addresses: the discovery mechanism will only allow addresses that are included and not excluded.

Let's take for instance the following pattern specifications:

jppf.discovery.include.ipv4 = 192.168.1.
jppf.discovery.exclude.ipv4 = 192.168.1.128-

The equivalent patterns in CIDR notation would be:

jppf.discovery.include.ipv4 = 192.168.1.0/24
jppf.discovery.exclude.ipv4 = 192.168.1.128/25

The inclusion pattern only allows IP addresses in the range 192.168.1.0 ... 192.168.1.255
The exclusion pattern filters out IP addresses in the range 192.168.1.128 ... 192.168.1.255
Thus, we actually defined a filter that only accepts addresses in the range 192.168.1.0 ... 192.168.1.127

Instead of these 2 patterns, we could have simply defined the following equivalent inclusion pattern:

jppf.discovery.include.ipv4 = 192.168.1.-127

or, in CIDR notation:

jppf.discovery.include.ipv4 = 192.168.1.0/25

### Manual connection configuration
If server discovery is disabled, network access to a server must be configured manually. To this effect, the node requires the address of host on which the server is running, and a TCP port, as shown in this example:

# IP address or host name of the server
jppf.server.host = my_host
# JPPF server port
jppf.server.port = 11111

Not defining these properties is equivalent to assigning them their default value (i.e. “localhost” for the host address, 11111 or 11143 for the port number, depending on whether SSL is disabled or enabled, respectively).

### JMX management configuration
JPPF uses JMX to provide remote management capabilities for the nodes, and uses the JMXMP connector for communication.

The management features are enabled by default; this behavior can be changed by setting the following property:

# Enable or disable management of this node
jppf.management.enabled = true

When management is enabled, the following properties must be defined:

# JMX management host IP address. If not specified (recommended), the first non-local
# IP address (i.e. neither 127.0.0.1 nor localhost) on this machine will be used.
# If no non-local IP is found, localhost will be used.
jppf.management.host = localhost
# JMX management port, used by the remote JMX connector
jppf.node.management.port = 11198

These properties have the same meaning and usage as for a server, as described in the driver JMX configuration section.

Note that, as of JPPF versions 4.1.2 and 4.2, the configuration property name for the management port has changed. If the new name is not specified, JPPF will still lookup the old name “jppf.management.port” to ensure backward-compatibility for existing configuration files.
### Interaction between connection recovery and server discovery
When dicovery is enabled for the node (jppf.dicovery.enabled = true) and the maximum reconnection time is not infinite (reconnect.max.time = <strictly_positive_value>), a sophisticated failover mechanism takes place, following the sequence of steps below:

- the node attempts to reconnect to the driver to which it was previously connected (or attempted to connect), during a maximum time specified by the configuration property "reconnect.max.time"
- during this maximum time, it will make multiple attempts to connect to the same driver. This covers the case when the driver is restarted in the mean time.
- after this maximum time has elapsed, it will attempt to auto-discover another driver, during a maximum time, specified via the configuration property "jppf.discovery.timeout" (in milliseconds)
- if the node still fails to reconnect after this timeout has expired, it will fall back to the driver manually specified in the node's configuration file
- the cycle starts again
### Recovery from hardware failures
The mechanism to recover from hardwaire failure has its counterpart on each node, which works as follows:

- the node establishes a specific connection to the server, dedicated to failure detection
- at connection time, a handshake takes place, where the node communicates a unique id (UUID) to the server
- the node will then attempt to get a message from the server (“check” message).
- if the message from the server is not received in a specified time frame, and this, a specified number of times in a row, the node will consider the connection to the server broken, will close it cleanly, and let the recovery and failover mechanism take over, as described in the previous section.

The following configuration properties are those required by the nodes' hardware failure recovery mechanism implemented by the server:

# Enable recovery from hardware failures on the node. Default is false (disabled).
jppf.recovery.enabled = false
# Dedicated port number for the detection of node failure, must be the same as
# the value specified in the server configuration. Default value is 22222.
jppf.recovery.server.port = 22222
# Maximum number of attempts to get a message from the server before the
# connection is considered broken. Default value is 2.
jppf.recovery.max.retries = 2
# Maximum time in milliseconds allowed for each attempt to get a message
# from the server. Default value is 60000 (1 minute).
jppf.recovery.read.timeout = 60000

Important note: given the implementation of this mechanism, you must be careful to keep some consistency between the server and node settings. As a general rule of thumb, the settings should always respect the following constraint:
serverReaperInterval < nodeMaxRetries * nodeTimeout
This rule applies between any server and node, as well as between any two servers if you enabled communication between servers.

Note: if server discovery is active for a node, then the port number specified for the driver will override the one specified in the node's configuration.
### Processing threads
A node can process multiple tasks concurrently, using a pool of threads. The size of this pool is configured as follows:

# number of threads running tasks in this node
jppf.processing.threads = 4

If this property is not defined, its value defaults to the number of processors or cores available to the JVM.
### Node process configuration
In the same way as for a server (see server process configuration), the node is made of 2 processes. In addition to the properties and environment inherited from the controller process, it is possible to specify other JVM options via the following configuration property:
jppf.jvm.options = -Xms64m -Xmx512m

As for the server, it is possible to specify additional class path elements through this property, by adding one or more “-cp” or “-classpath” options (unlike the Java command which only accepts one). For example:

jppf.jvm.options = -cp "dir with spaces/myJar1.jar" -cp lib/myJar1.jar -Xmx512m
### Class loader cache
Each node creates a specific class loader for each new client whose tasks are executed in that node. The cache itself is managed as a bounded queue, and the oldest class loader will be evicted from the cache whenever the maximum size is reached. The evicted class loader then becomes unreachable and can be garbage collected. In most modern JDKs, this also results in the classes being unloaded.

If the class loader cache size is too large, this can lead to an out of memory condition in the node, especially in these 2 scenarios:

- if too many classes are loaded, the space reserved to the class definitions (permanent generation in Oracle JDK) will fill up and cause an “OutOfMemoryError: PermGen space”
- if the classes hold a large amount of static data (via static fields and static initializers), an “OutOfMemoryError: Heap Space” will be thrown

To mitigate this, the size of the class loader cache can be configured in the node as follows:

jppf.classloader.cache.size = 50

The default value for this property is 50, and the value must be at least equal to 1.
### Class loader resources cache
To avoid uncessary network round trips, the node class loaders can store locally the resources found in their extended classpath when one of their methods getResourceAsStream(), getResource(), getResources() or getMultipleResources() is called. This cache is enabled by default and the type of storage and location of the file-persisted cache can be configured as follows:

# whether the resource cache is enabled, defaults to 'true'
jppf.resource.cache.enabled = true
# type of storage: either 'file' (the default) or 'memory'
jppf.resource.cache.storage = file
# root location of the file-persisted caches
jppf.resource.cache.dir = some_directory

When “file” persistence is configured, the node will fall back to memory persistence if the resource cannot be saved to the file system for any reason. This could happen, for instance, when the file system runs out of space.

For more details, please refer to the “Class Loading In JPPF > Local caching of network resources” section of this documentation.
### Security policy
To limit what the nodes can do on the machine that hosts them, It is possible to specify what permissions are granted to them on their host. These permissions are based on the Java security policy model.

To implement security, nodes require a security policy file. The syntax of this file is similar to that of Java security policy files, except that it only accepts permission entries (no grant or security context entries).

Some examples of permission entries:

// permission to read, write, delete node log file in current directory
permission java.io.FilePermission "${user.dir}/jppf-node.log", "read,write,delete";
// permission to read all log4j system properties
permission java.util.PropertyPermission "log4j.*", "read";
// permission to connect to a MySQL database on the default port on localhost
permission java.net.SocketPermission "localhost:3306", "connect,listen";

To enable the security policy, the node configuration file must contain the following property definition:

# Path to the security file, relative to the current directory or classpath
jppf.policy.file = jppf.policy

When this property is not defined, or the policy file cannot be found, security is disabled.

The policy file does not have to be local to the node. If it is not present locally, the node will download it from the server. In this case it has to be locally accessible by the server, and the path to the policy file will be interpreted as path on the server's file system. This feature, combined with the ablity to remotely restart the nodes, allows to easily update and propagate changes to the security policy for all the nodes.
### Offline mode
A node can be configured to run in “offline” mode. In this mode, there will be no class loader connection to the server (and thus no distributed dynamic class loading will occur), and remote management via JMX is disabled. For more details on this mode, please read the documentation section Deployment and run modes > Offline nodes.

To turn on the offline mode:

# set the offline mode (false by default)
jppf.node.offline = true

### Redirecting the console output
As for JPPF drivers, the output of System.out and System.err of a node can be redirected to files. This can be accomplished with the following properties:

# file on the file system where System.out is redirected
jppf.redirect.out = /some/path/someFile.out.log
# whether to append to an existing file or to create a new one
jppf.redirect.out.append = false

# file on the file system where System.err is redirected
jppf.redirect.err = /some/path/someFile.err.log
# whether to append to an existing file or to create a new one
jppf.redirect.err.append = false

By default, a new file is created each time the node is started, unless “jppf.redirect.out.append = true” or “jppf.redirect.err.append = true” are specified. If a file path is not specified, then the corresponding output is not redirected.
### Specifying the path to the JVM
It is possible to choose which JVM will run a node, by specifying the full path to the Java executable with the following property:

# Full path to the java executable
jppf.java.path = <path_to_java_executable>
# Linux example
jppf.java.path = /opt/jdk1.8.0/bin/java
# Windows example
jppf.java.path = C:/java/jdk1.7.0/bin/java.exe

This property is used in several situations:

- by the shell script from the node distribution that launches the node (startNode.sh or startNode.bat)
- by slave nodes when the property is specified as a configuration override, allowing to start a slave node with a different JVM than its master's
- when a node is restarted with one of the JPPFNodeAdminMBean.updateConfiguration() management methods with jppf.java.path specified as an overriden property.

## Client and administration console configuration
### Server discovery in the client
By default, JPPF clients are configured to automatically discover active servers on the network. This mechanism works in the same way as for the nodes, and uses the same configuration properties, except for the discovery timeout:

# Enable or disable automatic discovery of JPPF drivers
jppf.discovery.enabled = true
# UDP multicast group to which drivers broadcast their connection parameters
jppf.discovery.group = 230.0.0.1
# UDP multicast port to which drivers broadcast their connection parameters
jppf.discovery.port = 11111

# IPv4 address inclusion patterns
jppf.discovery.include.ipv4 =
# IPv4 address exclusion patterns
jppf.discovery.exclude.ipv4 =
# IPv6 address inclusion patterns
jppf.discovery.include.ipv6 =
# IPv6 address exclusion patterns
jppf.discovery.exclude.ipv6 =

A major difference is that, when discovery is enabled, the client does not stop attempting to find one or more servers. A client can also connect to multiple servers, and will effectively connect to every server it discovers on the network.

The JPPF client will manage a pool of connections to each discovered server, which can be used for concurrent job submissions. The size of the connection pools is configured with the following property:

# connection pool size for each discovered server; defaults to 1 (single connection)
jppf.pool.size = 5

Each server connection has an assigned name, following the pattern: “jppf_discovery-<n>-<p>”, where n is a driver number, in order of discovery, and p is the connection number, if the defined connection pool size is greater than 1. For instance, if we defined jppf.pool.size = 2, then the first discovered driver will have 2 connections named “jppf_discovery-1-1” and “jppf_discovery-1-2”

Each connection pool has an associated pool of JMX connections, whose size is independently configured as follows:

# JMX connection pool size, defaults to 1
jppf.jmx.pool.size = 1

The inclusion and exclusion pattern definitions work exactly in the same way as for the node configuration. Please refer to the node's configuration of server discovery for more details.

It is also possible to specify the priority of all discovered server connections, so that they will easily fit into a failover strategy defined via the manual network configuration:

# priority assigned to all auto-discovered connections; defaults to 0
# this is equivalent to "<driver_name>.jppf.priority" in manual network configuration
jppf.discovery.priority = 10

Additionally, you can specify the behavior to adopt, when a driver broadcasts its connection information for multiple network interfaces. In this case, the client may end up creating multiple connections to the same driver, but with different IP addresses. This default behavior can be disabled by setting the following property:

# enable or disable multiple network interfaces for each driver
jppf.pool.acceptMultipleInterfaces = false

This property defaults to false, meaning that only the first discovered interface for a driver will be taken into account.

### Manual network configuration
As we have seen, a JPPF client can connect to multiple drivers. The first step will this be to name these drivers:

# space-separated list of drivers this client may connect to
# defaults to “default-driver”
jppf.drivers = driver-1 driver-2

Then for each driver, we will define the connection and behavior attributes, including:

Connection to the JPPF server

# host name, or ip address, of the host the JPPF driver is running on
driver-1.jppf.server.host = localhost
# port number for the on which the driver accepts connections
driver-1.jppf.server.port = 11111

Here, driver-1.class.server.port and driver-1.app.server.port must have the same value as the corresponding properties class.server.port and app.server.port defined in the server configuration.

Connection pool size

# size of the pool of connections to this driver
driver-1.jppf.pool.size = 5

This allows the creation of a connection pool with a specific size for each server we connect to, whereas all pools would have the same size when server discovery is enabled.

As for automatic server discovery, each connection pool has an associated pool of JMX connections, whose size is independently configured as follows:

# JMX connection pool size, defaults to 1
driver-1.jppf.jmx.pool.size = 1

Priority

# assigned driver priority
driver-1.jppf.priority = 10

The priority assigned to a server connection enables the defintion of a fallback strategy for the client. In effect, the client will always use connections that have the highest priority. If the connection with the server is interrupted, then the client we use connections with the next highest priority in the remaining accessible server connection pools.

Connection to the management server

# management port for this driver
driver-1.jppf.management.port = 11198

This will allow direct access to the driver's JMX server using the client APIs, unless the client configuration property jppf.management.enabled is set to false.

Note that this property is optional, since the JPPF client fetches it from the JPPF driver during the communication handshake. It is thus recommended to leave it unspecified.
### Using manual configuration and server discovery together
It is possible to use the manual server configuration simultaneously with the server discovery, by adding a special driver name, “jppf_discovery” to the list of manually configured drivers:

# enable discovery
jppf.discovery.enabled = true
# specifiy both discovery and manually configured drivers
jppf.drivers = jppf_discovery driver-1
# host for this driver
driver-1.jppf.server.host = my_host
# port for this driver
driver-1.jppf.server.port = 11111
### Load-balancing and failover of server connection pools
Connection pools can be organized in any combination of two modes, using the priority attribute of each pool:

Load-balancing mode occurs when the connection pools have the same priority. In this case, the JPPF client will balance the jobs between the connections of the pools, according to the load-balancer settings. Example configuration:

jppf.drivers = driver-1 driver-2

driver-1.jppf.server.host = my.host1.com
driver-1.jppf.server.port = 11111
driver-1.jppf.priority = 20

driver-2.jppf.server.host = my.host2.com
driver-2.jppf.server.port = 11111
driver-2.jppf.priority = 20

Failover mode occurs when connection pools have different priorities. In this case, the JPPF client will only send jobs through the pool(s) with the highest priority. If the highest priority pool fails for any reason, the JPPF client will then fall back to the highest priority among the remaining connection pools, and so on. The following example shows such a configuration:

jppf.drivers = primary-pool secondary-pool

primary-pool.jppf.server.host = my.host1.com
primary-pool.jppf.server.port = 11111
primary-pool.jppf.priority = 20

secondary-pool.jppf.server.host = my.host2.com
secondary-pool.jppf.server.port = 11111
secondary-pool.jppf.priority = 10

You can also combine load-balancing and failover modes, since there is no limit to the number of connection pools you can define. For example:

jppf.drivers = primary-pool-1 primary-pool-2 secondary-pool-1 secondary-pool-2

primary-pool-1.jppf.server.host = my.host1.com
primary-pool-1.jppf.server.port = 11111
primary-pool-1.jppf.priority = 20

primary-pool-2.jppf.server.host = my.host2.com
primary-pool-2.jppf.server.port = 11111
primary-pool-2.jppf.priority = 20

secondary-pool-1.jppf.server.host = my.host3.com
secondary-pool-1.jppf.server.port = 11111
secondary-pool-1.jppf.priority = 10

secondary-pool-2.jppf.server.host = my.host4.com
secondary-pool-2.jppf.server.port = 11111
secondary-pool-2.jppf.priority = 10
### Socket connections idle timeout
In some environments, a firewall may be configured to automatically close socket connections that have been idle for more than a specified time. This may lead to a situation where a server may be unaware that a client was disconnected, and cause one or more jobs to never return. To remedy to that situation, it is possible to configure an idle timeout on the client side of the connection, so that the connection can be closed cleanly and grid operations can continue unhindered. This is done via the following property:

jppf.socket.max-idle = timeout_in_seconds

If the timeout value is less than 10 seconds, then it is considered as no timeout. The default value is -1.

### Local and remote execution
It is possible for a client to execute jobs locally (i.e. in the client JVM) rather than by submitting them to a server. This feature allows taking advantage of muliple CPUs or cores on the client machine, while using the exact same APIs as for a distributed remote execution. It can also be used for local testing and debugging before going “live”.

Local execution is disabled by default. To enable it, set the following configuration property:

# enable local job execution; defaults to false
jppf.local.execution.enabled = true

Local execution uses a pool of threads, whose size is configured as follows:

# number of threads to use for local execution
# the default value is the number of CPUs or cores available to the JVM
jppf.local.execution.threads = 4

A priority can be assigned to the local executor, so that it will easily fit into a failover strategy defined via the manual network configuration:

# priority assigned to the local executor; defaults to 0
# this is equivalent to "<driver_name>.jppf.priority" in manual network configuration
jppf.local.execution.priority = 10

It is also possible to mix local and remote execution. This will happen whenever the client is connected to a server and has local execution enabled. In this case, the JPPF client uses an adaptive load-balancing alogrithm to balance the workload between local execution and node-side execution.

Finally, the JPPF client also provides the ability to disable remote execution. This can be useful if you want to test the execution of jobs purely locally, even if the server discovery is enabled or the server connection properties would otherwise point to a live JPPF server. To achieve this, simply configure the following:

# enable remote job execution; defaults to true
jppf.remote.execution.enabled = false

Important note: when remote execution is disabled with jppf.remote.execution.enabled = false, neither automatic server discovery nor manual network configuration settings will have any effect anymore. In effect, this property allows to completely disable the built-in server discovery mechanisms (auto discovery and manual configuration), while still allowing optional custom discovery mechanisms to work.
### Load-balancing in the client
The JPPF client allows load balancing between local and remote execution. The load balancing configuration is exactly the same as for the driver, which means it uses exactly the same configuration properties, algorithms, parameters, etc...
Please refer to the driver load-balancing configuration section for the configuration details. The default configuration, if none is provided, is equivalent to the following:

# name of the load balancing algorithm
jppf.load.balancing.algorithm = manual
# name of the set of parameter values (aka profile) to use for the algorithm
jppf.load.balancing.profile = jppf
# "jppf" profile
jppf.load.balancing.profile.jppf.size = 1000000

Also note that the load balancing is active even if only remote execution is available. This has an impact on how tasks within a job will be sent tot he server. For instance, if the “manual” algorithm is configured, with a size of 1, this means the tasks in a job will be sent one at a time.
### Resolution of the drivers IP addresses
You can switch on or off the DNS name resolution for the drivers a client connects, with the following property:

# whether to resolve the drivers' ip addresses into host names
# defaults to true (resolve the addresses)
org.jppf.resolve.addresses = true
### UI refresh intervals in the administration tool
You may change the values of these properties if the graphical administration and monitoring tool is having trouble displaying all the information received from the nodes and servers. This may happen when the number of nodes and servers becomes large and the UI cannot cope. Increasing the refresh intervals (or decreasing the frequency of the updates) in the UI resolves such situations. The available configuration properties are defined as follows:

# refresh interval for the statistcs panel in millis; defaults to 1000
# this is the interval between 2 succesive stats requests to a driver via JMX
jppf.admin.refresh.interval.stats = 1000

# refresh interval in millis for the topology panels: tree view and graph view
# this is the interval between 2 successive runs of the task that refreshes the
# topology via JMX requests; defaults to 1000
jppf.admin.refresh.interval.topology = 1000

# refresh interval for the JVM health panel in millis; defaults to 1000
# this is the interval between 2 successive runs of the task that refreshes
# the JVM health via JMX requests
jppf.admin.refresh.interval.health = 1000

# UI refresh interval for the job data panel in ms. Its meaning depends on the
# publish mode specified with property "jppf.gui.publish.mode" (see below):
# - in "immediate_notifications" mode, this is not used
# - in "deferred_notifications" mode, this is the interval between 2 publications
# of updates as job monitoring events
# - in "polling" mode this is the interval between 2 polls of each driver
jppf.gui.publish.period = 1000

# UI refresh mode for the job data panel. The possible values are:
# - polling: the job data is polled at regular intervals and updates to the view are
# computed as the differences with the previous poll. This mode generates less network
# traffic than the other modes, but some updates, possibly entire jobs, may be missed
# - deferred_notifications: updates are received as jmx notifications and published at
# regular intervals, possibly aggregated in the interval. This mode provides a more
# accurate view of the jobs life cycle, at the cost of increased network traffic
# - immediate_notifications: updates are received as jmx notifications and are all
# published immediately as job monitoring events, which are pushed to the UI. In this
# mode, no event is missed, however this causes higher cpu and memory consumption
# The default value is immediate_notifications
jppf.gui.publish.mode = immediate_notifications
### Customizing the administration console's splash screen
At startup, the administration console displays a splash screen made of a sequence of rolling images with a fixed text at the center. The splash screen can now be customized with the following properties:

# Whether to display the animated splash screen at console startup, defaults to false
jppf.ui.splash = true
# The fixed text displayed at center of the window
jppf.ui.splash.message = The JPPF Admin Console is starting ...
# The message's font color, expressed as an rgb or rgba value. If alpha is not
# specified, it is assumed to be 255 (fully opaque).
# Examples: 255, 233, 127 (opaque) | 255, 233, 127, 128 (semi-transparent)
jppf.ui.splash.message.color = 64, 64, 128
# One or more paths to the images displayed in a rolling sequence (like a slide show)
# The images may be either in the file system or in the classpath and are separated with # '|' (pipe) characters
jppf.ui.splash.images = image_path_1 | ... | image_path_N
# interval between images in milliseconds
jppf.ui.splash.delay = 500

## Common configuration properties
### Lookup of classpath resources in the file system
By default, the JPPF distributed class loader looks for requested resources in the file system (using the resource name as file path), if they are not found in the class path. This behavior can be disabled by setting the following property in a node, server or client:

# Enable or disable the lookup of classpath resources in the file system
jppf.classloader.file.lookup = true

Since this property applies to the lookup of remote resources, the file system lookup will occur if and only if this property is true in the node configuration and in the server or client configuration. Also note that its value is true by default.
### Socket connections recovery and failover
When the connection to a server is interrupted, the node, client or peer servr will automatically attempt, for a given length of time, and at regular intervals, to reconnect to the same server. These properties are configured as follows, with their default values:

# number of seconds before the first reconnection attempt
jppf.reconnect.initial.delay = 0
# time after which the system stops trying to reconnect, in seconds
# a value of zero or less means it never stops
jppf.reconnect.max.time = 60
# time between two connection attempts, in seconds
jppf.reconnect.interval = 1

With these values, we have configured the recovery mechanism such that it will attempt to reconnect to the server after a 0 second delay, for 60 seconds and with connection attemps at 1 second intervals.
### JMX requests timeout
In some very rare cases, a JMX request may be stuck because an error occurrred in the remote driver or node, without breaking the JMX connection. A typical example is when an OutOfMemoryError occurs while the remote peer is executing the request. To avoid this, it is possible to set JMX request timeout withi this configuration property:

# Timeout in millis for JMX requests. Defaults to Long.MAX_VALUE (2^63 - 1)
jppf.jmx.request.timeout = $script{ java.lang.Long.MAX_VALUE }$
### Global performance tuning parameters
These configuration properties affect the performance and throughput of I/O operations in JPPF. The values provided in the vanilla JPPF distribution (listed below) are known to offer a good performance in most situations and environments. These properties are defined as follows:

# Size of send and receive buffer for socket connections
# Defaults to 32768 and must be in range [1024, 1024*1024]
jppf.socket.buffer.size = 65536

# Size of temporary buffers (including direct buffers) used in I/O transfers
# Defaults to 32768 and must be in range [1024, 1024*1024]
jppf.temp.buffer.size = 12288

# Maximum size of temporary buffers pool (excluding direct buffers).# When this size
# is reached, new buffers are still created, but not released into the pool, so they
# can be quickly garbage-collected.
# The size of each buffer is defined with ${jppf.temp.buffer.size}
# Defaults to 10 and must be in range [1, 2048]
jppf.temp.buffer.pool.size = 200

# Size of temporary buffer pool for reading lengths as ints (size of each buffer is 4)
# Defaults to 100 and must be in range [1, 2048]
jppf.length.buffer.pool.size = 100

## Putting it all together

After seeing all the configuration details for the JPPF components, we would like to take a step back and have a look at the big picture of what the configuration is about: defining a JPPF grid topology the way we want it. For this purpose, we will define a specific non-trivial topology, and make two diagrams of this topology, where the JPPF components in each diagram are annotated with the minimal set of configuration properties that must be defined. One diagram presents the configuration when the connections between components are defined manually, the other diagram when they are automatically discovered.
### Defining a topology
Here is the JPPF topology we want to achieve:

Let's state plainly the components involved and their relationships:
- there are one client, two servers (server1 and server2) and two nodes (node1 and node2)
- the client is connected to both servers
- each server is connected to the other server
- node1 is connected to server1
- node2 is connected to server2

In the following diagrams a property definition between parentheses means that the definition uses a default value, and thus doesn't need to be defined. This notation is used to emphasize what default values actually mean. For convenience, we will also assume that server1 is on a machine with IP address 10.1.10.1 and server2 on a machine with the IP address 10.1.10.2. They also listen on ports 11111 and 11112, respectively.
### Automatic discovery of the topology

As we can see, automatic discovery involves very few configuration properties. The discovery itself is active by default (jppf.discovery.enabled = true). The client actually does not need any property at all and will work with an empty configuration. The drivers only need to override properties that define non-default values. Lastly, the nodes specify an inclusive pattern for which server to connect to, otherwise they could pickup the wrong server, connect both to the same server, etc.

Also note that, if our topology only included server1, then no configuration property at all would be needed in the client, server1, node1 or node2. That is the power of automatic discovery in JPPF master/worker topologies.
### Manual configuration of the topology

## Configuring SSL/TLS communications

A JPPF grid has the ability to use secure connections between its components. This is done by using the SSL/TLS protocols over network connections, and provides security services such as peer authentication, data encryption and data integrity. This documentation aims at describing how to configure secure connections between JPPF servers, nodes and clients. If you wish to learn details of the SSL/TLS protocols in Java, our recommendation is to read about this in the Java Secure Socket Extension (JSSE) Reference Guide.

Additionally, all downloadable JPPF components now come with a predefined set of SSL configuration files, which can be used as-is for testing purposes. These files notably include a truststore and a keystore containing self-signed certificates and private keys. For real-world secure connectivity in JPPF, you will have to provide your own key- and trust- stores, with the proper certificate chains, validated by trusted certificate authorities.
### Enabling secure connectivity
#### In the clients
There is a global property which applies to all drivers found via the auto-discovery mechanism:

# Enable SSL for auto-dsicovered drivers. Default value is false (disabled).
# If enabled, only SSL/TLS connections are established.
jppf.ssl.enabled = true

For drivers specified manually in the client configuration, SSL connectivity is specified individually:

# disable discovery
jppf.discovery.enabled = false
# mnaually specifiy two drivers
jppf.drivers = driver1 driver2

# define secure connectivity to driver1
driver1.jppf.server.host = secure_host
driver1.jppf.server.port = 11443
# secure connections are made to this driver
driver1.jppf.ssl.enabled = true

# define non-secure connectivity to driver2
driver2.jppf.server.host = non_secure_host
driver2.jppf.server.port = 11111
# the default value is false and needs not be specified
#driver2.jppf.ssl.enabled = false
#### In the nodes
Nodes use either secure connections, or non-secure connections, but not both at the same time. Thus, this is determined from a single configuration property in their respective configuration file:

# Enable SSL. Default value is false (disabled).
# If enabled, only SSL/TLS connections are established
jppf.ssl.enabled = true

For a node, this also means that its embedded JMX server will only accept secure connections. This has an impact on the driver configuration: since the driver connects to the node's JMX server, it will be considered a SSL client from the JMX perspective. This means the driver will need to have the proper node certificate in its trust store.
#### In the servers
A JPPF server has the ability to accept both secure and non-secure connections, i.e. this is not a single on/off switch as for nodes and clients. Additionally, there are 3 areas of a JPPF server that can be configured separately: “standard” connections from nodes and clients (grid jobs handling and distributed class loader), connections to other servers and embedded JMX server. These are configured via the following properties in the server's configuration file:

# Port number to which the server listens for secure connections, defaults to 11443
# A negative value indicates that no secure connection is accepted
jppf.ssl.server.port = 11443

# toggle to enable secure connections to remote peer servers, defaults to false
jppf.peer.ssl.enabled = true

# Enabling JMX features via secure connections, defaults to false
jppf.management.ssl.enabled = true

Please note that jppf.ssl.server.port (secure port) comes in addition to jppf.server.port (non secure) and that both can be used together. For instance, if you wish to only accept secure connections, you will have to disable the non-secure connection by specifying a negative port number:

# disable non-secure connections
jppf.server.port = -1
# enable secure connections
jppf.ssl.server.port = 11443

As for the non-secure port, assigning a value of 0 will cause JPPF to dynamically allocate a valid port number.

In a similar way you can use either JMX secure or non-secure connections, or both:

# Enabling JMX via non-secure connections, defaults to true
jppf.management.enabled = false
# Enabling JMX via secure connections, defaults to false
jppf.management.ssl.enabled = true
# Secure JMX server port
jppf.management.ssl.port = 11193
### Locating the SSL configuration
The SSL configuration is loaded separately from the JPPF configuration itself. The effect of this is that it is harder to find for a remote application, and it will not appear in the JPPF monitoring tools and APIs, the goal being to avoid providing information about how JPPF is secured, which would defeat the purpose of securing it in the first place.
#### Configuration as a file or classpath resource
To specify the location of the SSL configuration as a file, you can use the jppf.ssl.configuration.file property in the JPPF configuration file of the driver, node or client:

# location of the SSL configuration in the file system or classpath
jppf.ssl.configuration.file = config/ssl/ssl.properties

The lookup for the specified file or resource is performed first in the file system, then in the classpath. This allows you for instance to embed a configuration file in a jar file, with the possibility to override it with another file.

Relative paths are relative to the current working directory as specified by System.getProperty("user.dir").
#### Configuration as an external source
JPPF provides a more sophisticated way to locate its SSL configuration, which requires the implementation of a specific plugin. This is useful in situations where a configuration file is not considered secure enough, or if you need to load the configuration from a centralized location, for instance if you run JPPF in a cloud environment and want to fetch the configuration via a cloud storage facility such as Amazon's S3.

This is done via the jppf.ssl.configuration.source property:

# SSL configuration as an arbitrary source. Value is the fully qualified name
# of an implementation of java.util.concurrent.Callable<InputStream> with optional
# space-separated arguments
jppf.ssl.configuration.source = implementation_of_Callable<InputStream> arg1 ... argN

where implementation_of_Callable<InputStream> is the fully qualified name of a class which implements the interface Callable<InputStream> and which must have either a noarg constructor, or a (String...args) vararg constructor.

For example, the predefined JPPF plugin FileStoreSource is implemented as follows:

package org.jppf.ssl;

import java.io.InputStream;
import java.util.concurrent.Callable;
import org.jppf.utils.FileUtils;

// A secure store source that uses a file as source
public class FileStoreSource implements Callable<InputStream> {

  // Optional arguments that may be specified in the configuration
  private final String[] args;

  public FileStoreSource(final String... args) throws Exception {
    this.args = args;
    if ((args == null) || (args.length == 0))
      throw new SSLConfigurationException("missing parameter: file path");
  }

  @Override
  public InputStream call() throws Exception {
    // lookup in the file system, then in the classpath
    InputStream is = FileUtils.getFileInputStream(args[0]);
    if (is == null)
      throw new SSLConfigurationException("could not find file " + args[0]);
    return is;
  }
}

We can then use it in the configuration:

jppf.ssl.configuration.source = org.jppf.ssl.FileStoreSource config/ssl/ssl.properties

which is in fact equivalent to:

jppf.ssl.configuration.file = config/ssl/ssl.properties
### SSL configuration properties
These properties are defined in the SSL configuration file and represent the information required to create and initialize SSLContext, SSLSocket and SSLEngine objects.
#### SSLContext protocol
This is the protocol name used in SSLContext.getInstance(String protocol). It is defined as:

# SSLContext protocol, defaults to SSL
jppf.ssl.context.protocol = SSL

A list of valid protocol names is available here.
#### Enabled protocols
This is the list of supported protocol versions, such as returned by SSLEngine.getEnabledProtocols(). It is defined as a list of space-separated names:

# list of space-separated enabled protocols
jppf.ssl.protocols = SSLv2Hello SSLv3

A list of valid protocol versions is available here.
#### Enabled cipher suites
This is the list of supported protocol versions, such as returned by SSLEngine.getEnabledCipherSuites(). It is defined as a list of space-separated names:

# enabled cipher suites as a list of space-separated values
jppf.ssl.cipher.suites = SSL_RSA_WITH_RC4_128_MD5 SSL_RSA_WITH_RC4_128_SHA

A list of supported cipher suites is available here.
#### Client authentication
The client authentication mode is determined by calling the methods SSLEngine.getWantClientAuth() and SSLEngine.getNeedClientAuth(). It is defined as:

# client authentication mode
# possible values: none | want | need
jppf.ssl.client.auth = none
#### Key store and associated password
As for the location of the SSL configuration, there are two ways to specify the location of a keystore:

# path to the key store on the file system
jppf.ssl.keystore.file = config/ssl/keystore.ks
# an implementation of Callable<InputStream> with optional space-separated arguments
jppf.ssl.keytstore.source = org.jppf.ssl.FileStoreSource config/ssl/keystore.ks

Note that, if both properties are defined, JPPF will first attempt to load the key store from the defined source, then from the specified file path.

In a similar fashion, there are two ways to specify the key store's password: either as a clear text password, or as a password source. This can be done as follows:

# keystore password in clear text
jppf.ssl.keystore.password = password
# keystore password from an arbitrary source
# the source is an implementation of Callable<char[]> with optional parameters
jppf.ssl.keystore.password.source = org.jppf.ssl.PlainTextPassword password

Lastly, the format of the key store is specified with the following property:

# The key store format to use. When unspecified, it defaults to the value of
# KeyStore.getDefaultType(). For instance on the Oracle JVM it will be 'JKS',
# on Android's Dalvik it will be BKS, etc.
jppf.ssl.keystore.type = JKS

Note that, depending on the environment on which a node is executing, you may need to use different formats for the node's key store (if using mutual authentication) and for the driver's key store. For instance, if the node is running on Android, the "JKS" format, which is the default on the Oracle JVM, will not be supported and the key store will need to be converted to e.g. BKS (BouncyCastle KeyStore), which is the default on Android.
#### Trust store and associated password
The trust store and its password are defined in the same way as for the key store:

# path to the trust store on the file system
jppf.ssl.truststore.file = config/ssl/truststore.ks
# an implementation of Callable<InputStream> with optional space-separated arguments
jppf.ssl.truststore.source = org.jppf.ssl.FileStoreSource config/ssl/truststore.ks

# keystore password in clear text
jppf.ssl.truststore.password = password
# keystore password from an arbitrary source
# the source is an implementation of Callable<char[]> with opptional parameters
jppf.ssl.truststore.password.source = org.jppf.ssl.PlainTextPassword password

As for the key store, the format of the trust store is specified with the following property:

# the format to use for the trust store. When unspecified, it defaults to the
# value of KeyStore.getDefaultType(). For instance on the Oracle JVM it will be
# 'JKS', on Android's Dalvik it will be BKS, etc.
jppf.ssl.truststore.type = JKS

#### Special case: distinct driver trust stores for nodes and clients
In the case when the JPPF driver has mutual authentication enabled (jppf.ssl.client.auth = need”), it might be desirable to use distinct trust stores for the certificates of the nodes and the clients that will connect to the driver. This can be done as follows:

# specify that a separate trust store must be used for client certificates
jppf.ssl.client.distinct.truststore = true

# path to the client trust store on the file system
jppf.ssl.client.truststore.file = config/ssl/truststore_cli.ks
# an implementation of Callable<InputStream> with optional space-separated arguments
jppf.ssl.client.truststore.source = o.j.s.FileStoreSource config/ssl/truststore_cli.ks

# keystore password in clear text
jppf.ssl.client.truststore.password = password
# keystore password from an arbitrary source
# the source is an implementation of Callable<char[]> with opptional parameters
jppf.ssl.client.truststore.password.source = org.jppf.ssl.PlainTextPassword password

# the format to use for the client trust store. When unspecified, it defaults to
# the value of KeyStore.getDefaultType(). For instance on the Oracle JVM it will
# be 'JKS', on Android's Dalvik it will be BKS, etc.
jppf.ssl.client.truststore.type = JKS

In this configuration, a client will not be able to authenticate with the server if it uses a copy of the node's keystore, even if it uses the correct password.
### Full SSL configuration example
# SSLContext protocol, defaults to SSL
jppf.ssl.context.protocol = SSL
# list of space-separated enabled protocols
jppf.ssl.protocols = SSLv2Hello SSLv3
# enabled cipher suites as a list of space-separated values
jppf.ssl.cipher.suites = SSL_RSA_WITH_RC4_128_MD5 SSL_RSA_WITH_RC4_128_SHA
# client authentication mode; possible values: none | want | need
jppf.ssl.client.auth = none

# key store format
jppf.ssl.keystore.type = JKS
# path to the key store on the file system.
jppf.ssl.keystore.file = config/ssl/keystore.ks
# keystore password in clear text
jppf.ssl.keystore.password = password

# trust store format
jppf.ssl.truststore.type = JKS
# the trust store location as an arbitrary source:
# an implementation of Callable<InputStream> with optional space-separated arguments
jppf.ssl.truststore.source = org.jppf.ssl.FileStoreSource config/ssl/truststore.ks
# truststore password as an arbitrary source:
# an implementation of Callable<char[]> with optional space-separated arguments
jppf.ssl.truststore.password.source = org.jppf.ssl.PlainTextPassword password

## The JPPF configuration API
### General properties handling
The JPPF configuration properties are accessible at runtime, via a static method call:
JPPFConfiguration.getProperties(). This method returns an object of type TypedProperties, which is an extension of java.util.Properties with additional methods to handle properties with primitive values: boolean, int, long, float, double, char and boolean, and also String and File.

Here is a summary of the API provided by TypedProperties:

public class TypedProperties extends Properties {
  // constructors
  public TypedProperties()
  // initialize with existing key/value pairs from a map
  public TypedProperties(Map<Object, Object> map)
  // string properties
  public String getString(String key)
  public String getString(String key, String defValue)
  public TypedProperties setString(String key, String value)
  // int properties
  public int getInt(String key)
  public int getInt(String key, int defValue)
  public TypedProperties setInt(String key, int value)
  // long properties
  public long getLong(String key)
  public long getLong(String key, long defValue)
  public TypedProperties setLong(String key, long value)
  // float properties
  public float getFloat(String key)
  public float getFloat(String key, float defValue)
  public TypedProperties setFloat(String key, float value)
  // double properties
  public double getDouble(String key)
  public double getDouble(String key, double defValue)
  public TypedProperties setDouble(String key, double value)
  // char properties
  public char getChar(String key)
  public char getChar(String key, char defValue)
  public TypedProperties setChar(String key, char value)
  // boolean properties
  public boolean getBoolean(String key)
  public boolean getBoolean(String key, boolean defValue)
  public TypedProperties setBoolean(String key, boolean value)
  // File properties
  public File getFile(String key)
  public File getFile(String key, File defValue)
  public TypedProperties setFile(String key, File value)
}

As you can see, each getXXX() method has a corresponding method that takes a default value, to be returned if the property is not defined for the specified key. Most of them also have a corresponding fluent setter method, which allows setting multiple properties of diffferent types in a call chain.

It is possible to alter the JPPF configuration, via calls to the setXXX(String, XXX) methods of TypedProperties. If you wish to programmatically change one or more JPPF configuration properties, then it should be done before they are used. For instance, in a client application, it should be done before the JPPF client is initialized, as in this sample code:

// get the configuration and set the connection properties programmatically
JPPFConfiguration.getProperties().setBoolean("jppf.discovery.enabled", false)
  .setString("jppf.drivers", "driver1")
  .setString("driver1.jppf.server.host", "www.myhost.com")
  .setInt("driver1.jppf.server.port", 11111);
// now our configuration will be used
JPPFClient client = new JPPFClient();

### Predefined JPPF properties
The JPPF properties documented in the Configuration properties reference chapter are also avaialable as instances of the JPPFProperty interface, which is defined as follows:

public interface JPPFProperty<T> extends Serializable {
  // Get the name of this property
  String getName();

  // Get the default value of this property
  T getDefaultValue();

  // Get the aliases for this property, that is, other names it may be known as,
  // such as legacy names from prior versions
  String[] getAliases();

  // Convert the specified value into the type of values handled by this property
  T valueOf(String value);

  // Convert the specified value to a string
  String toString(T value);

  // Return the class object for the type of values of this property
  Class<T> valueType();

  // Return a concise localized description of the property
  String getDocumentation();
}

The class JPPFProperties holds a static enumeration of the predefined properties, each with a specific type parameter. For instance, the property whose name is "jppf.server.port" holds an int value and is obtained like this:

JPPFProperty<Integer> prop = JPPFProperties.SERVER_PORT;
System.out.printf("name: %s, default: %s, type: %s%n",
  prop.getName(), prop.getDefaultValue(), prop.valueType().getName());

As much as possible, the names of the constants in JPPFProperties are kept similar to the actual properties names: the constant names are all in upper case characters, the "jppf" prefix is removed, and the dots are replaced with underscores. For example "jppf.local.execution.enabled" will correspond to the LOCAL_EXECUTION_ENABLED constant.

The class TypedProperties has specific methods that use predefined properties:

public class TypedProperties extends Properties {
  // Get the value of a predefined property
  public <T> T get(JPPFProperty<T> property);

  // Set the value of a predefined property
  public <T> TypedProperties set(JPPFProperty<T> property, T value);

  // Remove the specified predefined property
  public <T> T remove(JPPFProperty<T> property);
}

Example usage:

int nbThreads = JPPFConfiguration.getProperties().get(JPPFProperties.PROCESSING_THREADS);
JPPFConfiguration.getProperties().set(JPPFProperties.DISCOVERY_ENABLED, true)
  .set(JPPFProperties.POOL_SIZE, 5).setString("custom.property", "some value");

Note the automatic type inference that is automatically performed by the compiler, as well as the preservation of the fluent interface for setting properties, allowing both custom and predefined properties to be set in the same statement.

JPPFConfiguration also has shortcut methods that make use of predefined properties:

public class JPPFConfiguration {
  // Get the value of a predefined property
  public static <T> T get(JPPFProperty<T> property);

  // Set the value of a predefined property
  public static <T> TypedProperties set(JPPFProperty<T> property, T value);

  // Remove the specified predefined property
  public static <T> T remove(JPPFProperty<T> property);
}

These methods resolve into equivalent calls to JPPFConfiguration.getProperties.get/set/remove(...).

For example, these two statements do exactly the same thing

JPPFConfiguration.getProperties().set(JPPFProperties.SERVER_PORT, 11111);
JPPFConfiguration.set(JPPFProperties.SERVER_PORT, 11111);

Similarly for getting values:

int port;
port = JPPFConfiguration.getProperties().get(JPPFProperties.SERVER_PORT);
port = JPPFConfiguration.get(JPPFProperties.SERVER_PORT);

Combined with an import static statement, this leads to significantly smaller and more readable code:

import static org.jppf.utils.configuration.JPPFProperties.*;

...

int nbThreads = JPPFConfiguration.get(PROCESSING_THREADS);
JPPFConfiguration.set(DISCOVERY_ENABLED, true).set(POOL_SIZE, 5)
  .setString("custom.property", "some value").set(SERVER_PORT, 11111);