# JPPF Performance Tuning

jppf.low.memory.threshold	32	long	Minimum heap size in MB below which disk overflow is systematically triggered, to avoid heap fragmentation and ensure there's enough memory to deserialize job headers
jppf.disk.overflow.threshold	2.0	double	Ratio of available heap over the size of an object to deserialize, below which disk overflow is triggered
jppf.gc.on.disk.overflow	true	boolean	Whether to call System.gc() and recompute the avalaible heap size before triggering disk overflow

jppf.socket.buffer.size	32768	int	Receive/send buffer size for socket connections
jppf.socket.keepalive	false	boolean	Enable/disable socket keepalive
jppf.socket.tcp_nodelay	true	boolean	Enable/disable Nagle's algorithm
jppf.temp.buffer.pool.size	10	int	Maximum size of temporary buffers pool
jppf.temp.buffer.size	32768	int	Size of temporary buffers used in I/O transfers