# Configuration guide
A JPPF grid is composed of many distributed components interacting with each other, often in different environments. While JPPF will work in most environments, the default behavior may not be appropriate or adapted to some situations. Much of the behavior in JPPF components can thus be modified, fine-tuned or sometimes even disabled, via numerous configuration properties. These properties apply to many mechanisms and behaviors in JPPF, including:

- network communication
- management and monitoring
- performance / load-balancing
- failover and recovery

Any configuration property has a default value that is used when the property is not specified, and which should work in most environments. In practice, this means that JPPF can work without any explicitely specified configuration at all.

For a full list of the JPPF configuration properties, do not hesitate to read the chapter Appendix A: configuration properties reference of this manual.
## Configuration file specification and lookup
All JPPF components work with a set of configuration properties. The format of these propertiesis as specified in the Java Properties class. To enable a JPPF component to retrieve thiese properties file, their source must be specified using one of the two, mutually exclusive, system properties:

- jppf.config.plugin = class_name, where class_name is the fully qualified name of a class implementing either the interface JPPFConfiguration.ConfigurationSource, or the interface JPPFConfiguration.ConfigurationSourceReader, enabling a configuration source from any origin, such as a URL, a distributed file system, a remote storage facility, a database, etc.
- jppf.config = path, where path is the location of the configuration file, either on the file system, or relative to the JVM's classpath root. If this system property is not specified, JPPF will look for a default file named "jppf.properties" in the current directory or in the classpath root.

Example use:

java -Djppf.config.plugin=my.own.Configuration ...

or

java -Djppf.config=my/folder/myFile.properties ...

The configuration file lookup mechanism is as follows:

1. if jppf.plugin.config is specified
  a) instantiate an object of the specified class name and read the properties via the stream provided by this object's getPropertyStream() or getPropertyReader() method, depending on which interface it implements.
  b) if, for any reason, the stream cannot be obtained or reading the properties from it fails, go to 3.
2. else if jppf.config is specified
  1. look for the file in the file system
  2. if not found in the file system, look in the classpath
  3. if not found in the classpath use default configuration values
3. if jppf.config is not specified
  1. use default file "jppf.properties"
  2. look for "jppf.properties" in the file system
  3. if not found in the file system, look for it in the classpath
  4. if not found in the classpath use default configuration values

A practical side effect of this mechanism is that it allows us to place a configuration file in the classpath, for instance packaged in a jar file, and override it if needed with an external file, since the the file system is always looked up first.

## Includes, substitutions and scripted values in the configuration
### Includes
A JPPF configuration source, whether as a file or as a plugin, can include other configuration sources by adding one or more “#!include” statements in the following format:

#!include source_type source_path

The possible values for source_type are “file”, “url” or “class”. For each of these values, source_path has a different meaning:

- when source_type is “file”, source_path is the path to a file on the file_system or in the JVM's classpath. If the file exists in both classpath and file system, the file system will have priority over the classpath. Relative paths are interpeted as relative to the JVM's current user directory, as determined by System.getProperty(“user.dir”).

- when source_type is “url”, source_path is a URL pointing to a configuration file. It must be a URL such that the JVM can open a stream from it.

- when source_type is “class”, source_path is the fully qualified class name of a configuration plugin, i.e. an implementation of either JPPFConfiguration.ConfigurationSource or JPPFConfiguration.ConfigurationSourceReader.

Examples:

# a config file in the file system
#!include file /home/me/jppf/jppf.properties

# a config file in the classpath
#!include file META-INF/jppf.properties

# a config file obtained from a url
#!include url http://www.myhost.com/jppf/jppf.properties

# a config file obtained from a configuration plugin
#!include class myPackage.MyConfigurationSourceReader

Includes can be nested without any limit on the nesting level. Thus, you need to be careful not to introduce cycles in your includes. If that happens, JPPF will catch the resulting StackOverflowException and display an error message in the console output and in the log.
### Substitutions in the values of configuration properties
The JPPF configuration can handle a syntax of the form “propertyName = prefix${otherPropertyName}suffix”, where prefix and suffix are arbitrary strings and ${otherPropertyName} is a placeholder referencing another property, whose value will be substituted to the placeholder. If you have experience with Apache Ant, this syntax is very similar to the way Ant properties are used in a build script.

Let's take an example illustrating how this works. The following property definitions:

prop.1 = value1
prop.2 = ${prop.1}
prop.3 = value3 ${prop.2}
prop.4 = value4 ${prop.2} + ${prop.3}

will be resolved into:

prop.1 = value1
prop.2 = value1
prop.3 = value3 value1
prop.4 = value4 value1 + value3 value1

Note 1: the order in which the properties are defined has no impact on the resolution of substitutions.
Note 2: substitutions are resolved after all includes are fully resolved and loaded.

#### Unresolved substitutions
A referenced property is unresolvable if, and only if, it refers to a property that is not defined or it is involved in a resolution cycle. In this case, the value of the unresolved value will be the literal syntax in its initial definition, that is in the literal form “${otherPropertyName}”. Let's illustrate this with examples.

In the following configuration:

prop.1 = ${prop.2}

the value of “prop.1” will remain “${prop.2}”, since the property “prop.2” is not defined.

In this configuration:

prop.1 = ${prop.2}
prop.2 = ${prop.3} ${prop.1}
prop.3 = value3

“prop.1” and “prop.2” introduce an unresolvable cycle, and only the reference to “prop.3” can be fully resolved. According to this, the final values will be:

prop.1 = ${prop.2}
prop.2 = value3 ${prop.1}
prop.3 = value3
#### Environment variable substitutions
Any reference to a property name in the form “env.variableName” will be substituted with the value of the environment variable whose name is “variableName”. For example, if the environment variable JAVA_HOME is defined as “/opt/java/jdk1.7.0”, then the following configuration:

prop.1 = ${env.JAVA_HOME}/bin/java

will be resolved into:

prop.1 = /opt/java/jdk1.7.0/bin/java

If the value of a property refers to an undefined environment variable, then the reference will be replaced with the literal syntax in its initial definition, that is in the literal form “${env.<UndefinedVariable>}”.
#### System properties substtutions
References to system properties work in exactly the same way as for environment variables, except that the prefix for a system property reference is "sys." instead of "env.". The syntax for the reference is then "${sys.systemPropertyName}".

For example, if the Java command includes an option "-DTest.property=some.test.value", then the following configuration property:

prop.1 = ${sys.Test.property}

will be resolved into:

prop.1 = some.test.value
### Scripted property values
The values of configuration properties can be partially or complety computed as expressions written in any JSR 223-compliant dynamic script language. Such properties contain one or more expressions of the form:

my.property = $script:language:source_type{script_source}$

Where:

- language is the script language to use, such as provided by the javax.script APIs. It defaults to "javascript"
- source_type determines how to find the script, with possible values "inline", "file" or "url". It defaults to "inline"
- script_source is either the script expression, or its location, depending on the value of source_type:
- if source_type = inline, then script_source is the script itself.
  For example: my.prop = $script:javascript:inline{"hello " + "world"}$
- if source_type = file, then script_source is a script file, looked up first in the file system, then in the classpath.
  For example: my.prop = $script:javascript:file{/home/me/myscript.js}$
- if source_type = url, then script_source is a script loaded from a URL.
  For example: my.prop = $script:javascript:url{file:///home/me/myscript.js}$

If the language or source type are left unspecified, they will be assigned their default value. For instance the following patterns will all resolve in language = 'javascript' and source_type = 'inline' :

$script{ 2 + 3 }$
$script:{ 2 + 3 }$
$script::{ 2 + 3 }$
$script::inline{ 2 + 3 }$
$script:javascript{ 2 + 3 }$
$script:javascript:{ 2 + 3 }$

Note: the syntax for scripted values may be quite cumbersome. It is possible to alleviate it by using 'S' or 's' instead of "script", and the first character (case insensitive) of the source type instead of its full name. For instance, the following properties are equivalent and will resolve to the exact same value:
prop.1 = $script:js:file{/home/me/script.js}$
prop.2= $S:js:f{/home/me/script.js}$

The default script language can be specified with the property 'jppf.script.default.language'. This property is always evaluated first, in case it is also expressed with script expressions (which can only be in javascript). If it is not specified explicitely, it will default to 'javascript'. For example, in the following:

# using javascript expression to set the default language to groovy
jppf.script.default.language = $script{ 'groo' + 'vy' }$
# inline expression using default language 'groovy'
my.property = $script{ return 2 + 3 }$

The value of 'my.property' will evaluate to 5, resulting from the inline groovy expression 'return 2 + 3'.

The scripts are evaluated after all includes and variable substitutions have been resolved. This will allow the scripts to use a variable binding for the Properties (or TypedProperties object) being loaded, with the best possible accuracy. For example, in the following:

prop.1 = hello world
prop.2 = $script:javascript{ thisProperties.getString('prop.1') + ' of scripting' }$

the value of 'prop.2' will evaluate to 'hello world of scripting', which is the value of 'prop.1' to which another string is concatenated. The predefined variable thisProperty is bound to the properties object being evaluated. Note that the same result can be achieved with a property substitution:

prop.1 = hello world
prop.2 = $script:javascript{ '${prop.1}' + ' of scripting' }$

Here, the substitution of ${prop.1} is performed before the script evaluation, and must be enclosed within quotes to be parsed as a string literal inside the script.

Finally, property values can contain any number of script expressions, which can be written in different script languages and loaded from different sources. For example, the value of the following property:

prop.1 = hello $script:javascript{'my ' + 'world'}$ number $script:groovy{return 2 + 3}$

will evaluate to 'hello my world number 5'.
## Reminder: JPPF topology
Before reviewing the details of each configuration property, it is useful to have the big picture of what we are configuring exactly. In a few words, a JPPF grid is made of clients (instances of your applications), servers and nodes. An application submits jobs to a server, and a server distributes the tasks in each job to its attached nodes. The simplest configuration you can have would be as illustrated in this picture:

We can see here that we have a single client communicating with one server, to which a single node is attached. In practice, there will be many nodes attached to the server, and many clients will be able to communicate with the server concurrently. It is also possible to link servers together, forming a peer-to-peer network of JPPF servers, allowing servers to delegate a part of their workload to other servers.
We could effectively build a much more complex JPPF network, such as the one in this picture:

The role of the configuration will be essentially to determine where each component can find the others, and how their interactions will be processed.
## Configuring a JPPF server
### Basic network configuration
The server network communication mechanism uses TCP/IP to do its basic work of receiving jobs and dispatching them for execution, over plain connections, secure connections, or both. Each type of connection requires the configuration of a dedicated TCP port In the configuration file, this property would be defined as follows, with its default value:

# JPPF server port for plain connections; default value is 11111
jppf.server.port = 11111

# JPPF server port for secure connections via SSL/TLS; default value is -1
jppf.ssl.server.port = 11143

Note 1: to disable either plain or secure connectivity, set the corresponding port value to -1.

Note 2: secure connectivity is disabled by default, therefore you must explicitely configure the secure port to enable it

Note 3: when the port number is set to 0, JPPF will dynamically allocate a valid port number. Note that this feature is mostly useful when server discovery is enabled, since the port number will not be known in advance to connecting nodes.and client
### Server JVM options
A JPPF server is in fact made of two processes: a “controller” process and a “server” process. The controller launches the server as a separate process and watches its exit code. If the exit code has a pre-defined value of 2, then it will restart the server process, otherwise it will simply terminate. This mechanism allows the remote (eventually delayed) restart of a server using the management APIs or the management console. It is also made such that, if any of the two processes dies unexpectedly, then the other process will die as well, leaving no lingering Java process in the OS.

The server process inherits the following parameters from the controller process:
- location of jppf configuration (-Djppf.config or -Djppf.config.plugin)
- location of Log4j configuration (-Dlog4j.configuration)
- current directory
- environment variables
- Java class path

It is possible to specify additional JVM parameters for the server process, using the configuration property jppf.jvm.options, as in this example:

jppf.jvm.options = -Xms64m -Xmx512m

Here is another example with remote debugging options:

jppf.jvm.options = -server -Xmx512m \
 -Xrunjdwp:transport=dt_socket,address=localhost:8000,server=y,suspend=n

It is possible to specify additional class path elements through this property, by adding one or more “-cp” or “-classpath” options (unlike the Java command which only accepts one). For example:

jppf.jvm.options = -cp lib/myJar1.jar:lib/myJar1.jar -Xmx512m \
  -classpath lib/external/externalJar.jar

This syntax allows configuring multiple paths in an OS-independant way, in particular with regards to the path separator character (e.g. ':' on Linux, ';' on Windows).

If a classpath element contains one or more spaces, the path(s) if defines must be surrounded with double quotes:

jppf.jvm.options = -Xmx512m -cp "dir with spaces/myJar1.jar" -cp NoSpaces/myJar2.jar
### Server discovery through UDP multicast
By default, JPPF nodes and clients are configured to automatically discover active servers on the network. This is made possible because, by default, a JPPF server will broadcast the required information (i.e. host address and port numbers) using the UDP multicast mechanism.
#### Enabling and disabling UDP multicast
This is done with the following property, which defaults to true (enabled):

# Enable or disable broadcast of the JPPF driver's information s via UDP multicast
jppf.discovery.enabled = true
#### Configuration of UDP multicast
The configuration is done by defining a multicast group and port number, as in this example showing their default values:

# UDP multicast group to which the driver broadcasts its connection parameters
jppf.discovery.group = 230.0.0.1
# UDP multicast port to which the driver broadcasts its connection parameters
jppf.discovery.port = 11111
#### Broadcast interval
Since the UDP protocol offers no guarantee of delivery, the JPPF driver will periodically broadcast its connection information, at regular intervals defined with the following property:

# How long a driver should wait between 2 broadcasts, in millis
jppf.discovery.broadcast.interval = 1000
#### Inclusion and exclusion patterns
The driver can be configured to allow or exclude broadcasting on specific network interfaces, according to their IP addresses. The following properties define inclusion and exclusion patterns for IPv4 and IPv6 addresses. Each of these patterns defines a list of comma- or semicolumn- separated patterns. The IPv4 patterns can be exppressed in either CIDR notation, or in a syntax defined in the Javadoc for the class IPv4AddressPattern. Similarly, IPv6 patterns can be expressd in CIDR notation or in a syntax defined in IPv6AddressPattern. This enables filtering out unwanted IP addresses: the discovery mechanism will only allow addresses that are included and not excluded.

# IPv4 address inclusion patterns
jppf.discovery.boradcast.include.ipv4 =
# IPv4 address exclusion patterns
jppf.discovery.boradcast.exclude.ipv4 =
# IPv6 address inclusion patterns
jppf.discovery.boradcast.include.ipv6 =
# IPv6 address exclusion patterns
jppf.discovery.boradcast.exclude.ipv6 =

Let's take for instance the following pattern specifications:

jppf.discovery.include.ipv4 = 192.168.1.
jppf.discovery.exclude.ipv4 = 192.168.1.128-

The equivalent patterns in CIDR notation would be:

jppf.discovery.include.ipv4 = 192.168.1.0/24
jppf.discovery.exclude.ipv4 = 192.168.1.128/25

The inclusion pattern only allows IP addresses in the range 192.168.1.0 ... 192.168.1.255. The exclusion pattern filters out IP addresses in the range 192.168.1.128 ... 192.168.1.255. Thus, we actually defined a filter that only accepts addresses in the range 192.168.1.0 ... 192.168.1.127.

These 2 patterns can in fact be rewritten as a single inclusion pattern:
jppf.discovery.include.ipv4 = 192.168.1.-127

or, in CIDR notation:
jppf.discovery.include.ipv4 = 192.168.1.0/25
### Connecting to other servers
We have seen in the "reminder" section that servers can connect to each other, up to a full-fledged peer-to-peer topology. When a server A connects to another server B, A will act as a node attached to B (from B's perspective). The benefit is that, when server A is connected to server B, B will be able to ollload some of its workload to server A, for example when all nodes attahed to B are already busy.

There are 4 possible kinds of connectivity between 2 servers:

- A and B are not connected at all
- A is connected to B (i.e. A acts as a node attached to B)
- B is connected to A (i.e. B acts as a node attached to A)
- A and B are connected to each other

Because of this flexibility, it is possible to define any type of topology made of JPPF drivers, up to fully connected P2P topologies.
#### Orphan servers
The default behavior when a server doesn't have any attached node (i.e.orphan server) is, for the peer servers it is connected to, to not send any job to this server. Servers are automatically notified of the number of nodes attached to their peers, and will start sending jobs their way as soon as they have at least one node.

To force a server to send jobs to their peers even when they don't have any node, for instance if you wish to set a server as a router to other servers, you can set the following property in its configuration:

# ingore the fact that peer servers may not have any node; default to false
jppf.peer.allow.orphans = true
#### Configuring peer connections manually
This will be best illustrated with an example configuration:

# define a space-separated list of peers to connect to
jppf.peers = server_1 server_2
# connection to server_1
jppf.peer.server_1.server.host = host_1
jppf.peer.server_1.server.port = 11111
jppf.peer.server_1.pool.size = 2

# connection to server_2
jppf.peer.server_2.server.host = host_2
jppf.peer.server_2.server.port = 11111
jppf.peer.server_2.pool.size = 2

To connect to each peer, we must define its IP address or host name as well as a port number. Please note that the value we have defined for "jppf.peer.server_1.server.port" must be the same as the one defined for "jppf.server.port" in server_1's configuration, and the value for "jppf.peer.server_1.server.port" must be equal to that of "jppf.server.port" in server_1's configuration.

As for auto-discovered servers, it is possible to specifiy the number of connections to each manually configured peer server with the "jppf.peer.<peer_name>.pool.size" property, which defaults to 1 if unspecified.
#### Discovering peer drivers via UDP multicast
In this scenario, we must enable the discovery of peer servers:

# Enable or disable auto-discovery of other peer servers (defaults to false)
jppf.peer.discovery.enabled = true
# number of connections to establish with each dicovered server, aka pool size
# (defaults to 1)
jppf.peer.pool.size = 2

For this to work, the server broadcast must be enabled on the peer server(s), and the properties defined in the previous "server discovery" section will be used, hence they must be set to the same values on the other server(s). A server can discover other servers without having to broadcast its own connection information (i.e. without being "discoverable").

Please note that the default value for "jppf.peer.discovery.enabled" is "false". Setting the default to "true" would cause each server to connect to all other servers accessible on the network, with a high risk of unwanted side effects.

It is also possible to define more than one connection with each discovered peer driver, by setting the property "jppf.peer.pool.size" to the desired number of connections. If this property is unspecified, it will default to 1.

#### Using manual configuration and server discovery together
It is possible to use the manual configuration together with the UDP multicast discovery, by adding a special driver name, “jppf_discovery”, to the list of manually configured peers:

# enable auto-discovery of other peer servers
jppf.peer.discovery.enabled = true
# specifiy both discovery and manually configured drivers
jppf.peers = jppf_discovery server_1
# connection to server_1
jppf.peer.server_1.server.host = host_1
jppf.peer.server_1.server.port = 11111
### JMX management configuration
JPPF uses JMX to provide remote management capabilities for the servers, and uses its own JMX connector for communication. The management features are enabled by default; this behavior can be changed by setting the following property:

# Enable or disable management of this server
jppf.management.enabled = true
### Load-balancing
The distribution of the tasks to the nodes is performed by the JPPF driver. This work is actually the main factor of the observed performance of the framework. It consists essentially in determining how many tasks will go to each node for execution, out of a set of tasks, or job, sent by the client application. Each set of tasks sent to a node is called a "task bundle", and the role of the load balancing (or task scheduling) algorithm is to optimize the performance by adjusting the number of task sent to each node.
#### General configuration
The algorithm to use is configured with the following property:

jppf.load.balancing.algorithm = <algorithm_name>

The algorithm name can be one of those prefefined in JPPF, or a user-defined one. JPPF has a number of predefined load-balancing algorithms to compute the distribution of tasks to the nodes, each with its own configuration parameters.

The predefined possible values for the property jppf.load.balancing.algorithm are: manual, autotuned, proportional, rl2 and nodethreads. If not specified, the algorithm defaults to manual. For example:

jppf.load.balancing.algorithm = proportional

Each algorithm uses its own set of parameters, which define together a profile for the algorithm, A profile has a name that serves to identify a group of parameters and their values, using the following pattern:

jppf.load.balancing.profile = <profile_name>

jppf.load.balancing.profile.<profile_name>.<parameter_1> = <value_1>
...
jppf.load.balancing.profile.<profile_name>.<parameter_n> = <value_n>

Using this, you can define multiple profiles and easily switch from one to the other, by simply changing the value of jppf.load.balancing.profile. It is also possible to mix, in a single profile, the parameters for multiple algorithms, however it is not recommended, as there may be name collisions.
#### Predefined algorithms
##### “manual” algorithm
With this algorithm, each bundle has a fixed number of tasks, meaning that each node will receive at most this number of tasks. This is equivalent to performing a round-robin assignment of the tasks to the nodes.

# algorithm name
jppf.load.balancing.algorithm = manual
# name of the set of parameter values or profile for the algorithm
jppf.load.balancing.profile = manual_profile

# "manual" profile
strategy.manual_profile.size = 1
##### “autotuned” algorithm
This is an: adaptive heuristic algorithm based on a simulated annealing technique. "Adaptive" means that the number of tasks sent to each node varies, depending on the node's past performance and the nature of the workload.

# algorithm name
jppf.load.balancing.algorithm = autotuned
# name of the set of parameter values or profile for the algorithm
jppf.load.balancing.profile = autotuned_profile
# "autotuned" profile
jppf.load.balancing.profile.autotuned_profile.size = 5
jppf.load.balancing.profile.autotuned_profile.minSamplesToAnalyse = 100
jppf.load.balancing.profile.autotuned_profile.minSamplesToCheckConvergence = 50
jppf.load.balancing.profile.autotuned_profile.maxDeviation = 0.2
jppf.load.balancing.profile.autotuned_profile.maxGuessToStable = 50
jppf.load.balancing.profile.autotuned_profile.sizeRatioDeviation = 1.5
jppf.load.balancing.profile.autotuned_profile.decreaseRatio = 0.2
##### “proportional” algorithm
This is an adaptive algorithm based on the contribution of each node to the overall mean task execution time.

# algorithm name
jppf.load.balancing.algorithm = proportional
# name of the set of parameter values or profile for the algorithm
jppf.load.balancing.profile = proportional_profile
# "proportional" profile
jppf.load.balancing.profile.proportional_profile.initialSize = 5
jppf.load.balancing.profile.proportional_profile.performanceCacheSize = 1000
jppf.load.balancing.profile.proportional_profile.proportionalityFactor = 1
##### “rl2” algorithm
This is an adaptive algorithm based on an artificial intelligence technique called “reinforcement learning”

# algorithm name
jppf.load.balancing.algorithm = rl2
# name of the set of parameter values or profile for the algorithm
jppf.load.balancing.profile = rl2_profile
# "rl2" profile
jppf.load.balancing.profile.rl2_profile.performanceCacheSize = 1000
jppf.load.balancing.profile.rl2_profile.performanceVariationThreshold = 0.75
jppf.load.balancing.profile.rl2_profile.minSamples = 20
jppf.load.balancing.profile.rl2_profile.maxSamples = 100
jppf.load.balancing.profile.rl2_profile.maxRelativeSize = 0.5
##### “nodethreads” algorithm
With this algorithm, each node will receive at most n * m tasks, where n is the number of processing threads in the node and m is a user-defined parameter named 'multiplicator". Note that the number f processing threads of a node can be changed dynamically through the JPPF management features, in which case the algorithm will be notfied and adapt accordingly.

# algorithm name
jppf.load.balancing.algorithm = nodethreads
# name of the set of parameter values or profile for the algorithm
jppf.load.balancing.profile = nodethreads_profile
# means that multiplicator * nbThreads tasks will be sent to each node
jppf.load.balancing.profile.nodethreads_profile.multiplicator = 1
#### Load-balancing documentation references
For a detailed explanation of the load-balancing in JPPF, its APIs and the predefined algorithms, please refer to the Load Balancing section of the manual.

Defining a custom algorithm is described in the "creating a custom load-balancer" section of this manual.
### Configuring a local node
Each JPPF driver can run a single node in its own JVM, called ”local node”. The main advantage is that the communication between server and node is much faster, since the network overhead is removed. This is particularly useful if you intend to create a pure P2P topology, where all servers communicate with each other and only one node is attached to each server.

To enable a local node in the driver, use the following configuration propoerty, which defaults to “false”:

jppf.local.node.enabled = true

Note 1: the local node can be configured using the same properties as described in the Node Configuration section, except for the network-related properties, since no network is involved between driver and local node

Note 2: for the same reason, the SSL configuration does not apply to a local node
### Heartbeat-based connection failure detection
Network disconnections due to hardware failures are notoriously difficult to detect, let alone recover from. JPPF implements a configurable heartbeat mechanism that enables detecting such failures, and recover from them, in a reasonable time frame. This mechanism works as follows:

- the JPPF node or client - designated here as heartbeat client - establishes a specific connection to the server, dedicated to failure detection
- at connection time, a handshake protocol takes place, where the heartbeat client communicates a unique id to the server, that can be correlated to other connections for this heartbeat client (job data channel, distributed class loader)
- at regular intervals (heartbeats), the server will send a very short message to the heartbeat client, who will acknowledge it by sending a short response of its own
- if the heartbeat client's response is not received in a specified time frame (heartbeat timeout), and this, a specified number of times in a row (heartbeat retries), the server will consider the connection to be broken, will close it cleanly, close the associated connections, and handle the recovery, such as requeing tasks that were being executed
- on the heartbeat client side, if no message is received from the server for a time greater than heartbeat_timeout * heartbeat_retries, then it will close its connection to the server and attempt to reconnect.

In practice, the polling of the heartbeat clients is performed by a “reaper” object that will handle the querying of the nodes, using a pool of dedicated threads rather than one thread per node. This enables a higher scalability with a large number of nodes ort clients.

The ability to specify multiple attempts at getting a response from the node is useful to handle situations where the network is slow, or when the node or server is busy with a high CPU utilization level.On the server side, the parameters of this mechanism are configurable via the following properties:

# Enable recovery from hardware failures on the nodes. Defaults to false (disabled).
jppf.recovery.enabled = true
# Maximum number of attempts to get a response form the node before the
# connection is considered broken. Default value is 3.
jppf.recovery.max.retries = 3
# Maximum time in milliseconds allowed for each attempt to get a response
# from the node. Default value is 15000 (15 seconds)
jppf.recovery.read.timeout = 15000
# Number of threads allocated to the reaper, defaults to the number of available CPUs
jppf.recovery.reaper.pool.size = 8
### Redirecting the console output
In some situations, it might be desirable to redirect the standard and error output of the driver, that is, the output of System.out and System.err, to files. This can be accomplished with the following properties:

# file on the file system where System.out is redirected
jppf.redirect.out = /some/path/someFile.out.log
# whether to append to an existing file or to create a new one
jppf.redirect.out.append = false
# file on the file system where System.err is redirected
jppf.redirect.err = /some/path/someFile.err.log
# whether to append to an existing file or to create a new one
jppf.redirect.err.append = false

By default, a new file is created each time the driver is started, unless “jppf.redirect.out.append = true” or “jppf.redirect.err.append = true” are specified. If a file path is not specified, then the corresponding output is not redirected.
### Resolution of the nodes IP addresses
You can switch on or off the DNS name resolution for the nodes connecting to this driver, with the following property:

# whether to resolve the nodes' ip addresses into host names
# defaults to true (resolve the addresses)
org.jppf.resolve.addresses = true

## Node configuration
### Server discovery
In a JPPF node, the JPPF server discovery mechanisms are all implemented as node connection strategy plugins. JPPF provides several built-in such strategies, including the default strategy which uses the node configuration to find a JPPF driver to connect to. This mechanism allows both automatic discovery via UDP multicast, and manual configuration of the connection. These two features are described in the following sections.
#### Discovery through UDP multicast
By default, JPPF nodes are configured to automatically discover active servers on the network. As we have seen in the server discovery section of the JPPF driver configuration, this is possible thanks to the UDP broadcast mechanism of the server. On the other end, the node needs to join the same UDP group to subscribe to the bradcasts from the server.
##### Enabling and disabling UDP multicast
This is done with the following property, which defaults to true (enabled):

# Enable or disable automatic discovery of JPPF drivers via UDP multicast
jppf.discovery.enabled = true
##### Configuration of UDP multicast
The configuration is performed by defining a multicast group and port number, as in this example showing their default values:

# UDP multicast group to which drivers broadcast their connection parameters
jppf.discovery.group = 230.0.0.1
# UDP multicast port to which drivers broadcast their connection parameters
jppf.discovery.port = 11111

Note: the values of these properties must be the same as those defined in the server configuration.
##### Inclusion and exclusion patterns
The following properties define inclusion and exclusion patterns for IPv4 and IPv6 addresses. They provide a means of controlling whether to connect to a server, based on its IP address. Each of these patterns defines a list of comma- or semicolumn- separated patterns. The IPv4 patterns can be exppressed in either CIDR notation, or in a syntax defined in the Javadoc for the class IPv4AddressPattern. Similarly, IPv6 patterns can be expressd in CIDR notation or in a syntax defined in IPv6AddressPattern. This enables filtering out unwanted IP addresses: the discovery mechanism will only allow addresses that are included and not excluded.

# IPv4 address inclusion patterns
jppf.discovery.include.ipv4 =
# IPv4 address exclusion patterns
jppf.discovery.exclude.ipv4 =
# IPv6 address inclusion patterns
jppf.discovery.include.ipv6 =
# IPv6 address exclusion patterns
jppf.discovery.exclude.ipv6 =

Let's take for instance the following pattern specifications:

jppf.discovery.include.ipv4 = 192.168.1.
jppf.discovery.exclude.ipv4 = 192.168.1.128-

The equivalent patterns in CIDR notation would be:

jppf.discovery.include.ipv4 = 192.168.1.0/24
jppf.discovery.exclude.ipv4 = 192.168.1.128/25

The inclusion pattern only allows IP addresses in the range 192.168.1.0 ... 192.168.1.255. The exclusion pattern filters out IP addresses in the range 192.168.1.128 ... 192.168.1.255. Thus, we actually defined a filter that only accepts addresses in the range 192.168.1.0 ... 192.168.1.127.

These 2 patterns can in fact be rewritten as a single inclusion pattern:
jppf.discovery.include.ipv4 = 192.168.1.-127

or, in CIDR notation:
jppf.discovery.include.ipv4 = 192.168.1.0/25
#### Manual connection configuration
If server discovery is disabled, network access to a server must be configured manually. To this effect, the node requires the address or host on which the JPPF server is running, and a TCP port, as shown in this example:

# IP address or host name of the server
jppf.server.host = my_host
# JPPF server port
jppf.server.port = 11111

Not defining these properties is equivalent to assigning them their default value (i.e. “localhost” for the host address, 11111 or 11143 for the port number, depending on whether secure connectivity is disabled or enabled, respectively).
#### Enabling secure connectivity
To enable secure connectivity via SSL/TLS for the configured connections, simply set the following:

# enable SSL/TLS over the discovered connections; defaults to false (disabled)
jppf.ssl.enabled = true
#### Heartbeat-based connection failure detection
The heartbeat mechanism to recover from hardware failure is enabled in the node with the following configuration property:

# Enable recovery from hardware failures on the node. Default is false (disabled)
jppf.recovery.enabled = true

As described in the server configuration counterpart, when the node hasn't received any heartbeat message for a time greater than heartbeat_timeout * heartbeat_retries, then it will close its connection to the server and attempt to reconnect.
#### Interaction between connection recovery and server discovery
When discovery is enabled for the node (jppf.discovery.enabled = true) and the maximum reconnection time is not infinite (reconnect.max.time = <strictly_positive_value>), a sophisticated failover mechanism takes place, following the sequence of steps below:

- the node attempts to reconnect to the driver to which it was previously connected (or attempted to connect), during a maximum time specified by the configuration property "reconnect.max.time"
- during this maximum time, it will make multiple attempts to connect to the same driver. This covers the case when the driver is restarted in the mean time.
- after this maximum time has elapsed, it will attempt to auto-discover another driver, during a maximum time, specified via the configuration property "jppf.discovery.timeout" (in milliseconds)
- if the node still fails to reconnect after this timeout has expired, it will fall back to the driver manually specified in the node's configuration file
- the cycle starts again
### Node JVM options
In the same way as for a server (see server JVM options), the node is made of 2 processes: a “controller” process and a “node” process. The controller launches the node as a separate process and watches its exit code. If the exit code has a pre-defined value of 2, then the controller will restart the node process, otherwise it will simply terminate.

This mechanism allows the remote restart (eventually delayed) of a JPPF node using the management APIs or the management console. It is also made such that, if any of the two processes dies unexpectedly, then the other process will die as well, leaving no lingering Java process in the OS.

The node process inherits the following parameters from the controller process:
- location of jppf configuration (-Djppf.config or -Djppf.config.plugin)
- location of Log4j configuration (-Dlog4j.configuration)
- current directory
- environment variables
- Java class path

It is possible to specify additional JVM parameters for the server process, using the configuration property jppf.jvm.options, as in this example:

jppf.jvm.options = -Xms64m -Xmx512m

Here is another example with assertions enabled and remote debugging options:

jppf.jvm.options = -server -Xmx512m -ea \
 -Xrunjdwp:transport=dt_socket,address=localhost:8000,server=y,suspend=n

Contrary to the Java command line, It is possible to specify multiple class path elements through this property, by adding one or more “-cp” or “-classpath” options. For example:

jppf.jvm.options = -cp lib/myJar1.jar:lib/myJar1.jar -Xmx512m \
  -classpath lib/external/externalJar.jar

This syntax allows configuring multiple paths in an OS-independant way, in particular with regards to the path separator character (e.g. ':' on Linux, ';' on Windows).

If a classpath element contains one or more spaces, the path(s) it defines must be surrounded with double quotes:

jppf.jvm.options = -Xmx512m -cp "dir with spaces/myJar1.jar" -cp NoSpaces/myJar2.jar
### JMX management configuration
JPPF uses JMX to provide remote management capabilities for the nodes, and uses its own JMX connector for communication. The management features are enabled by default; this behavior can be changed by setting the following property:

# Enable or disable management of this node
jppf.management.enabled = true

When management is enabled, the JPPF node runs its own JMX remote sevrer. The port on which this JMX server will listen can be defined as follows:

# JMX management port; defaults to 11198
jppf.node.management.port = 11198

Note: if the specified JMX port is already in use, the JPPF node will lookup the next port numbers in sequence, until it finds one that is available.
### Processing threads
A node can process multiple tasks concurrently, using a pool of threads. The size of this pool is configured as follows:

# number of threads running tasks in this node
jppf.processing.threads = 4

If this property is not defined, its value defaults to the number of processors or cores available to the JVM.
### Class loader cache
Each node creates a specific class loader for each new client whose tasks are executed in that node. The cache itself is managed as a bounded queue, and the oldest class loader will be evicted from the cache whenever the maximum size is reached. The evicted class loader then becomes unreachable and can be garbage collected. In most modern JDKs, this also results in the classes being unloaded.

If the class loader cache size is too large, this can lead to an out of memory condition in the node, especially in these 2 scenarios:

- if too many classes are loaded, the space reserved to the class definitions (permanent generation in Oracle JDK) will fill up and cause an “OutOfMemoryError: PermGen space”
- if the classes hold a large amount of static data (via static fields and static initializers), an “OutOfMemoryError: Heap Space” will be thrown

To mitigate this, the size of the class loader cache can be configured in the node as follows:

jppf.classloader.cache.size = 50

The default value for this property is 50, and the value must be at least equal to 1.
### Class loader resources cache
To avoid uncessary network round trips, the node class loaders can store locally the resources found in their extended classpath when one of their methods getResourceAsStream(), getResource(), getResources() or getMultipleResources() is called. This cache is enabled by default and the type of storage and location of the file-persisted cache can be configured as follows:

# whether the resource cache is enabled, defaults to 'true'
jppf.resource.cache.enabled = true
# type of storage: either 'file' (the default) or 'memory'
jppf.resource.cache.storage = file
# root location of the file-persisted caches
jppf.resource.cache.dir = some_directory

When “file” persistence is configured, the node will fall back to memory persistence if the resource cannot be saved to the file system for any reason. This could happen, for instance, when the file system runs out of space.

For more details, please refer to the local caching of network resources section of this documentation.
### Security policy
To limit what the nodes can do on the machine that hosts them, It is possible to specify what permissions are granted to them on their host. These permissions are based on the Java security policy model.

To implement security, nodes require a security policy file. The syntax of this file is similar to that of Java security policy files, except that it only accepts permission entries (no grant or security context entries).

Some examples of permission entries:

// permission to read, write, delete node log file in current directory
permission java.io.FilePermission "${user.dir}/jppf-node.log", "read,write,delete";
// permission to read all log4j system properties
permission java.util.PropertyPermission "log4j.*", "read";
// permission to connect to a MySQL database on the default port on localhost
permission java.net.SocketPermission "localhost:3306", "connect,listen";

To enable the security policy, the node configuration file must contain the following property definition:

# Path to the security file, relative to the current directory or classpath
jppf.policy.file = jppf.policy

When this property is not defined, or the policy file cannot be found, security is disabled.

The policy file does not have to be local to the node. If it is not present locally, the node will download it from the server. In this case it has to be locally accessible by the server, and the path to the policy file will be interpreted as path on the server's file system. This feature, combined with the ablity to remotely restart the nodes, allows to easily update and propagate changes to the security policy for all the nodes.
### Offline mode
A node can be configured to run in “offline” mode. In this mode, there will be no class loader connection to the server (and thus no distributed dynamic class loading will occur), and remote management via JMX is disabled. For more details on this mode, please read the documentation section on offline nodes.

To turn the offline mode on:

# set the offline mode (false by default)
jppf.node.offline = true
### Redirecting the console output
As for JPPF drivers, the output of System.out and System.err of a node can be redirected to files. This can be accomplished with the following properties:

# file on the file system where System.out is redirected
jppf.redirect.out = /some/path/someFile.out.log
# whether to append to an existing file or to create a new one
jppf.redirect.out.append = false

# file on the file system where System.err is redirected
jppf.redirect.err = /some/path/someFile.err.log
# whether to append to an existing file or to create a new one
jppf.redirect.err.append = false

By default, a new file is created each time the node is started, unless “jppf.redirect.out.append = true” or “jppf.redirect.err.append = true” are specified. If a file path is not specified, then the output is not redirected.
### Specifying the path to the JVM
It is possible to choose which JVM will run a node, by specifying the full path to the Java executable with the following property:

# Full path to the java executable
jppf.java.path = <path_to_java_executable>
# Linux example
jppf.java.path = /opt/jdk1.8.0/bin/java
# Windows example
jppf.java.path = C:/java/jdk1.7.0/bin/java.exe

This property is used in several situations:

- by the shell script from the node distribution that launches the node (startNode.sh or startNode.bat)
- by slave nodes when the property is specified as a configuration override, allowing to start a slave node with a different JVM than its master's
- when a node is restarted with one of the JPPFNodeAdminMBean.updateConfiguration() management methods with jppf.java.path specified as an overriden property.

## Client and administration console configuration
### Server discovery in the client
Connection pools: when a JPPF client connects to one or more servers, its connections are organized by pools. All the connections in a pool share the same basic characteristics:

- name given to the pool, used as a prefix for individual connections names. A pool named "pool" will name its individual connections as "pool-1", ..., "pool-N", where N is the number of connections in the pool.
- server host or IP address
- server port
- whether secure connectivity via SSL/TLS is enabled
- pool priority: allows defining a failover hierarchy of connection pools, where the client only uses the available pool(s) with the highest priority. Whenever these pools become unavailable for any reason, the client will fall back to the pools with the next highest priorirty, switching back to the previous pools later on if they become available again
- associated JMX connections pool size: each connection pool also maintains one or more JMX connections to allow the administration and monitoring of the corresponding server

Pool size: in addition to the propertie above, each connection pool has a size, which determines how many connections it manages. The size of a connection pool can be defined statically in the configuration, but it can also be changed programmatically using the connection pools API.

Definition: server discovery is the mechanism by which a JPPF client finds which servers to connect to, how to connect to them and organizes this information into a set of connections pools.

In a JPPF client, all server discovery strategies are implemented as discovery plugins. By default, JPPF provides a built-in discovery mechanism that uses the client configuration properties to find which servers to connect to. This mechanism allows automatic discovery via UDP multicast, along with the manual configuration of the connections pools. These two features are described in the following sections.
#### Discovery through UDP multicast
By default, JPPF clients are configured to automatically discover active servers on the network via UDP multicast. With this mechanism, the server broadcasts data packets on the network that contain sufficient information to establish a standard TCP/IP connection.
##### Enabling and disabling UDP multicast
This is done with the following property, which defaults to true (enabled):

# Enable or disable automatic discovery of JPPF drivers via UDP multicats
jppf.discovery.enabled = true

When discovery is enabled, the client does not stop attempting to find one or more servers. A client can also connect to multiple servers, and will effectively connect to every server it discovers on the network.
##### Configuration of UDP multicast
The configuration is performed by defining a multicast group and port number, as in this example showing their default values:

# UDP multicast group to which drivers broadcast their connection parameters
jppf.discovery.group = 230.0.0.1
# UDP multicast port to which drivers broadcast their connection parameters
jppf.discovery.port = 11111

Note: the values of these properties must be the same as those defined in the server configuration.
##### Connection pool size
The JPPF client will manage a pool of connections for each discovered server. The size of the connection pools is configured with the following property:

# connection pool size for each discovered server; defaults to 1 (single connection)
jppf.pool.size = 5

##### JMX Connection pool size
Each server connection pool has an associated pool of JMX connections, whose size is configured as follows:

# JMX connection pool size, defaults to 1
jppf.jmx.pool.size = 1
##### Connections naming
Each server connection has an assigned name, following the pattern: “jppf_discovery-<n>-<p>”, where n is a driver number, in order of discovery, and p is the connection number within the corresponding connection pool. For instance, if we defined jppf.pool.size = 2, then the first discovered driver will have 2 connections named “jppf_discovery-1-1” and “jppf_discovery-1-2”
##### Enabling secure connectivity
To enable secure connectivity via SSL/TLS for the discovered connections, simply set the following:

# enable SSL/TLS over the discovered connections
jppf.ssl.enabled = true
##### Connections pools priority
It is also possible to specify the priority of all discovered server connections, so that they will easily fit into a failover or load-balancing strategy:

# priority assigned to all auto-discovered connections; defaults to 0
# this is equivalent to "<driver_name>.jppf.priority" in manual network configuration
jppf.discovery.priority = 10
##### Inclusion and exclusion patterns
The following four properties define inclusion and exclusion patterns for IPv4 and IPv6 addresses. They provide a means of controlling whether to connect to a server, based on its IP address. Each of these patterns defines a list of comma- or semicolumn- separated patterns. The IPv4 patterns can be exppressed in either CIDR notation, or in a syntax defined in the Javadoc for the class IPv4AddressPattern. Similarly, IPv6 patterns can be expressd in CIDR notation or in a syntax defined in IPv6AddressPattern. This enables filtering out unwanted IP addresses: the discovery mechanism will only allow addresses that are included and not excluded.

# IPv4 address inclusion patterns
jppf.discovery.include.ipv4 =
# IPv4 address exclusion patterns
jppf.discovery.exclude.ipv4 =
# IPv6 address inclusion patterns
jppf.discovery.include.ipv6 =
# IPv6 address exclusion patterns
jppf.discovery.exclude.ipv6 =

Let's take for instance the following pattern specifications:

jppf.discovery.include.ipv4 = 192.168.1.
jppf.discovery.exclude.ipv4 = 192.168.1.128-

The equivalent patterns in CIDR notation would be:

jppf.discovery.include.ipv4 = 192.168.1.0/24
jppf.discovery.exclude.ipv4 = 192.168.1.128/25

The inclusion pattern only allows IP addresses in the range 192.168.1.0 ... 192.168.1.255. The exclusion pattern filters out IP addresses in the range 192.168.1.128 ... 192.168.1.255. Thus, we actually defined a filter that only accepts addresses in the range 192.168.1.0 ... 192.168.1.127.

These 2 patterns can in fact be rewritten as a single inclusion pattern:
jppf.discovery.include.ipv4 = 192.168.1.-127

or, in CIDR notation:
jppf.discovery.include.ipv4 = 192.168.1.0/25
##### Accepting multiple network interfaces per server
Additionally, you can specify the behavior to adopt, when a driver broadcasts its connection information for multiple network interfaces. In this case, the client may end up creating multiple connections to the same driver, but with different IP addresses. This default behavior can be disabled by setting the following property:

# enable or disable multiple network interfaces for each driver
jppf.pool.acceptMultipleInterfaces = false

This property defaults to false, meaning that only the first discovered interface for a driver will be taken into account.
##### Heartbeat-based connection failure detection
To enable the detection of connection failure through a heartbeat mechanism, set the following property:

# enable the heartbeat mechanism for all discovered drivers; defaults to false (disabled)
jppf.recovery.enabled = true

Note 1: the heartbeat mechanism must also be enabled in the remote server's configuration
Note 2: this setting applies to all servers discovered via UDP multicast
#### Manual network configuration
As we have seen, a JPPF client can connect to multiple drivers. The first step will thus be to list and name these drivers:

# space-separated list of drivers this client may connect to
# defaults to “default-driver”
jppf.drivers = driver-1 driver-2

Then for each driver, we will define the connection attributes, each of them suffixed with "driver-1." or "driver-2.".
##### Connection to the JPPF server
The host name (or IP address) and port of each named server are defined as follows:

# host name, or ip address, of the host the JPPF driver is running on
driver-1.jppf.server.host = localhost
# port number for the on which the driver accepts connections
driver-1.jppf.server.port = 11111

When left unspecifed, they will default to "localhost" and "11111", respectively.
##### Connection pool size
# size of the pool of connections to this driver; defaults to 1
driver-1.jppf.pool.size = 5

Note that, contrary to UDP multicast discovery, each manually configured connection pool can have a different size
##### JMX Connection pool size
The size of the associated JMX connection pool is configured as follows:

# JMX connection pool size, defaults to 1
driver-1.jppf.jmx.pool.size = 1
##### Enabling secure connectivity
To enable secure connectivity via SSL/TLS for the configured connections, simply set the following:

# enable SSL/TLS over the discovered connections; defaults to fals (disabled)
driver-1.jppf.ssl.enabled = true
##### Priority
# assigned driver priority; defaults to 0
driver-1.jppf.priority = 10

The priority assigned to a server connection enables the defintion of a fallback strategy for the client. In effect, the client will always use connections that have the highest priority. If the connection with the server is interrupted, then the client will use connections with the next highest priority in the remaining accessible server connection pools.
##### Heartbeat-based connection failure detection
To enable the detection of connection failure through a heartbeat mechanism, set the following property:

# enable the heartbeat mechanism for all discovered drivers; defaults to false (disabled)
driver-1.jppf.recovery.enabled = true

Note: the heartbeat mechanism must also be enabled in the remote server's server's configuration.
#### Using manual configuration and UDP multicast together
It is possible to use the manual server configuration simultaneously with the UDP multicast discovery, by adding a special driver name, “jppf_discovery” to the list of manually configured drivers:

# enable discovery
jppf.discovery.enabled = true
# specifiy both discovery and manually configured drivers
jppf.drivers = jppf_discovery driver-1
# host for this driver
driver-1.jppf.server.host = my_host
# port for this driver
driver-1.jppf.server.port = 11111
### Load-balancing and failover of server connection pools
Connection pools can be organized in any combination of two modes, using the priority attribute of each pool:

Load-balancing mode occurs when the connection pools have the same priority. In this case, the JPPF client will balance the jobs between the connections of the pools, according to the load-balancer settings. Example configuration:

jppf.drivers = driver-1 driver-2

driver-1.jppf.server.host = my.host1.com
driver-1.jppf.server.port = 11111
driver-1.jppf.priority = 20

driver-2.jppf.server.host = my.host2.com
driver-2.jppf.server.port = 11111
driver-2.jppf.priority = 20

Failover mode occurs when connection pools have different priorities. In this case, the JPPF client will only send jobs through the pool(s) with the highest priority. If the highest priority pool fails for any reason, the JPPF client will then fall back to the highest priority among the remaining connection pools, and so on. The following example shows such a configuration:

jppf.drivers = primary-pool secondary-pool

primary-pool.jppf.server.host = my.host1.com
primary-pool.jppf.server.port = 11111
primary-pool.jppf.priority = 20

secondary-pool.jppf.server.host = my.host2.com
secondary-pool.jppf.server.port = 11111
secondary-pool.jppf.priority = 10

You can also combine load-balancing and failover modes, since there is no limit to the number of connection pools you can define. For example:

jppf.drivers = primary-pool-1 primary-pool-2 secondary-pool-1 secondary-pool-2

primary-pool-1.jppf.server.host = my.host1.com
primary-pool-1.jppf.server.port = 11111
primary-pool-1.jppf.priority = 20

primary-pool-2.jppf.server.host = my.host2.com
primary-pool-2.jppf.server.port = 11111
primary-pool-2.jppf.priority = 20

secondary-pool-1.jppf.server.host = my.host3.com
secondary-pool-1.jppf.server.port = 11111
secondary-pool-1.jppf.priority = 10

secondary-pool-2.jppf.server.host = my.host4.com
secondary-pool-2.jppf.server.port = 11111
secondary-pool-2.jppf.priority = 10
### Local and remote execution
It is possible for a client to execute jobs locally (i.e. in the client JVM) rather than by submitting them to a server. This feature allows taking advantage of muliple CPUs or cores on the client machine, while using the exact same APIs as for a distributed remote execution. It can also be used for local testing and debugging before going “live”.

Local execution is disabled by default. To enable it, set the following configuration property:

# enable local job execution; defaults to false
jppf.local.execution.enabled = true

Local execution uses a pool of threads, whose size is configured as follows:

# number of threads to use for local execution
# the default value is the number of CPUs or cores available to the JVM
jppf.local.execution.threads = 4

A priority can be assigned to the local executor, so that it will easily fit into a failover strategy defined via the manual network configuration:

# priority assigned to the local executor; defaults to 0
# this is equivalent to "<driver_name>.jppf.priority" in manual network configuration
jppf.local.execution.priority = 10

It is also possible to mix local and remote execution. This will happen whenever the client is connected to a server and has local execution enabled. In this case, the JPPF client uses an adaptive load-balancing alogrithm to balance the workload between local execution and node-side execution.

Finally, the JPPF client also provides the ability to disable remote execution. This can be useful if you want to test the execution of jobs purely locally, even if the server discovery is enabled or the server connection properties would otherwise point to a live JPPF server. To achieve this, simply configure the following:

# enable remote job execution; defaults to true
jppf.remote.execution.enabled = false

Important note: when remote execution is disabled with jppf.remote.execution.enabled = false, neither UDP multicast discovery nor manual network configuration settings will have any effect anymore. In effect, this property allows to completely disable the built-in server discovery mechanisms, while still allowing optional custom discovery mechanisms to work.
### Load-balancing in the client
The JPPF client allows load balancing between local and remote execution. The load balancing configuration is exactly the same as for the driver, which means it uses exactly the same configuration properties, algorithms, parameters, etc...
Please refer to the driver load-balancing configuration section for the configuration details. The default configuration, if none is provided, is equivalent to the following:

# name of the load balancing algorithm
jppf.load.balancing.algorithm = manual
# name of the set of parameter values (aka profile) to use for the algorithm
jppf.load.balancing.profile = jppf
# "jppf" profile
jppf.load.balancing.profile.jppf.size = 1000000

Also note that the load balancing is active even if only one remote execution is available. This has an impact on how tasks within a job will be sent tot he server. For instance, if the “manual” algorithm is configured, with a size of 1, this means the tasks in a job will be sent one at a time.
### Resolution of the drivers IP addresses
You can switch on or off the DNS name resolution for the drivers a client connects, with the following property:

# whether to resolve the drivers' ip addresses into host names
# defaults to true (resolve the addresses)
org.jppf.resolve.addresses = true
### Socket connections idle timeout
In some environments, a firewall may be configured to automatically close socket connections that have been idle for more than a specified time. This may lead to a situation where a server may be unaware that a client was disconnected, and cause one or more jobs to never return. To remedy to that situation, it is possible to configure an idle timeout on the client side of the connection, so that the connection can be closed cleanly and grid operations can continue unhindered. This is done via the following property:

jppf.socket.max-idle = timeout_in_seconds

If the timeout value is less than 10 seconds, then it is considered as no timeout. The default value is -1.
### UI refresh intervals in the administration tool
You may change the values of these properties if the graphical administration and monitoring tool is having trouble displaying all the information received from the nodes and servers. This may happen when the number of nodes and servers becomes large and the UI cannot cope. Increasing the refresh intervals (or decreasing the frequency of the updates) in the UI resolves such situations. The available configuration properties are defined as follows:

# refresh interval for the statistcs panel in millis; defaults to 1000
# this is the interval between 2 succesive stats requests to a driver via JMX
jppf.admin.refresh.interval.stats = 1000

# refresh interval in millis for the topology panels: tree view and graph view
# this is the interval between 2 successive runs of the task that refreshes the
# topology via JMX requests; defaults to 1000
jppf.admin.refresh.interval.topology = 1000

# refresh interval for the JVM health panel in millis; defaults to 1000
# this is the interval between 2 successive runs of the task that refreshes
# the JVM health via JMX requests
jppf.admin.refresh.interval.health = 1000

# UI refresh interval for the job data panel in ms. Its meaning depends on the
# publish mode specified with property "jppf.gui.publish.mode" (see below):
# - in "immediate_notifications" mode, this is not used
# - in "deferred_notifications" mode, this is the interval between 2 publications
# of updates as job monitoring events
# - in "polling" mode this is the interval between 2 polls of each driver
jppf.gui.publish.period = 1000

# UI refresh mode for the job data panel. The possible values are:
# - polling: the job data is polled at regular intervals and updates to the view are
# computed as the differences with the previous poll. This mode generates less network
# traffic than the other modes, but some updates, possibly entire jobs, may be missed
# - deferred_notifications: updates are received as jmx notifications and published at
# regular intervals, possibly aggregated in the interval. This mode provides a more
# accurate view of the jobs life cycle, at the cost of increased network traffic
# - immediate_notifications: updates are received as jmx notifications and are all
# published immediately as job monitoring events, which are pushed to the UI. In this
# mode, no event is missed, however this causes higher cpu and memory consumption
# The default value is immediate_notifications
jppf.gui.publish.mode = immediate_notifications

### Customizing the administration console's splash screen
At startup, the desktop administration console displays a splash screen made of a sequence of rolling images with a fixed text at the center. The splash screen can be customized with the following properties:

# Whether to display the animated splash screen at console startup, defaults to false
jppf.ui.splash = true
# The fixed text displayed at center of the window
jppf.ui.splash.message = The JPPF Admin Console is starting ...
# The message's font color, expressed as an rgb or rgba value. If alpha is not
# specified, it is assumed to be 255 (fully opaque).
# Examples: 255, 233, 127 (opaque) | 255, 233, 127, 128 (semi-transparent)
jppf.ui.splash.message.color = 64, 64, 128
# One or more paths to the images displayed in a rolling sequence (like a slide show)
# The images may be either in the file system or in the classpath and are separated with # '|' (pipe) characters
jppf.ui.splash.images = image_path_1 | ... | image_path_N
# interval between images in milliseconds
jppf.ui.splash.delay = 500

## Common configuration properties
### Lookup of classpath resources in the file system
By default, the JPPF distributed class loader looks for requested resources in the file system (using the resource name as file path), if they are not found in the class path. This behavior can be disabled by setting the following property in a node, server or client:

# Enable or disable the lookup of classpath resources in the file system
jppf.classloader.file.lookup = true

Since this property applies to the lookup of remote resources, the file system lookup will occur if and only if this property is true in the node configuration and in the server or client configuration. Also note that its value is true by default.
### Socket connections recovery and failover
When the connection to a server is interrupted, the node, client or peer servr will automatically attempt, for a given length of time, and at regular intervals, to reconnect to the same server. These properties are configured as follows, with their default values:

# number of seconds before the first reconnection attempt
jppf.reconnect.initial.delay = 0
# time after which the system stops trying to reconnect, in seconds
# a value of zero or less means it never stops
jppf.reconnect.max.time = 60
# time between two connection attempts, in seconds
jppf.reconnect.interval = 1

With these values, we have configured the recovery mechanism such that it will attempt to reconnect to the server after a 0 second delay, for 60 seconds and with connection attemps at 1 second intervals.
### JMX requests timeout
In some very rare cases, a JMX request may be stuck because an error occurrred in the remote driver or node, without breaking the JMX connection. A typical example is when an OutOfMemoryError occurs while the remote peer is executing the request. To avoid this, it is possible to set JMX request timeout withi this configuration property:

# Timeout in millis for JMX requests. Defaults to Long.MAX_VALUE (2^63 - 1)
jppf.jmx.request.timeout = $script{ java.lang.Long.MAX_VALUE }$
### Global performance tuning parameters
These configuration properties affect the performance and throughput of I/O operations in JPPF. The values provided in the vanilla JPPF distribution (listed below) are known to offer a good performance in most situations and environments. These properties are defined as follows:

# Size of send and receive buffer for socket connections
# Defaults to 32768 and must be in range [1024, 1024*1024]
jppf.socket.buffer.size = 65536

# Size of temporary buffers (including direct buffers) used in I/O transfers
# Defaults to 32768 and must be in range [1024, 1024*1024]
jppf.temp.buffer.size = 12288

# Maximum size of temporary buffers pool (excluding direct buffers).# When this size
# is reached, new buffers are still created, but not released into the pool, so they
# can be quickly garbage-collected.
# The size of each buffer is defined with ${jppf.temp.buffer.size}
# Defaults to 10 and must be in range [1, 2048]
jppf.temp.buffer.pool.size = 200

# Size of temporary buffer pool for reading lengths as ints (size of each buffer is 4)
# Defaults to 100 and must be in range [1, 2048]
jppf.length.buffer.pool.size = 100

## Putting it all together

After seeing all the configuration details for the JPPF components, we would like to take a step back and have a look at the big picture of what the configuration is about: defining a JPPF grid topology the way we want it. For this purpose, we will define a specific non-trivial topology, and make two diagrams of this topology, where the JPPF components in each diagram are annotated with the minimal set of configuration properties that must be defined. One diagram presents the configuration when the connections between components are defined manually, the other diagram when they are automatically discovered.
### Defining a topology
Here is the JPPF topology we want to achieve:

Let's state plainly the components involved and their relationships:
- there are one client, two servers (server1 and server2) and two nodes (node1 and node2)
- the client is connected to both servers
- each server is connected to the other server
- node1 is connected to server1
- node2 is connected to server2

In the following diagrams a property definition between parentheses means that the definition uses a default value, and thus doesn't need to be defined. This notation is used to emphasize what default values actually mean. For convenience, we will also assume that server1 is on a machine with IP address 10.1.10.1 and server2 on a machine with the IP address 10.1.10.2. They also listen on ports 11111 and 11112, respectively.
### Automatic discovery of the topology

As we can see, automatic discovery involves very few configuration properties. The discovery itself is active by default (jppf.discovery.enabled = true). The client actually does not need any property at all and will work with an empty configuration. The drivers only need to override properties that define non-default values. Lastly, the nodes specify an inclusive pattern for which server to connect to, otherwise they could pickup the wrong server, connect both to the same server, etc.

Also note that, if our topology only included server1, then no configuration property at all would be needed in the client, server1, node1 or node2. That is the power of automatic discovery in JPPF master/worker topologies.
### Manual configuration of the topology

## Configuring SSL/TLS communications

A JPPF grid has the ability to use secure connections between its components. This is done by using the SSL/TLS protocols over network connections, and provides security services such as peer authentication, data encryption and data integrity. This documentation aims at describing how to configure secure connections between JPPF servers, nodes and clients. If you wish to learn details of the SSL/TLS protocols in Java, our recommendation is to read about this in the Java Secure Socket Extension (JSSE) Reference Guide.

Additionally, all downloadable JPPF components now come with a predefined set of SSL configuration files, which can be used as-is for testing purposes. These files notably include a truststore and a keystore containing self-signed certificates and private keys. For real-world secure connectivity in JPPF, you will have to provide your own key- and trust- stores, with the proper certificate chains, validated by trusted certificate authorities.
### Enabling secure connectivity
#### In the clients
There is a global property which applies to all drivers found via the auto-discovery mechanism:

# Enable SSL for auto-dsicovered drivers. Default value is false (disabled).
# If enabled, only SSL/TLS connections are established.
jppf.ssl.enabled = true

For drivers specified manually in the client configuration, SSL connectivity is specified individually:

# disable discovery
jppf.discovery.enabled = false
# mnaually specifiy two drivers
jppf.drivers = driver1 driver2

# define secure connectivity to driver1
driver1.jppf.server.host = secure_host
driver1.jppf.server.port = 11443
# secure connections are made to this driver
driver1.jppf.ssl.enabled = true

# define non-secure connectivity to driver2
driver2.jppf.server.host = non_secure_host
driver2.jppf.server.port = 11111
# the default value is false and needs not be specified
#driver2.jppf.ssl.enabled = false
#### In the nodes
Nodes use either secure connections, or non-secure connections, but not both at the same time. Thus, this is determined from a single configuration property in their respective configuration file:

# Enable SSL. Default value is false (disabled).
# If enabled, only SSL/TLS connections are established
jppf.ssl.enabled = true

For a node, this also means that its embedded JMX server will only accept secure connections. This has an impact on the driver configuration: since the driver connects to the node's JMX server, it will be considered a SSL client from the JMX perspective. This means the driver will need to have the proper node certificate in its trust store.
#### In the servers
A JPPF server has the ability to accept both secure and non-secure connections, i.e. this is not a single on/off switch as for nodes and clients. Additionally, there are 3 areas of a JPPF server that can be configured separately: “standard” connections from nodes and clients (grid jobs handling and distributed class loader), connections to other servers and embedded JMX server. These are configured via the following properties in the server's configuration file:

# Port number to which the server listens for secure connections, defaults to 11443
# A negative value indicates that no secure connection is accepted
jppf.ssl.server.port = 11443

# toggle to enable secure connections to remote peer servers, defaults to false
jppf.peer.ssl.enabled = true

# Enabling JMX features via secure connections, defaults to false
jppf.management.ssl.enabled = true

Please note that jppf.ssl.server.port (secure port) comes in addition to jppf.server.port (non secure) and that both can be used together. For instance, if you wish to only accept secure connections, you will have to disable the non-secure connection by specifying a negative port number:

# disable non-secure connections
jppf.server.port = -1
# enable secure connections
jppf.ssl.server.port = 11443

As for the non-secure port, assigning a value of 0 will cause JPPF to dynamically allocate a valid port number.

In a similar way you can use either JMX secure or non-secure connections, or both:

# Enabling JMX via non-secure connections, defaults to true
jppf.management.enabled = false
# Enabling JMX via secure connections, defaults to false
jppf.management.ssl.enabled = true
# Secure JMX server port
jppf.management.ssl.port = 11193
### Locating the SSL configuration
The SSL configuration is loaded separately from the JPPF configuration itself. The effect of this is that it is harder to find for a remote application, and it will not appear in the JPPF monitoring tools and APIs, the goal being to avoid providing information about how JPPF is secured, which would defeat the purpose of securing it in the first place.
#### Configuration as a file or classpath resource
To specify the location of the SSL configuration as a file, you can use the jppf.ssl.configuration.file property in the JPPF configuration file of the driver, node or client:

# location of the SSL configuration in the file system or classpath
jppf.ssl.configuration.file = config/ssl/ssl.properties

The lookup for the specified file or resource is performed first in the file system, then in the classpath. This allows you for instance to embed a configuration file in a jar file, with the possibility to override it with another file.

Relative paths are relative to the current working directory as specified by System.getProperty("user.dir").
#### Configuration as an external source
JPPF provides a more sophisticated way to locate its SSL configuration, which requires the implementation of a specific plugin. This is useful in situations where a configuration file is not considered secure enough, or if you need to load the configuration from a centralized location, for instance if you run JPPF in a cloud environment and want to fetch the configuration via a cloud storage facility such as Amazon's S3.

This is done via the jppf.ssl.configuration.source property:

# SSL configuration as an arbitrary source. Value is the fully qualified name
# of an implementation of java.util.concurrent.Callable<InputStream> with optional
# space-separated arguments
jppf.ssl.configuration.source = implementation_of_Callable<InputStream> arg1 ... argN

where implementation_of_Callable<InputStream> is the fully qualified name of a class which implements the interface Callable<InputStream> and which must have either a noarg constructor, or a (String...args) vararg constructor.

For example, the predefined JPPF plugin FileStoreSource is implemented as follows:

package org.jppf.ssl;

import java.io.InputStream;
import java.util.concurrent.Callable;
import org.jppf.utils.FileUtils;

// A secure store source that uses a file as source
public class FileStoreSource implements Callable<InputStream> {

  // Optional arguments that may be specified in the configuration
  private final String[] args;

  public FileStoreSource(final String... args) throws Exception {
    this.args = args;
    if ((args == null) || (args.length == 0))
      throw new SSLConfigurationException("missing parameter: file path");
  }

  @Override
  public InputStream call() throws Exception {
    // lookup in the file system, then in the classpath
    InputStream is = FileUtils.getFileInputStream(args[0]);
    if (is == null)
      throw new SSLConfigurationException("could not find file " + args[0]);
    return is;
  }
}

We can then use it in the configuration:

jppf.ssl.configuration.source = org.jppf.ssl.FileStoreSource config/ssl/ssl.properties

which is in fact equivalent to:

jppf.ssl.configuration.file = config/ssl/ssl.properties
### SSL configuration properties
These properties are defined in the SSL configuration file and represent the information required to create and initialize SSLContext, SSLSocket and SSLEngine objects.
#### SSLContext protocol
This is the protocol name used in SSLContext.getInstance(String protocol). It is defined as:

# SSLContext protocol, defaults to SSL
jppf.ssl.context.protocol = SSL

A list of valid protocol names is available here.
#### Enabled protocols
This is the list of supported protocol versions, such as returned by SSLEngine.getEnabledProtocols(). It is defined as a list of space-separated names:

# list of space-separated enabled protocols
jppf.ssl.protocols = SSLv2Hello SSLv3

A list of valid protocol versions is available here.
#### Enabled cipher suites
This is the list of supported protocol versions, such as returned by SSLEngine.getEnabledCipherSuites(). It is defined as a list of space-separated names:

# enabled cipher suites as a list of space-separated values
jppf.ssl.cipher.suites = SSL_RSA_WITH_RC4_128_MD5 SSL_RSA_WITH_RC4_128_SHA

A list of supported cipher suites is available here.
#### Client authentication
The client authentication mode is determined by calling the methods SSLEngine.getWantClientAuth() and SSLEngine.getNeedClientAuth(). It is defined as:

# client authentication mode
# possible values: none | want | need
jppf.ssl.client.auth = none
#### Key store and associated password
As for the location of the SSL configuration, there are two ways to specify the location of a keystore:

# path to the key store on the file system
jppf.ssl.keystore.file = config/ssl/keystore.ks
# an implementation of Callable<InputStream> with optional space-separated arguments
jppf.ssl.keytstore.source = org.jppf.ssl.FileStoreSource config/ssl/keystore.ks

Note that, if both properties are defined, JPPF will first attempt to load the key store from the defined source, then from the specified file path.

In a similar fashion, there are two ways to specify the key store's password: either as a clear text password, or as a password source. This can be done as follows:

# keystore password in clear text
jppf.ssl.keystore.password = password
# keystore password from an arbitrary source
# the source is an implementation of Callable<char[]> with optional parameters
jppf.ssl.keystore.password.source = org.jppf.ssl.PlainTextPassword password

Lastly, the format of the key store is specified with the following property:

# The key store format to use. When unspecified, it defaults to the value of
# KeyStore.getDefaultType(). For instance on the Oracle JVM it will be 'JKS',
# on Android's Dalvik it will be BKS, etc.
jppf.ssl.keystore.type = JKS

Note that, depending on the environment on which a node is executing, you may need to use different formats for the node's key store (if using mutual authentication) and for the driver's key store. For instance, if the node is running on Android, the "JKS" format, which is the default on the Oracle JVM, will not be supported and the key store will need to be converted to e.g. BKS (BouncyCastle KeyStore), which is the default on Android.
#### Trust store and associated password
The trust store and its password are defined in the same way as for the key store:

# path to the trust store on the file system
jppf.ssl.truststore.file = config/ssl/truststore.ks
# an implementation of Callable<InputStream> with optional space-separated arguments
jppf.ssl.truststore.source = org.jppf.ssl.FileStoreSource config/ssl/truststore.ks

# keystore password in clear text
jppf.ssl.truststore.password = password
# keystore password from an arbitrary source
# the source is an implementation of Callable<char[]> with opptional parameters
jppf.ssl.truststore.password.source = org.jppf.ssl.PlainTextPassword password

As for the key store, the format of the trust store is specified with the following property:

# the format to use for the trust store. When unspecified, it defaults to the
# value of KeyStore.getDefaultType(). For instance on the Oracle JVM it will be
# 'JKS', on Android's Dalvik it will be BKS, etc.
jppf.ssl.truststore.type = JKS

#### Special case: distinct driver trust stores for nodes and clients
In the case when the JPPF driver has mutual authentication enabled (jppf.ssl.client.auth = need”), it might be desirable to use distinct trust stores for the certificates of the nodes and the clients that will connect to the driver. This can be done as follows:

# specify that a separate trust store must be used for client certificates
jppf.ssl.client.distinct.truststore = true

# path to the client trust store on the file system
jppf.ssl.client.truststore.file = config/ssl/truststore_cli.ks
# an implementation of Callable<InputStream> with optional space-separated arguments
jppf.ssl.client.truststore.source = o.j.s.FileStoreSource config/ssl/truststore_cli.ks

# keystore password in clear text
jppf.ssl.client.truststore.password = password
# keystore password from an arbitrary source
# the source is an implementation of Callable<char[]> with opptional parameters
jppf.ssl.client.truststore.password.source = org.jppf.ssl.PlainTextPassword password

# the format to use for the client trust store. When unspecified, it defaults to
# the value of KeyStore.getDefaultType(). For instance on the Oracle JVM it will
# be 'JKS', on Android's Dalvik it will be BKS, etc.
jppf.ssl.client.truststore.type = JKS

In this configuration, a client will not be able to authenticate with the server if it uses a copy of the node's keystore, even if it uses the correct password.
### Full SSL configuration example
# SSLContext protocol, defaults to SSL
jppf.ssl.context.protocol = SSL
# list of space-separated enabled protocols
jppf.ssl.protocols = SSLv2Hello SSLv3
# enabled cipher suites as a list of space-separated values
jppf.ssl.cipher.suites = SSL_RSA_WITH_RC4_128_MD5 SSL_RSA_WITH_RC4_128_SHA
# client authentication mode; possible values: none | want | need
jppf.ssl.client.auth = none

# key store format
jppf.ssl.keystore.type = JKS
# path to the key store on the file system.
jppf.ssl.keystore.file = config/ssl/keystore.ks
# keystore password in clear text
jppf.ssl.keystore.password = password

# trust store format
jppf.ssl.truststore.type = JKS
# the trust store location as an arbitrary source:
# an implementation of Callable<InputStream> with optional space-separated arguments
jppf.ssl.truststore.source = org.jppf.ssl.FileStoreSource config/ssl/truststore.ks
# truststore password as an arbitrary source:
# an implementation of Callable<char[]> with optional space-separated arguments
jppf.ssl.truststore.password.source = org.jppf.ssl.PlainTextPassword password

## The JPPF configuration API
### General properties handling
The JPPF configuration properties are accessible at runtime, via a static method call:
JPPFConfiguration.getProperties(). This method returns an object of type TypedProperties, which is an extension of java.util.Properties with additional methods to handle properties with primitive values: boolean, int, long, float, double, char and boolean, and also String and File.

Here is a summary of the API provided by TypedProperties:

public class TypedProperties extends AbstractTypedProperties {
  // constructors
  public TypedProperties()
  // initialize with existing key/value pairs from a map
  public TypedProperties(Map<Object, Object> map)
  // string properties
  public String getString(String key)
  public String getString(String key, String defValue)
  public TypedProperties setString(String key, String value)
  // int properties
  public int getInt(String key)
  public int getInt(String key, int defValue)
  public TypedProperties setInt(String key, int value)
  // long properties
  public long getLong(String key)
  public long getLong(String key, long defValue)
  public TypedProperties setLong(String key, long value)
  // float properties
  public float getFloat(String key)
  public float getFloat(String key, float defValue)
  public TypedProperties setFloat(String key, float value)
  // double properties
  public double getDouble(String key)
  public double getDouble(String key, double defValue)
  public TypedProperties setDouble(String key, double value)
  // char properties
  public char getChar(String key)
  public char getChar(String key, char defValue)
  public TypedProperties setChar(String key, char value)
  // boolean properties
  public boolean getBoolean(String key)
  public boolean getBoolean(String key, boolean defValue)
  public TypedProperties setBoolean(String key, boolean value)
  // File properties
  public File getFile(String key)
  public File getFile(String key, File defValue)
  public TypedProperties setFile(String key, File value)
}

As you can see, each getXXX() method has a corresponding method that takes a default value, to be returned if the property is not defined for the specified key. Most of them also have a corresponding fluent setter method, which allows setting multiple properties of diffferent types in a call chain.

It is possible to alter the JPPF configuration, via calls to the setXXX(String, XXX) methods of TypedProperties. If you wish to programmatically change one or more JPPF configuration properties, then it should be done before they are used. For instance, in a client application, it should be done before the JPPF client is initialized, as in this sample code:

// get the configuration and set the connection properties programmatically
JPPFConfiguration.getProperties().setBoolean("jppf.discovery.enabled", false)
  .setString("jppf.drivers", "driver1")
  .setString("driver1.jppf.server.host", "www.myhost.com")
  .setInt("driver1.jppf.server.port", 11111);
// now our configuration will be used
JPPFClient client = new JPPFClient();

### Predefined JPPF properties
The JPPF properties documented in the Configuration properties reference chapter are also avaialable as instances of the JPPFProperty interface, which is defined as follows:

public interface JPPFProperty<T> extends Serializable {
  // Get the name of this property
  String getName();

  // Get the default value of this property
  T getDefaultValue();

  // Get the aliases for this property, that is, other names it may be known as,
  // such as legacy names from prior versions
  String[] getAliases();

  // Convert the specified value into the type of values handled by this property
  T valueOf(String value);

  // Convert the specified value to a string
  String toString(T value);

  // Return the class object for the type of values of this property
  Class<T> valueType();

  // Return a concise localized description of the property
  String getDocumentation();
}

The class JPPFProperties holds a static enumeration of the predefined properties, each with a specific type parameter. For instance, the property whose name is "jppf.server.port" holds an int value and is obtained like this:

JPPFProperty<Integer> prop = JPPFProperties.SERVER_PORT;
System.out.printf("name: %s, default: %s, type: %s%n",
  prop.getName(), prop.getDefaultValue(), prop.valueType().getName());

As much as possible, the names of the constants in JPPFProperties are kept similar to the actual properties names: the constant names are all in upper case characters, the "jppf" prefix is removed, and the dots are replaced with underscores. For example "jppf.local.execution.enabled" will correspond to the LOCAL_EXECUTION_ENABLED constant.

The class TypedProperties has specific methods that use predefined properties:

public class TypedProperties extends Properties {
  // Get the value of a predefined property
  public <T> T get(JPPFProperty<T> property);

  // Set the value of a predefined property
  public <T> TypedProperties set(JPPFProperty<T> property, T value);

  // Remove the specified predefined property
  public <T> T remove(JPPFProperty<T> property);
}

Example usage:

int nbThreads = JPPFConfiguration.getProperties().get(JPPFProperties.PROCESSING_THREADS);
JPPFConfiguration.getProperties().set(JPPFProperties.DISCOVERY_ENABLED, true)
  .set(JPPFProperties.POOL_SIZE, 5).setString("custom.property", "some value");

Note the automatic type inference that is automatically performed by the compiler, as well as the preservation of the fluent interface for setting properties, allowing both custom and predefined properties to be set in the same statement.

Additionally, the get(JPPFProperty) method automatically returns the value of the property's getDefaultValue() method, whenever the property is not defined in the configuration.
JPPFConfiguration also has shortcut methods that make use of predefined properties:

public class JPPFConfiguration {
  // Get the value of a predefined property
  public static <T> T get(JPPFProperty<T> property);

  // Set the value of a predefined property
  public static <T> TypedProperties set(JPPFProperty<T> property, T value);

  // Remove the specified predefined property
  public static <T> T remove(JPPFProperty<T> property);
}

These methods resolve into equivalent calls to JPPFConfiguration.getProperties().get/set/remove(...).

For example, these two statements do exactly the same thing

JPPFConfiguration.getProperties().set(JPPFProperties.SERVER_PORT, 11111);
JPPFConfiguration.set(JPPFProperties.SERVER_PORT, 11111);

Similarly for getting values:

int port;
port = JPPFConfiguration.getProperties().get(JPPFProperties.SERVER_PORT);
port = JPPFConfiguration.get(JPPFProperties.SERVER_PORT);

Combined with an import static statement, this leads to significantly smaller and more readable code:

import static org.jppf.utils.configuration.JPPFProperties.*;

...

int nbThreads = JPPFConfiguration.get(PROCESSING_THREADS);
JPPFConfiguration.set(DISCOVERY_ENABLED, true).set(POOL_SIZE, 5)
  .setString("custom.property", "some value").set(SERVER_PORT, 11111);
#### Parametrized properties
A parametrized property has one or more parts of its name defined as parameters which are substituted at runtime with actual string values. For instance, the following property is parameterized:

# define one RGB component of a named color
JPPFProperty<Integer> colorProp =
  new IntProperty("color.<color_name>.component.<rgb_comp>", 0):

Here, the parameters color_name and rgb_comp are recognized as such because they are enclosed within '<' and '>' delimiters. The class TypedProperties has overloads of the get(), set() and remove() methods to handle the parameters:

public class TypedProperties extends AbstractTypedProperties {
  // Get the value of a parametrized property
  public <T> T get(JPPFProperty<T> property, String...parameters);

  // Set the value of a predefined property
  public <T> TypedProperties set(JPPFProperty<T> property, T value, String...parameters);

  // Remove the specified predefined property
  public <T> T remove(JPPFProperty<T> property, String...parameters);
}

As an example, to fully define the color "cyan", we could write:

TypedProperties colors = new TypedProperties()
  .set(colorProp, 102, "cyan", "r") // red component
  .set(colorProp, 255, "cyan", "g") // green component
  .set(colorProp, 255, "cyan", "b"); // blue component

In a properties file, this would correspond to:

color.cyan.component.r = 102
color.cyan.component.g = 255
color.cyan.component.b = 255

Similarly, JPPFConfiguration overloads its get(), set() and remove() methods:

public class JPPFConfiguration {
  // Get the value of a parametrized property
  public static <T> T get(JPPFProperty<T> property, String...parameters);

  // Set the value of a parametrized property
  public static <T> TypedProperties set(
    JPPFProperty<T> property, T value, String...parameters);

  // Remove the specified parametrized property
  public static <T> T remove(JPPFProperty<T> property, String...parameters);
}

Lastly, the interface JPPFProperty also provides a getParameters() method which returns an array of the parameters names, which may be empty if the property is not parametrized..

The following example shows, using parametrized properties, how to manually configure the connection from a client to a driver.

Using a configuration file:

# non-parametrized properties
jppf.discovery.enabled = false
jppf.drivers = driver1

# parametrized properties in the form <driver_name>.jppf.xxx
driver1.jppf.server.host = 192.168.1.24
driver1.jppf.server.port = 11111
driver1.jppf.priority = 20
driver1.jppf.pool.size = 3

By API:

String driver = "driver1";
JPPFConfiguration.set(JPPFProperties.DISCOVERY_ENABLED, false)
  .set(JPPFProperties.DRIVERS, new String[] { driver })
  .set(JPPFProperties.PARAM_SERVER_HOST, "192.168.1.24", driver)
  .set(JPPFProperties.PARAM_SERVER_PORT, 11111, driver)
  .set(JPPFProperties.PARAM_PRIORITY, 20, driver)
  .set(JPPFProperties.PARAM_POOL_SIZE, 3, driver);