# J2EE Connector
## Overview of the JPPF Resource Adapter
### What is it?
The JPPF Resource Adapter is a JCA-compliant resource adapter module that encapsulates a JPPF client. It provides J2EE application servers with an access to JPPF grid services. It is intended for deployment as either a standalone module or embedded within an enterprise application, while preserving the ease of use of JPPF.
### Features
- Supports the same configuration properties as a standalone JPPF client, including server discovery, connection to multiple drivers, connection pool per driver
- Supports disconnection from, and reconnection to, any JPPF driver
- Compliant with the JCA 1.5 specifications
- API similar to that of the standard JPPF client (submit(job))
- No transaction support
### Architecture

## Supported Platforms
Note: we have not tested all versions of all platforms, thus it is possible that the integration, with the version of the application server you are using, may not work out-of-the-box. We hope that the existing framework and instructions will allow you to adapt the build scripts and code to do so. If you have issues with a specific port, or if you wish to report one that is not specified in this documentation, we invite you to provide your feedback and comments on the JPPF Forums.

Technology	Tested Platforms
Operating System	All Windows systems supporting JDK 1.7 or later All Linux and Unix systems supporting JDK 1.7 or later
JVM	Sun JDK 1.7 and later IBM JVM 1.7 and later BEA JRockit 1.7 and later
Application Server	JBoss 4.x, 5.x, 6.x, 7.x / Wildfly 8.x Glassfish 2.x, 3.x IBM Websphere Application Server 8.5+ Oracle Weblogic 9.x, 10.x, 11.x / Apache Geronimo 2.1.x , 3.0.x

## Configuration and build
### Requirement
For building, configuring and customizing the JPPF Resource Adapter, your will need the latest version of the JPPF source code distribution. It can be found on the JPPF download page. The name of the file should be '''JPPF-2.x-j2ee-connector.zip'''
### Build structure
The J2EE connector has the following folder structure:

Folder	Description
root folder	The root folder, contains the build.xml Ant build script
appserver	contains common and application server-specific configurations for the JPPF resource adapter and the demo application
build	this folder contains all jars, .ear and .rar files resulting from the build
classes	contains the compiled code of the JPPF resource adapter
config	contains application server-specific resources for the deployment of the resource adapter
docroot	contains resources for the build of the demo application on some application servers
src	contains the source code for the resource adapter and demo application.

### Building the JPPF resource adapter
To build the resource adapter:

- Open a command prompt
- Go to the JPPF-x.y-j2ee-connector folder
- Enter “ant build”
- The resulting .rar and .ear files are generated in the “build” subfolder.
### Configuring the resource adapter and demo application
The configuration files and deployment descriptors are all contained in the '''appserver''' folder. The detailed content of this folder is as follows:

Folder	Description
appserver	root folder, contains: / the resource adapter's deployment descriptor ra.xml. It is in this file that you set the configuration parameters for the connection to the JPPF drivers, by setting the values of the configuration properties as follows: / <!-- JPPF Client Configuration --> / <config-property> / <description>Defines how the JPPF configuration is to be located. / This property is defined in the format "type|path", where "type" can be one of: / - "classpath": "path" is a path to a properties file in one of the jars of the .rar file / example: "classpath|resources/config/jppf.properties" / - "url": "path" is a url that points to a properties file / example: "url|file:///home/me/jppf/jppf.properties" (could be a http:// or ftp:// url as well) / - "file": "path" is considered a path on the file system / example: "file|/home/me/jppf/config/jppf.properties" / When no value or an invalid value is specified, "classpath|jppf.properties" is used / </description> / <config-property-name>ConfigurationSource</config-property-name> / <config-property-type>java.lang.String</config-property-type> / <config-property-value>classpath|jppf.properties</config-property-value> / </config-property> / the demo application's deployment desciptor application.xml
appserver/common	contains files common to all application servers, for the demo enterprise application
appserver/<server_name>	root of <server_name>-specific configuration and deployment files. Contains a commons-logging.properties file where you can configure which logging framework will be used (i.e. Log4j, JDK logger, etc...)
appserver/<server_name>/application	contains <server_name>-specific deployment descriptor for the demo application, for example: weblogic-application.xml.
appserver/<server_name>/docroot	contains a <server_name>-specific JSP for the demo application. The specificity is the JNDI name used to look up the JPPF connection factory. It relates to the corresponding resource-ref defined in the web.xml descriptor.
appserver/<server_name>/ra	contains a <server_name>-specific deployment descriptor for the resource adapter. It generally contains the definition of the corresponding JCA connection factory. Not all application servers require one. Example: weblogic-ra.xml.
appserver/<server_name>/WEB-INF	contains the <server_name>-specific deployment descriptors for the demo web application. The specificity is mostly in the resource-ref definition of the JNDI name for the JPPF connection factory. For example: web.xml and jboss-web.xml.

## How to use the connector API
### Obtaining and closing a resource adapter connection
The J2EE connector is accessed via the JPPFConnection interface. This implies that any operation performed should follow these steps:

1. obtain a connection from the resource adapter connection pool
2. perform one or more JPPF-related operation(s)
3. close the connection

The following helper code illustrates how to obtain and release connections from the resource adapter:

import javax.naming.*;
import javax.resource.ResourceException;
import javax.resource.cci.ConnectionFactory;

public class JPPFHelper {
  // JNDI name of the JPPFConnectionFactory.
  public static final String JNDI_NAME = "eis/JPPFConnectionFactory";

  // Obtain a JPPF connection from the resource adapter's connection pool
  public static JPPFConnection getConnection()
    throws NamingException, ResourceException {
    // Perform a JNDI lookup of the JPPF connection factory
    InitialContext ctx = new InitialContext();
    JPPFConnectionFactory factory;
    Object objref = ctx.lookup(JNDI_NAME);
    if (objref instanceof JPPFConnectionFactory) {
      factory = (JPPFConnectionFactory) objref;
    } else {
      factory = (JPPFConnectionFactory) javax.rmi.PortableRemoteObject.narrow(
        objref, ConnectionFactory.class);
    }
    // get a JPPFConnection from the connection factory
    return (JPPFConnection) factory.getConnection();
  }

  // Release a connection
  public static void closeConnection(JPPFConnection conn) throws ResourceException {
    conn.close();
  }
}

Please note that the actual JNDI name for the JPPF connection factory depends on which application server is used:
- on Apache Geronimo: "jca:/JPPF/jca-client/JCAManagedConnectionFactory/eis/JPPFConnectionFactory"
- on JBoss 4-7: "java:eis/JPPFConnectionFactory"
- on Wildfly 8: "java:/eis/JPPFConnectionFactory"
- on Websphere: "java:comp/env/eis/JPPFConnectionFactory"
- on all other supported servers: "eis/JPPFConnectionFactory"
### Reset of the JPPF client
The method JPPFConnection.resetClient() will trigger a reset of the underlying JPPF client. This method enables reloading the JPPF configuration without having to restart the application server. Example use:

JPPFConnection connection = null;
try {
  connection = JPPFHelper.getConnection();
  connection.resetClient();
} finally {
  if (connection != null) JPPFHelper.closeConnection(connection);
}

As for JPPFClient.reset(), calling this method will not lose any already submitted jobs. Instead, the JCA connectior will resubmit them as soon as it is reset and server connections become available.
### Submitting jobs
JPPFConnection provides two methods for submitting jobs:

public interface JPPFConnection extends Connection, JPPFAccessor {
  // Submit a job to the JPPF client
  // This method exits immediately after adding the job to the queue
  String submit(JPPFJob job) throws Exception;

  // Submit a job to the JPPF client and register the specified status listener
  // This method exits immediately after adding the job to the queue
  String submit(JPPFJob job, SubmissionStatusListener listener) throws Exception;
}

You will note that both methods actually perform an asynchronous job submission. They return a unique id for the the submission, which is in fact the job UUID. This id is then used to retrieve the job results and its status.

In the following example, a JPPF job is submitted asynchronously. The submission returns an ID that can be used later on to check on the job status and retrieve its results.

public String submitJob() throws Exception {
  JPPFConnection connection = null;
  try {
    // get a JPPF Connection
    connection = JPPFHelper.getConnection();
    // create a JPPF job
    JPPFJob job = new JPPFJob();
    job.addTask(new DemoTask());
    // Use the connection to submit the JPPF job and obtain a submission ID
    return connection.submit(job);
  } finally {
    // close the connection
    JPPFHelper.closeConnection(connection);
  }
}
### Getting the status and results of a job
Here, we check on the status of a job and process the execution results or the resulting error:

public void checkStatus(String submitId) throws Exception {
  JPPFConnection connection = null;
  try {
    connection = JPPFHelper.getConnection();
    // Use the connection to check the status from the submission ID
    SubmissionStatus status = connection.getSubmissionStatus(submitID);
    if (status.equals(SubmissionStatus.COMPLETE)) {
      // if successful process the results
      List<Task<?>> results = connection.getResults(submitID);
    } else if (status.equals(SubmissionStatus.FAILED)) {
      // if failed process the errors
    }
  } finally {
    JPPFHelper.closeConnection(connection);
  }
}

### Cancelling a job
The J2EE allows cancelling a job by calling the method JPPFConnection.cancelJob(String submitId):

public void cancelJob(String submitId) throws Exception {
  JPPFConnection connection = null;
  try {
    connection = JPPFHelper.getConnection();
    // cancel the job
    connection.cancelJob(submitID);
  } finally {
    JPPFHelper.closeConnection(connection);
  }
}
### Synchronous execution
It is also possible to execute a job synchronously, without having to code the job submission and status checking in two different methods. The JPPFConnection API provides the method awaitResults(String submitID), which waits until the job has completed and returns the execution results. Here is an example use:

// Submit a job and return the execution results
public List<JTask<?>> submitBlockingJob() throws Exception {
  List<Task<?>> results = null;
  JPPFConnection connection = null;
  try {
    connection = JPPFHelper.getConnection();
    // create a new job
    JPPFJob job = new JPPFJob();
    job.setName("test job");
    // add the tasks to the job
    for (int i=0; i<5; i++) job.add(new MyTask(i));
    // submit the job and get the submission id
    String submitID = connection.submit(job);
    // wait until the job has completed
    results = connection.awaitResults(submitID);
  } finally {
    JPPFHelper.closeConnection(connection);
  }
  // now return the results
  return results;
}

Please note that, when using the synchronous submission mode from within a transaction, you must be careful as to how long the job will take to execute. If the job execution is too long, this may cause the transaction to time out and roll back, if the execution time is longer than the transaction timeout.
### Using submission status events
With the J2EE connector, It is possible to subscribe to events occurring during the life cycle of a job.
This can be done via the following two methods:

public interface JPPFConnection extends Connection, JPPFAccessor {
  // Add a status listener to the submission with the specified id
  void addSubmissionStatusListener(
    String submissionId, SubmissionStatusListener listener);

  // Submit a job to the JPPF client and register a status listener
  String submit(JPPFJob job, SubmissionStatusListener listener) throws Exception;
}

Note that submit(JPPFJob, SubmissionStatusListener) submits the job and registers the listener in a single atomic operation. As the job submssion is asynchronous, this ensures that no event is missed between the submission of the job and the registration of the listener.

The interface SubmissionStatusListener is defined as follows:

public interface SubmissionStatusListener extends EventListener {
  // Called when the status of a job has changed
  void submissionStatusChanged(SubmissionStatusEvent event);
}

Each listener receives events of type SubmissionStatusEvent, defined as follows:

public class SubmissionStatusEvent extends EventObject {
  // get the status of the job
  public SubmissionStatus getStatus()

  // get the id of the job
  public String getSubmissionId()
}

The possible statuses are defined in the enumerated type SubmissionStatus:

public enum SubmissionStatus {
  SUBMITTED, // the job was just submitted.
  PENDING, // the job is currently in the submission queue (on the client side)
  EXECUTING, // the job is being executed
  COMPLETE, // the job execution is complete
  FAILED // the job execution has failed
}

Here is an exemple usage of the status listeners:

public void submitWithListener() throws Exception {
  JPPFConnection connection = null;
  try {
    connection = JPPFHelper.getConnection();
    JPPFJob job = new JPPFJob();
    job.add(new DemoTask(duration));

    // a status listener can be added at submission time
    String id = connection.submit(job, new SubmissionStatusListener() {
      public void submissionStatusChanged(SubmissionStatusEvent event) {
        String id = event.getSubmissionId();
        SubmissionStatus status = event.getStatus();
        System.out.println("submission [" + id + "] changed to '" + status + "'");
      }
    });

    // or after the job has been submitted
    connection.addSubmissionStatusListener(id, new SubmissionStatusListener() {
      public void submissionStatusChanged(SubmissionStatusEvent event) {
        String id = event.getSubmissionId();
        SubmissionStatus status = event.getStatus();
        switch(status) {
        case COMPLETE:// process successful completion
        break;
        case FAILED:// process failure
        break;
        default:
        System.out.println("job [" + id + "] changed to '" + status + "'");
        break;
        }
      }
    });
    List<Task<?>> results = connection.awaitResults(id);
    // ... process the results ...
  } finally {
    JPPFHelper.closeConnection(connection);
  }
}
## Deployment on a J2EE application server
### Deployment on JBoss 4.x - 6.x
#### Deploying the JPPF resource adapter
copy the file "'''jppf_ra_JBoss.rar'''" in this folder: <JBOSS_HOME>/server/<your_server>/deploy, where <JBOSS_HOME> is the root installation folder for JBoss, and <your_server> is the server configuration that you use
(JBoss comes with 3 configurations: "default", "minimal" and "all")
#### Creating a connection factory
Create, in the <JBOSS_HOME>/server/<your_server>/deploy folder, a file named jppf-ra-JBoss-ds.xml. Edit this file with a text editor and add this content:

  <?xml version="1.0" encoding="UTF-8"?>
  <connection-factories>
    <no-tx-connection-factory>
      <jndi-name>eis/JPPFConnectionFactory</jndi-name>
      <application-managed-security/>
      <rar-name>jppf_ra_JBoss-rar</rar-name>
      <connection-definition>javax.resource.cci.ConnectionFactory</connection-definition>
      <adapter-display-name>JPPF</adapter-display-name>
      <min-pool-size>0</min-pool-size>
      <max-pool-size>10</max-pool-size>
      <blocking-timeout-millis>50000</blocking-timeout-millis>
      <idle-timeout-minutes>15</idle-timeout-minutes>
    </no-tx-connection-factory>
  </connection-factories>

You can also download this file.
#### Deploying the demo application
Copy the file “JPPF_J2EE_Demo_JBoss-4.0.ear” in the <JBOSS_HOME>/server/<your_server>/deploy folder
### Deployment on JBoss 7+ / Wildfly 8+
#### Deploying the resource adapter
- in the JBoss administration console, go to the "Deployments" view
- remove any existing JPPF deployments (.rar and .ear)

- click on "Add Content"
- browse to the file "jppf_ra_JBoss-7.rar"

- click "next"

- accept the default names and click "Finish"
- back to the "Deployments" view, you should see the deployed resource adapter:

- click on the "Enable" button to start it:

#### Deploying the demo application
- In the "Deployment" view, click on "Add Content" and browse to "JPPF_J2EE_Demo_JBoss-7.ear"

- click on "Next"
- Accept the default names and click on "Finish"
- You should now see the demo web app in the list of deployments:

- click on the "Enable" button to start it:

### Deployment on SunAS / Glassfish
#### Deploying the Resource Adapter
- in Sun AS console, go to "Applications > Connector modules"

- click on "Deploy"
- step 1: browse to the "jppf_ra_Glassfish.rar" file

- click "next"
- step 2: leave all default settings and click "Finish"

#### Creating a connector connection pool
- in the console tree on the left, go to "Resources > Connectors > Connector Connection Pools"

- click on "New"
- step 1: enter "JPPFConnectionPool" as the connection pool name and select "jppf_ra_Glassfish" for the resource adapter

- click "next"
- step 2: set the pool parameters, select "NoTransaction" for transaction support

- click "Finish"
#### Creating a connection factory
- in the console tree on the left, go to "Resources > Connectors > Connector Resources"

- click on "New"
- for the jndi name, enter "eis/JPPFConnectionFactory"
- for the connection pool, select "JPPFConnectionPool"

- click "OK"
- restart the application server

#### Deploying the demo application
- in SunAS console, go to "Applications > Enterprise Applications"

- click on "Deploy"
- step 1: browse to the file "JPPF_J2EE_Demo_Glassfish.ear"

- click "next"
- step 2: leave all default values

- click "Finish"
- restart the application server

### Deployment on Websphere
#### Deploying the Resource Adapter
- in WAS console, go to "Resources > Resource Adapters > Resource adapters"
- select scope = "Node"

- click "Install RAR"

- in the "Install RAR file" page, browse to the "jppf_ra_Websphere.rar" file

- click "Next"
- click "OK"
- click "Save directly to the master configuration"

#### Creating a connection factory
- in the list of resource adapters, click on "JPPF"
- in "Additional Properties", click on "J2C connection factories"
- click on "New"
- enter "JPPF Connection Factory" for the name and "eis/JPPFConnectionFactory" for the JNDI name, leave all other parameters as they are

- click "OK"
- click "Save directly to the master configuration"
- Restart the application server

#### Deploying the demo application
- in Websphere console, go to "Applications > Enterprise Applications"

- click on "Install"
- browse to the file "JPPF_J2EE_Demo_Websphere.ear"
- select "Prompt me only when additional information is required".

- click "Next"
- step 1: click "Next"
- step 2: check module "jppftest"

- click "Next"
- step 3: select "None" for the authentication method
- check the "jppftest" module and enter "eis/JPPFConnectionFactory" as Target Resource JNDI Name

- click "Next"
- step 4: check the "jppftest" module and keep "default_host" as the Virtual host

- click "Next"
- step 5: click "Finish"
- click "Save directly to the master configuration"
- in the list of enterprise applications, check "JPPF Demo"

- click on "Start"
- restart the application server

### Deployment on Weblogic
#### Deploying the resource adapter
- in Weblogic console, go to "Deployments"
- click on "Lock & Edit"

- click "Install"
- navigate to the "jppf_ra_Weblogic.rar" file and select it

- click "Next"
- click "Next"
- click "Finish"

- click "Activate Changes"
- in the list of deployments, check "jppf_ra_Weblogic"
- select "Start > Servicing all requests"

- Click "Yes"
- the state of the resource adapter must now show as "Active"
- restart the application server

Note: In the Weblogic output console, you will probably see periodic messages saying that 2 threads are stuck. These warnings are harmless. The related threads are required by the JPPF resource adapter and should not be interrupted. The period of these warnings is determined by a setting of the Weblogic instance called "Stuck Thread Timer Interval", set to 60 seconds by default. Consult with your administrator if you need to change that interval.
#### Deploying the demo application
- in Weblogic console, go to "Deployments"
- click on "Lock & Edit"

- click "Install"
- navigate to the "JPPF_J2EE_Demo_Weblogic.ear" file and select it

- click "Next"
- click "Finish"

- click "Activate Changes"
- in the list of deployments, check "JPPF_J2EE_Demo_Weblogic"
- select "Start > Servicing All Requests"

- Click "Yes"
- the state of the demo application must now show as "Active"
- restart the application server
### Deployment on Apache Geronimo
#### Deploying the resource adapter
- In the Geronimo administration console, click on “Applications > Deploy new”
- In the “Archive“ field, navigate to the file “jppf_ra_Geronimo.rar”

- click on “Install”
#### Deploying the demo application
- In the Geronimo administration console, click on “Applications > Deploy new”
- In the “Archive“ field, navigate to the file “JPPF_J2EE_Demo_Geronimo.ear”

- click on “Install”
## Packaging your enterprise application
For a J2EE enterprise application to work with the JPPF JCA connector, it is necessary to include a JPPF utility library called jppf-j2ee-client.jar, which can be found in the jca-client/build/lib folder. To ensure that this library can be made visible to all modules in the application, we recommend the following way of packaging it:

* add jppf-j2ee-client.jar in a lib folder under the root of the EAR file
* for each EJB, Web or Resource Adapter module of your application that will use JPPF, add a Class-Path entry in the META-INF/manifest.mf of the module, which will point to the JPPF library, for instance:
  Class-Path: lib/jppf-j2ee-client.jar

In a typical J2EE application, it would look like this:

  MyApplication.ear/

      lib/
        jppf-j2ee-client.jar

      MyEJBModule.jar/
        ...
        META-INF/
        manifest.mf:
        ...
        Class-Path: lib/jppf-j2ee-client.jar
        ...
        ...

      ... other modules ...

      MyWebApp.war/
        ...
        META-INF/
        manifest.mf:
        ...
        Class-Path: lib/jppf-j2ee-client.jar
        ...
        ...

Note: If you only need to use JPPF from a web application or module, then you can simply add jppf-j2ee-client.jar to the WEB-INF/lib folder of the war file.
## Creating an application server port
If the JPPF resource adapter does not include, out-of-the-box, a port for your application server, or your application server version, this section is for you. Here is a sequence of steps to create your own port:

1. copy one of the existing application server-specific folder in JPPF-x.y.z-j2ee-connector/appserver and give it a name that will distinguish it from the others. This name will be used throughout this process, so please make sure it is both unique and meaningful. For the sake of this exercise, we will use a generic name: "MyServer-1.0"

2. After creating the JPPF-x.y.z-j2ee-connector/appserver/MyServer-1.0 folder, edit the relevant configuration files and deployment descriptors.

3. Open the build.xml build script, in the JPPF-x.y.z-j2ee-connector folder, with a text editor.

4. At the start of the file, you will see the following section:

<!-- ========================================================================= -->
<!-- definition of application server-specific properties -->
<!-- the value is used to generate the names of the corresponding EAR and RAR -->
<!-- ========================================================================= -->
<property name="was" value="Websphere"/>
<property name="jboss" value="JBoss"/>
<property name="jboss7" value="JBoss-7"/>
<property name="wildfly8" value="Wildfly-8"/>
<property name="sunas" value="Glassfish"/>
<property name="weblogic" value="Weblogic"/>
<property name="geronimo" value="Geronimo"/>

You can add your own property here, for instance:

<property name="myserver10" value="MyServer-1.0"/>

The property value must be the name of the folder you just created.

5. (optional) navigate to the Ant target "ear.all" and add your own invocation for generating the demo application EAR:

<build.ear appserver="${myserver10}"/>

You may also remove or comment out those you do not need.

6. Navigate to the Ant target "ear.all" and add your own invocation for generating the resource adapter RAR:

<rar appserver="${myserver10}"/>

You may also remove or comment out those you do not need.