# Configuration properties reference
## Server properties

Property name	Default Value	Comments
jppf.server.port	11111	JPPF server port
jppf.management.enabled	true	enable server management
jppf.management.host	computed	management server host
jppf.management.port	11198	management remote connector port
jppf.discovery.enabled	true	enable server broadcast and discovery
jppf.discovery.group	230.0.0.1	UPD broadcast group
jppf.discovery.port	11111	UPD broadcast port
jppf.discovery.broadcast.interval	5000	UDP broadcast interval in milliseconds
jppf.peers	null	space separated list of peer server names
jppf.peer.<name>.server.host	localhost	named peer server host name or address
jppf.peer.<name>.server.port	11111	named peer server port
jppf.peer.dicovery.enabled	false	enable peer discovery
jppf.load.balancing.algorithm	proportional	load balancing algorithm name
jppf.load.balancing.profile	jppf	load balancing parameters profile name
jppf.load.balancing.profile.<profile> / .<parameter>	null	parameter for the named parameters profile
jppf.jvm.options	null	JVM options for the server process
jppf.transition.thread.pool.size	available processors	number of threads performing network I/O
jppf.local.node.enabled	false	enable a node to run in the same JVM
jppf.recovery.enabled	false	enable recovery from hardware failures on the nodes
jppf.recovery.max.retries	3	maximum number of failed pings to the node before the connection is considered broken
jppf.recovery.read.timeout	6000 (6 seconds)	maximum ping response time from the node
jppf.recovery.server.port	22222	port number for the detection of node failure
jppf.recovery.reaper.run.interval	60000 (1 minute)	interval between connection reaper runs
jppf.recovery.reaper.pool.size	available processors	number of threads allocated to the reaper
jppf.nio.connection.check	true	enable network connection checks on write operations
jppf.discovery.broadcast.include.ipv4	null	broadcast to the specified IPv4 addresses (inclusive filter)
jppf.discovery.broadcast.exclude.ipv4	null	don't broadcast to these IPv4 addresses (exclude filter)
jppf.discovery.broadcast.include.ipv6	null	broadcast to the specified IPv6 addresses (inclusive filter)
jppf.discovery.broadcast.exclude.ipv6	null	don't broadcast to these IPv6 addresses (exclude filter)
jppf.ssl.server.port	11443	port number for secure connections
jppf.peer.ssl.enabled	false	toggle secure connections to remote peer servers
jppf.management.ssl.enabled	false	enable JMX via secure connections
jppf.management.ssl.port	11193	secure JMX server port
jppf.redirect.out	null	file to redirect System.out to
jppf.redirect.out.append	false	append to existing file (true) or create new one (false)
jppf.redirect.err	null	file to redirect System.err to
jppf.redirect.err.append	false	append to existing file (true) or create new one (false)

## Node properties

Property name	Default Value	Comments
jppf.server.host	localhost	JPPF server host address
jppf.server.port	11111	JPPF server port
jppf.management.enabled	true	enable server management
jppf.management.host	computed	node's management server host
jppf.node.management.port	11198	node management remote connector port
jppf.discovery.enabled	true	enable server discovery
jppf.discovery.group	230.0.0.1	server discovery: UPD multicast group
jppf.discovery.port	11111	server discovery: UPD multicast port
jppf.discovery.timeout	5000	server discovery timeout in milliseconds
jppf.discovery.include.ipv4	null	IPv4 inclusion patterns for server discovery
jppf.discovery.exclude.ipv4	null	IPv4 exclusion patterns for server discovery
jppf.discovery.include.ipv6	null	IPv6 inclusion patterns for server discovery
jppf.discovery.exclude.ipv6	null	IPv6 exclusion patterns for server discovery
jppf.jvm.options	null	JVM options for the node process
jppf.processing.threads	available processors	number of threads used for tasks execution
jppf.policy.file	null	path to the security policy file, in the node's classpath or file system
jppf.idle.mode.enabled	false	enable the idle mode
jppf.idle.timeout	300000 (5 minutes)	time of keyboard and mouse inactivity before the node is idle, in ms
jppf.idle.poll.interval	1000 (1 second)	frequency of checks for keyboard and mouse inactivity, in ms
jppf.idle.detector.factory	null	implementation of the idle detector factory
jppf.recovery.enabled	false	enable recovery from hardware failures
jppf.recovery.server.port	22222	port number for the detection of hardware failure
jppf.classloader.cache.size	50	size of the class loader cache for the node
jppf.resource.cache.enabled	true	whether the class loader resource cache is enabled
jppf.resource.cache.storage	file	type of storage: either 'file' or 'memory'
jppf.resource.cache.dir	${java.io.tmpdir}	root location of the file-persisted caches
jppf.node.offline	false	whether the node runs in offline mode
jppf.ssl.enabled	false	toggle secure connections
jppf.redirect.out	null	file to redirect System.out to
jppf.redirect.out.append	false	append to existing file (true) or create new one (false)
jppf.redirect.err	null	file to redirect System.err to
jppf.redirect.err.append	false	append to existing file (true) or create new one (false)
jppf.node.provisioning.master	true	master node marker
jppf.node.provisioning.slave	false	slave node marker
jppf.node.provisioning.slave.path.prefix	slave_nodes/node_	path prefix for the root directory of slave nodes
jppf.node.provisioning.slave.config.path	config	directory where slave-specific configuration files are located
jppf.node.provisioning.slave. jvm.options	null	JVM options always added to the slave startup command

## Node screen saver properties

Property name	Default Value	Comments
General properties
jppf.screensaver.enabled	false	enable/disable the screen saver
jppf.screensaver.class	null	class name of an implementation of JPPFScreenSaver
jppf.screensaver.node.listener	null	class name of an implementation of NodeIntegration
jppf.screensaver.title	JPPF screensaver	title of the JFrame used in windowed mode
jppf.screensaver.icon	o/j/n/jppf-icon.gif *	path to the image for the frame's icon (windowed mode)
jppf.screensaver.fullscreen	false	display the screen saver in full screen mode
jppf.screensaver.width	1000	width in pixels (windowed mode)
jppf.screensaver.height	800	height in pixels (windowed mode)
jppf.screensaver.mouse.motion / .close	true	close on mouse motion (full screen mode)
Built-in screen saver (JPPFScreenSaverImpl) properties
jppf.screensaver.handle.collisions	true	handle collisions between moving logos
jppf.screensaver.logos	10	number of moving logos
jppf.screensaver.speed	100	speed of moving logos from 1 to 100
jppf.screensaver.logo.path	o/j/n/jppf_group_small.gif *	path(s) to the moving logo image(s)
jppf.screensaver.centerimage	o/j/n/jppf@home.gif *	path to the larger image at the center of the screen
jppf.screensaver.status.panel / .alignment	center	horizontal alignment of the status panel

* o/j/n means org/jppf/node, a package/folder in jppf-common-node.jar

## Application client and admin console properties

Property name	Default Value	Comments
jppf.drivers	default-driver	space-separated list of driver names
<driver_name>.jppf.server.host	localhost	named driver's address or host name
<driver_name>.jppf.server.port	11111	named driver's port
<driver_name>.jppf.management.host	localhost	named server's management host
<driver_name>.jppf.management.port	11198	named server's management remote connector port
<driver_name>.jppf.management.enabled	true	enable remote management of named server
<driver_name>.jppf.priority	0	named server priority
<driver_name>.jppf.pool.size	1	named server connection pool size
jppf.local.execution.enabled	true	enable remote execution
jppf.local.execution.enabled	false	enable local execution
jppf.local.execution.threads	available processors	maximum threads to use for local execution
jppf.pool.size	1	connection pool size when discovery is enabled
jppf.discovery.enabled	true	enable server discovery
jppf.discovery.group	230.0.0.1	server discovery: UDP multicast group
jppf.discovery.port	11111	server discovery: UDP multicast port
jppf.discovery.include.ipv4	null	IPv4 inclusion patterns for server discovery
jppf.discovery.exclude.ipv4	null	IPv4 exclusion patterns for server discovery
jppf.discovery.include.ipv6	null	IPv6 inclusion patterns for server discovery
jppf.discovery.exclude.ipv6	null	IPv6 exclusion patterns for server discovery
jppf.socket.max-idle	-1	number of seconds a socket connection can remain idle before being closed
jppf.ui.splash	true	enable display of splash screen at startup
jppf.ssl.enabled	false	toggle secure connections
jppf.admin.refresh.interval.stats	1000	interval between updates of the servers stats view
jppf.admin.refresh.interval.topology	1000	interval between updates of the topology views
jppf.admin.refresh.interval.health	3000	interval between updates of the JVM health view
jppf.gui.publish.period	33	interval between updates of the job data view

## Common configuration properties

Property name	Default Value	Comments
jppf.reconnect.initial.delay	1	delay in seconds before the first reconnection attempt
jppf.reconnect.max.time	60	delay in seconds after which reconnection attemps stop.
jppf.reconnect.interval	1	frequency in seconds of reconnection attempts
jppf.object.serialization.class	DefaultJavaSerialization	serialization scheme, a class implementing JPPFSerialization
jppf.data.transform.class	null	optional network data transformation
jppf.socket.buffer.size	32768	receive/send buffer size for socket connections
jppf.socket.tcp_nodelay	true	disable Nagle's algorithm
jppf.socket.keepalive	false	enable / disable keepalive
jppf.temp.buffer.size	32768	size of temporary buffers used in I/O transfers
jppf.ssl.configuration.file	null	SSL configuration in the file system or classpath
jppf.ssl.configuration.source	null	SSL configuration as an arbitrary source

## SSL properties

Property name	Default Value	Comments
jppf.ssl.context.protocol	SSL	SSLContext protocol
jppf.ssl.protocols	null	a list of space-separated enabled protocols
jppf.ssl.cipher.suites	null	enabled cipher suites as space-separated values
jppf.ssl.client.auth	none	SSL client authentication level
jppf.ssl.keystore.file	null	path to the key store in the file system or classpath
jppf.ssl.keytstore.source	null	key store location as an arbitrary source
jppf.ssl.keystore.password	null	plain text key store password
jppf.ssl.keyststore.password.source	null	key store password as an arbitrary source
jppf.ssl.truststore.file	null	path to the trust store in the file system or classpath
jppf.ssl.truststore.source	null	trust store location as an arbitrary source
jppf.ssl.truststore.password	null	plain text trust store password
jppf.ssl.truststore.password.source	null	trust store password as an arbitrary source
jppf.ssl.client.distinct.truststore	false	use a separate trust store for client certificates (server only)
jppf.ssl.client.truststore.file	null	path to the client trust store in the file system or classpath
jppf.ssl.client.truststore.source	null	client trust store location as an arbitrary source
jppf.ssl.client.truststore.password	null	plain text client trust store password
jppf.ssl.client.truststore.password.source	null	client trust store password as an arbitrary source