# Configuration guide
A JPPF grid is composed of many distributed components interacting with each other, often in different environments. While JPPF will work in most environments, the default behavior may not be appropriate or adapted to some situations. Much of the behavior in JPPF components can thus be modified, fine-tuned or sometimes even disabled, via numerous configuration properties. These properties apply to many mechanisms and behaviors in JPPF, including:

- network communication
- management and monitoring
- performance / load-balancing
- failover and recovery

Any configuration property has a default value that is used when the property is not specified, and which should work in most environments. In practice, this means that JPPF can work without any explicitely specified configuration at all.

For a full list of the JPPF configuration properties, do not hesitate to read the chapter Appendix A: configuration properties reference of this manual.
## Configuration file specification and lookup
All JPPF components work with a set of configuration properties. The format of these propertiesis as specified in the Java Properties class. To enable a JPPF component to retrieve thiese properties file, their source must be specified using one of the two, mutually exclusive, system properties:

- jppf.config.plugin = class_name, where class_name is the fully qualified name of a class implementing the interface JPPFConfiguration.ConfigurationSource, enabling a configuration source from any origin, such as a URL, a distributed file system, a remote storage facility, a database, etc.
- jppf.config = path, where path is the location of the configuration file, either on the file system, or relative to the JVM's classpath root. If this system property is not specified, JPPF will look for a default file named "jppf.properties" in the current directory or in the classpath root.

Example use:

java -Djppf.config.plugin=my.own.Configuration ...

or

java -Djppf.config=my/folder/myFile.properties ...

The configuration file lookup mechanism is as follows:

1. if jppf.plugin.config is specified
  a) instantiate an object of the specified class name and read the properties via the stream provided by this object's getPropertyStream() method.
  b) if, for any reason, the stream cannot be obtained or reading the properties from it fails, go to 3.
2. else if jppf.config is specified
  1. look for the file in the file system
  2. if not found in the file system, look in the classpath
  3. if not found in the classpath use default configuration values
3. if jppf.config is not specified
  1. use default file "jppf.properties"
  2. look for "jppf.properties" in the file system
  3. if not found in the file system, look for it in the classpath
  4. if not found in the classpath use default configuration values

A practical side effect of this mechanism is that it allows us to place a configuration file in the classpath, for instance packaged in a jar file, and override it if needed with an external file, since the the file system is always looked up first.
## Reminder: JPPF topology
Before reviewing the details of each configuration property, it is useful to have the big picture of what we are configuring exactly. In a few words, a JPPF grid is made of clients (instances of your applications), servers and nodes. An application submits jobs to a server, and a server distributes the tasks in each job to its attached nodes. The simplest configuration you can have would be as illustrated in this picture:

We can see here that we have a single client communicating with one server, to which a single node is attached. In practice, there will be many nodes attached to the server, and many clients will be able to communicate with the server concurrently. It is also possible to link servers together, forming a peer-to-peer network of JPPF servers, allowing servers to delegate a part of their workload to other servers.
We could effectively build a much more complex JPPF network, such as the one in this picture:

The role of the configuration will be essentially to determine where each component can find the others, and how their interactions will be processed.
## Configuring a JPPF server
### Basic network configuration
The server network communication mechanism uses TCP/IP. To do its basic work of receiving jobs and dispatching them for execution, 3 TCP ports are required:

- one port is reserved for the distributed class loader, and is also used by clients, nodes and other servers
- another port is reserved for the communication with the clients, to receive job requests and send the results
- the third port is reserved to communication with the nodes, and is used to dispatch jobs and tasks to the nodes, and receive the results of their execution. It is also used to delegate jobs to other servers.

In the configuration file, these properties would be defined as follows, with their default values:

  # class loader port
  class.server.port = 11111
  # communication with the client applications
  app.server.port = 11112
  # communication with the nodes
 node.server.port = 11113

Note that not defining these properties is equivalent to assigning them their default value.
### Server discovery
By default, JPPF nodes and clients are configured to automatically discover active servers on the network. This is made possible because, by default, a JPPF server will broadcast the required information (i.e. host address and port numbers) using the UDP multicast mechanism. This mechanism itself is configurable, by setting the following properties:

  # Enable or disable automatic discovery of JPPF drivers
 jppf.discovery.enabled = true

  # UDP multicast group to which drivers broadcast their connection parameters
 jppf.discovery.group = 230.0.0.1
 # UDP multicast port to which drivers broadcast their connection parameters
 jppf.discovery.port = 11111
 # How long a driver should wait between 2 broadcasts, in milliseconds
 jppf.discovery.broadcast.interval = 1000

The values indicated above are the default values. Note that, given the nature of the UDP protocol, the broadcast data is transient, and has to be re-sent at regular intervals to allow new nodes or clients to find the information. The broadcast interval property allows some control over the level of network traffic ("chattyness") thus generated.
### Connecting to other servers
We have seen in section 4.2 that servers can connect to each other, up to a full-fledged peer-to-peer topology. When a server A connects to another server B, A will act as a node attached to B (from B's perspective). Based on this, there are 4 possible kinds of connectivity between 2 servers:

- A and B are not connected at all
- A is connected to B (i.e. A acts as a node attached to B)
- B is connected to A (i.e. B acts as a node attached to A)
- A and B are connected to each other

There are 2 ways to define a connection from a server to other servers on the network:

Using automatic discovery

In this scenario, we must enable the discovery of peer servers:

  # Enable or disable auto-discovery of other peer servers (defaults to false)
  jppf.peer.discovery.enabled = true

For this to work, the server broadcast must be enabled on the peer server(s), and the properties defined in the previous section 4.3.2 will be used, hence they must be set to the same values on the other server(s). A server can discover other servers without having to broadcast its own connection information (i.e. without being "discoverable").

Please note that the default value for the above property is "false". Setting the default to "true" would imply that each server would connect to all other servers accessible on the network, with a high risk of unwanted side effects.

Manual connection to peer servers

This will be best illustrated with an example configuration:

  # define a space-separated list of peers to connect to
 jppf.peers = server_1 server_2
  # connection to server_1
  jppf.peer.server_1.server.host = host_1
 class.peer.server_1.server.port = 11111
 node.peer.server_1.server.port = 11113
  # connection to server_2
  jppf.peer.server_2.server.host = host_2
 class.peer.server_2.server.port = 11111
 node.peer.server_2.server.port = 11113

To connect to each peer, we must define its IP address or host name as well as two port numbers: one for the server's distributed class loader and the other for server to dispatch jobs. Please note that the value we have defined for " class.peer.server_1.server.port" must be the same as the one defined for "class.server.port" in server_1's configuration, and the value for "node.peer.server_1.server.port" must be equal to that of "node.server.port" in server_1's configuration.
### JMX management configuration
JPPF uses JMX to provide remote management capabilities for the servers, and uses the default RMI connector for communication. Each server has its own embedded RMI registry.

The management features are enabled by default; this behavior can be changed by setting the following property:

  # Enable or disable management of this server
  jppf.management.enabled = true

When management is enabled, the following properties must be defined:

  # JMX management host IP address. If not specified (recommended), the first non-local
  # IP address (i.e. neither 127.0.0.1 nor localhost) on this machine will be used.
  # If no non-local IP is found, localhost will be used.
 jppf.management.host = localhost
 # JMX management port, used by the remote JMX connector
 jppf.management.port = 11198
 # Internal RMI port used by JMX management
 jppf.management.rmi.port = 12198

Let's see in more details the usage of each of these properties:

- jppf.management.host: defines the host name or IP address for the remote management and monitoring of the servers and nodes. It represents the host where an RMI registry is running. When this property is not defined explicitely, JPPF will automatically fetch the first non-local IP address (meaning not the loopback address) it can find on the current host. If none is found, ''localhost'' will be used. This provides a way to use an identical configuration for all the servers on a network.
- jppf.management.port: defines the port number for connecting to the Mbean server. The default value for this property is '''11198'''. If 2 nodes, 2 drivers or a driver and a node run on the same host, they must have a different value for this property.
- jppf.management.rmi.port: this is the port number used by the embedded RMI registry. It is only used internally by the server, however its value must be distinct from that of any other server or node running on the same machine. The default value for this property is '''12198'''.

Note: if a management port is already in use by another JPPF component or application, JPPF will automatically increment it, until it finds an available port number. This means that you can in fact leave the port numbers to their default values (or not specify them at all), as JPPF will automatically ensure that valid unique port numbers are used.
### Load-balancing
The distribution of the tasks to the nodes is performed by the JPPF driver. This work is actually the main factor of the observed performance of the framework. It consists essentially in determining how many tasks will go to each node for execution, out of a set of tasks sent by the client application. Each set of tasks sent to a node is called a "bundle", and the role of the load balancing (or task scheduling) algorithm is to optimize the performance by adjusting the number of task sent to each node.

The algorithm to use is configured with the following property:

  jppf.load.balancing.algorithm = <algorithm_name>

The algorithm name can be one of those prefefined in JPPF, or a user-defined one. We will see how to define a custom alogrithm in Chapter 6 Extending JPPF of this manual. JPPF now has 4 predefined load-balancing algorithms to compute the distribution of tasks to the nodes, each with its own configuration parameters. These algorithms are:

- “manual” : each bundle has a fixed number of tasks, meaning that each will receive at most this number of tasks
- “autotuned” : adaptive heuristic algorithm based on the Monte Carlo algorithm
- “proportional” : an adaptive deterministic algorithm based on the contribution of each node to the overall mean task execution time
- “rl” : adaptive algorithm based on an artificial intelligence technique called “reinforcement learning”

The predefined possible values for the property jppf.load.balancing.algorithm are thus: manual, autotuned, proportional and rl. The default is manual, for example:

  jppf.load.balancing.algorithm = proportional
Each algorithm uses its own set of parameters, which define together a strategy for the algorithm, It is also called a performance profile or simply profile, and we will use these terms interchangeably. A strategy has a name that serves to identify a group of parameters and their values, using the following pattern:

  jppf.load.balancing.strategy = <profile_name>

  strategy.<profile_name>.<parameter_1> = <value_1>
  ...
  strategy.<profile_name>.<parameter_n> = <value_n>

Using this, you can define multiple profiles and easily switch from one to the other, by simple changing the value of jppf.load.balancing.strategy. It is also possible to mix, in a single profile, the parameters for multiple algorithms, however it is not recommended, as there may be name collisions.

To illustrate this, we will give a sample profile for each of the predefined algorithms:

“manual” algorithm

  # algorithm name
 jppf.load.balancing.algorithm = manual
 # name of the set of parameter values or profile for the algorithm
 jppf.load.balancing.strategy = manual_profile
 # "manual" profile
 strategy.manual_profile.size = 1

“autotuned” algorithm

  # algorithm name
  jppf.load.balancing.algorithm = autotuned

  # name of the set of parameter values or profile for the algorithm
  jppf.load.balancing.strategy = autotuned_profile

  # "autotuned" profile
  strategy.autotuned_profile.size = 5
  strategy.autotuned_profile.minSamplesToAnalyse = 100
  strategy.autotuned_profile.minSamplesToCheckConvergence = 50
  strategy.autotuned_profile.maxDeviation = 0.2
  strategy.autotuned_profile.maxGuessToStable = 50
  strategy.autotuned_profile.sizeRatioDeviation = 1.5
  strategy.autotuned_profile.decreaseRatio = 0.2

“proportional” algorithm

  # algorithm name
  jppf.load.balancing.algorithm = proportional

  # name of the set of parameter values or profile for the algorithm
  jppf.load.balancing.strategy = proportional_profile

  # "proportional" profile
  strategy.proportional_profile.size = 5
  strategy.proportional_profile.performanceCacheSize = 3000
  strategy.proportional_profile.proportionalityFactor = 2

“rl” algorithm

  # algorithm name
  jppf.load.balancing.algorithm = rl

  # name of the set of parameter values or profile for the algorithm
  jppf.load.balancing.strategy = rl_profile

  # "rl" profile
  strategy.rl_profile.performanceCacheSize = 3000
  strategy.rl_profile.performanceVariationThreshold = 0.001
### Server process configuration
A JPPF server is in fact made of two processes: a “controller” process and a “server” process. The controller launches the server as a separate process and watches its exit code. If the exit code has a pre-defined value of 2, then it will restart the server process, otherwise it will simply terminate. This mechanism allows the remote (eventually delayed) restart of a server using the management APIs or the management console. It is also made such that, if any of the two processes dies unexpectedly, then the other process will die as well, leaving no lingering Java process in the OS.

The server process inherits the following parameters from the controller process:

- location of jppf configuration file (-Djppf.config)
- current directory
- environment variables
- Java class path

It is possible to specify additional JVM parameters for the server process, using the configuration property jppf.jvm.options, as in this example:

  jppf.jvm.options = -Xms64m -Xmx512m

Here is another example with remote debugging options:

  jppf.jvm.options = -Xmx512m -server \
   -Xrunjdwp:transport=dt_socket,address=localhost:8000,server=y,suspend=n

It is possible to specify additional class path elements through this property, by adding one or more “-cp” or “-classpath” options (unlike the Java command which only accepts one). For example:

   jppf.jvm.options = -cp lib/myJar1.jar:lib/myJar1.jar -Xmx512m \
     -classpath lib/external/externalJar.jar
### Recovery from hardware failures of remote nodes
Network disconnections due to hardware failures are notoriously difficult to detect, let alone recover from. JPPF implements a configurable mechanism that enables detecting such failures, and recover from them, in a reasonable time frame. This mechanism works as follows:

- the node establishes a specific connection to the server, dedicated to failure detection
- at connection time, a handshake protocol takes place, where the node communicates a unique id (UUID) to the server, that can be correlated to other connections for this node (i.e. job server and distributed class loader)
- at regular intervals (heartbeats), the server will send a very short message to the node, which it expects the node to acknowledge by sending a short response of its own
- if the node's response is not received in a specified time frame, and this, a specified number of times in a row, the server will consider the connection to the node broken, will close it cleanly, close the associated connections, and handle the recovery, such as requeing tasks that were being executed by the node for execution on another node

In practice, the polling of the nodes is performed by a “reaper” object that will handle the querying of the nodes, using a pool of dedicated threads rather than one thread per node. This enables a higher scalability with a large number of nodes.

The ability to specify multiple attempts at getting a response from the node is useful to handle situations where the network is slow, or when the node or server is busy with a high CPU utilization level.On the server side, the parameters of this mechanism are configurable via the following properties:

  # Enable recovery from hardware failures on the nodes.
  # Default value is true (enabled).

  jppf.recovery.enabled = true

  # Maximum number of attempts to get a response form the node before the
  # connection is considered broken. Default value is 3.

  jppf.recovery.max.retries = 3

  # Maximum time in milliseconds allowed for each attempt to get a response
  # from the node. Default value is 6000 (6 seconds).

  jppf.recovery.read.timeout = 3000

  # Dedicated port number for the detection of node failure.
  # Default value is 22222.

  jppf.recovery.server.port = 22222

  # Interval in milliseconds between two runs of the connection reaper.
  # Default value is 60000 (1 minute).

  jppf.recovery.reaper.run.interval = 60000

  # Number of threads allocated to the reaper.
  # Default value is the number of available CPUs.

  jppf.recovery.reaper.pool.size = 8

### Full server configuration file (default values)
To link all the parts together, here is a sample server configuration file that can be reused as is:

  # port number for the class server that performs remote class loading
  class.server.port = 11111
  # port number the clients / applications connect to
  app.server.port = 11112
  # port number the nodes connect to
  node.server.port = 11113

  # Enabling JMX features
  jppf.management.enabled = true
  # JMX management host IP address
  #jppf.management.host = localhost
  # JMX management port
  jppf.management.port = 11198
  # Internal RMI port used by JMX management
  jppf.management.rmi.port = 12198

  # Enable/Disable automatic discovery of JPPF drivers
  jppf.discovery.enabled = true
  # UDP multicast group to which drivers broadcast their connection parameters
  jppf.discovery.group = 230.0.0.1
  # UDP multicast port to which drivers broadcast their connection parameters
  jppf.discovery.port = 11111
  # How long a driver should wait between 2 broadcasts, in milliseconds
  jppf.discovery.broadcast.interval = 1000
  # Enable/disable auto-discovery for peer-to-peer communication between drivers
  jppf.peer.discovery.enabled = false

  # Load-balancing algorithm
  jppf.load.balancing.algorithm = proportional
  # parameters profile name
  jppf.load.balancing.strategy = proportional_profile

  # "manual" profile
  strategy.manual_profile.size = 1

  # "autotuned" profile
  strategy.autotuned_profile.size = 5
  strategy.autotuned_profile.minSamplesToAnalyse = 100
  strategy.autotuned_profile.minSamplesToCheckConvergence = 50
  strategy.autotuned_profile.maxDeviation = 0.2
  strategy.autotuned_profile.maxGuessToStable = 50
  strategy.autotuned_profile.sizeRatioDeviation = 1.5
  strategy.autotuned_profile.decreaseRatio = 0.2

  # "proportional" profile
  strategy.proportional_profile.size = 5
  strategy.proportional_profile.performanceCacheSize = 3000
  strategy.proportional_profile.proportionalityFactor = 2

  # "rl" profile
  strategy.rl_profile.performanceCacheSize = 3000
  strategy.rl_profile.performanceVariationThreshold = 0.001

  # Other JVM options added to the java command line when the server is started
  # as a subprocess. Multiple options are separated by spaces
  jppf.jvm.options = -server -Xmx256m
## Node configuration
### Server discovery
By default, JPPF nodes are configured to automatically discover active servers on the network. As we have seen in 4.3.2 , this is possible thanks to the UDP broadcast mechanism of the server. On the other end, the node needs to join the same UDP group to subscribe to the bradcasts from the server, which is done by configuring the following properties:

  # Enable or disable automatic discovery of JPPF drivers
 jppf.discovery.enabled = true

  # UDP multicast group to which drivers broadcast their connection parameters
 jppf.discovery.group = 230.0.0.1
 # UDP multicast port to which drivers broadcast their connection parameters
 jppf.discovery.port = 11111

  # How long in milliseconds the node will attempt to automatically discover a driver
 # before falling back to the manual configuration parameters
 jppf.discovery.timeout = 5000

  # IPv4 address inclusion patterns
  jppf.discovery.include.ipv4 =

  # IPv4 address exclusion patterns
  jppf.discovery.exclude.ipv4 =

  # IPv6 address inclusion patterns
  jppf.discovery.include.ipv6 =

  # IPv6 address exclusion patterns
  jppf.discovery.exclude.ipv6 =

For the node to actually find a server on the network, the values for the group and port must be the same for a node and at least one server. If multiple servers are found on the network, the node will arbitrarily pick one.

Note the property jppf.discovery.timeout: if defines a fall back strategy that wil cause the node to connect to the server defined in the manual configuration parameters (see 4.4.2 ) after the specified time.

The last four properties define inclusion and exclusion patterns for IPv4 and IPv6 addresses. Each of them defines a list of comma- or semicolumn- separated patterns. For the syntax of the IPv4 patterns, please refer to the Javadoc for the class IPv4AddressPattern, and to IPv6AddressPattern for IPv6 patterns syntax.
This enables filtering out unwanted IP addresses: the discovery mechanism will only allow addresses that are included and not excluded.

Let's take for instance the following pattern specifications:

  jppf.discovery.include.ipv4 = 192.168.1.
  jppf.discovery.exclude.ipv4 = 192.168.1.100-

The inclusion pattern only allows IP addresses in the range 192.168.1.0 ... 192.168.1.255
The exclusion pattern filters out IP addresses in the range 192.168.1.100 ... 192.168.1.255
Thus, we actually defined a filter that only accepts addresses in the range 192.168.1.0 ... 192.168.1.100

Instead of these 2 patterns, we could have simply defined the following equivalent inclusion pattern:

  jppf.discovery.include.ipv4 = 192.168.1.0-99
### Manual network configuration
If server discovery is disabled, network access to a server must be configured manually. To this effect, the node requires the address of host on which the server is running, and 2 TCP ports, as shown in this example:

  # IP address or host name of the server
  jppf.server.host = my_host
  # class loader port
  class.server.port = 11111
 # communication between node and server
 node.server.port = 11113

To not define these properties is equivalent to assigning them their default value (i.e. “localhost” for the host address).
### JMX management configuration
JPPF uses JMX to provide remote management capabilities for the nodes, and uses the default RMI connector for communication. Each server has its own embedded RMI registry.

The management features are enabled by default; this behavior can be changed by setting the following property:

  # Enable or disable management of this node
  jppf.management.enabled = true

When management is enabled, the following properties must be defined:

  # JMX management host IP address. If not specified (recommended), the first non-local
  # IP address (i.e. neither 127.0.0.1 nor localhost) on this machine will be used.
  # If no non-local IP is found, localhost will be used.
 jppf.management.host = localhost
 # JMX management port, used by the remote JMX connector
 jppf.management.port = 11198
 # Internal RMI port used by JMX management
 jppf.management.rmi.port = 12198

These properties have the same meaning and usage as for a server, as described in 4.3.4 .
### Recovery and failover
When the connection to a server is interrupted, the node will automatically attempt, for a given length of time, and at regular intervals, to reconnect to the same server. These properties are configured as follows, with their default values:

  # number of seconds before the first reconnection attempt
 reconnect.initial.delay = 1
 # time after which the system stops trying to reconnect, in seconds
 # a value of zero or less means it never stops
  reconnect.max.time = 60
 # time between two connection attempts, in seconds
 reconnect.interval = 1

With these values, we have configured the recovery mechanism such that it will attempt to reconnect to the server after a 1 second delay, for 60 seconds and with connection attemps at 1 second intervals.
### Interaction of failover and server discovery
When dicovery is enabled for the node (jppf.dicovery.enabled = true) and the maximum reconnection time is not infinite (reconnect.max.time = <strictly_positive_value>), a sophisticated failover mechanism takes place, following the sequence of steps below:

- the node attempts to reconnect to the driver to which it was previously connected (or attempted to connect), during a maximum time specified by the configuration property "reconnect.max.time"
- during this maximum time, it will make multiple attempts to connect to the same driver. This covers the case when the driver is restarted in the mean time.
- after this maximum time has elapsed, it will attempt to auto-discover another driver, during a maximum time, specified via the configuration property "jppf.discovery.timeout" (in milliseconds)
- if the node still fails to reconnect after this timeout has expired, it will fall back to the driver manually specified in the node's configuration file
- the cycle starts again
### Recovery from hardware failures
The mechanism to recover from hardwaire failure has its counterpart on each node, which works as follows:

- the node establishes a specific connection to the server, dedicated to failure detection
- at connection time, a handshake protocol takes place, where the node communicates a unique id (UUID) to the server
- the node will then attempt to get a message from the server (“check” message).
- if the message from the server is not received in a specified time frame, and this, a specified number of times in a row, the node will consider the connection to the server broken, will close it cleanly, and let the recovery and failover mechanism take over, as described in the previous section “4.4.5”

The following configuration properties are those required by the nodes' hardware failure recovery mechanism implemented by the server:

  # Enable recovery from hardware failures on the node. Default is true (enabled).
  jppf.recovery.enabled = true

  # Dedicated port number for the detection of node failure, must be the same as
  # the value specified in the server configuration. Default value is 22222.
  jppf.recovery.server.port = 22222

  # Maximum number of attempts to get a message from the server before the
  # connection is considered broken. Default value is 2.
  jppf.recovery.max.retries = 2

  # Maximum time in milliseconds allowed for each attempt to get a message
  # from the server. Default value is 60000 (1 minute).
  jppf.recovery.read.timeout = 60000
### Processing threads
A node can process multiple tasks concurrently, using a pool of threads. The size of this pool is configured as follows:

  # number of threads running tasks in this node
 processing.threads = 4

If this property is not defined, its value defaults to the number of processors or cores available to the JVM.
### Node process configuration
In the same way as for a server (see 4.3.6 Server process configuration), the node is made of 2 processes. In addition to the properties and environment inherited from the controller process, it is possible to specify other JVM options via the following configuration property:
  jppf.jvm.options = -Xms64m -Xmx512m

As for the server, it is possible to specify additional class path elements through this property, by adding one or more “-cp” or “-classpath” options (unlike the Java command which only accepts one). For example:

   jppf.jvm.options = -cp lib/myJar1.jar:lib/myJar1.jar -Xmx512m
### Security policy
To limit what the nodes can do on the machine that hosts them, It is possible to specify what permissions are granted to them on their host. These permissions are based on the Java security policy model.

To implement security, nodes require a security policy file. The syntax of this file is similar to that of Java security policy files, except that it only accepts permission entries (no grant or security context entries).

Some examples of permission entries:

  // permission to read, write, delete node log file in current directory
  permission java.io.FilePermission "${user.dir}/jppf-node.log", "read,write,delete";
  // permission to read all log4j system properties
  permission java.util.PropertyPermission "log4j.*", "read";
  // permission to connect to a MySQL database on the default port on localhost
  permission java.net.SocketPermission "localhost:3306", "connect,listen";

To enable the security policy, the node configuration file must contain the following property definition:

  # Path to the security file, relative to the current directory or classpath
  jppf.policy.file = jppf.policy

When this property is not defined, or the policy file cannot be found, security is disabled.

The policy file does not have to be local to the node. If it is not present locally, the node will download it from the server. In this case it has to be locally accessible by the server, and the path to the policy file will be interpreted as path on the server's file system. This feature, combined with the ablity to remotely restart the nodes, allows to easily update and propagate changes to the security policy for all the nodes.
### Full node configuration file (default values)
  # Host name, or ip address, of the host the JPPF driver is running on
  jppf.server.host = localhost

  # port number for the class server that performs remote class loading
  class.server.port = 11111

  # port number the nodes connect to
  node.server.port = 11113

  # Enabling JMX features
  jppf.management.enabled = true

  # JMX management host IP address
  #jppf.management.host = localhost

  # JMX management port
  jppf.management.port = 12001

  # Internal RMI port used by JMX management
  jppf.management.rmi.port = 13001

  # path to the JPPF security policy file
  #jppf.policy.file = config/jppf.policy

  # Enable/Disable automatic discovery of JPPF drivers
  jppf.discovery.enabled = true

  # UDP multicast group to which drivers broadcast their connection parameters
  jppf.discovery.group = 230.0.0.1
    # UDP multicast port to which drivers broadcast their connection parameters
  jppf.discovery.port = 11111
  # How long the node will attempt to automatically discover a driver before
  # falling back to the parameters specified in this configuration file
  jppf.discovery.timeout = 5000

  # Automatic recovery: number of seconds before the first reconnection attempt
  reconnect.initial.delay = 1

  # Time after which the system stops trying to reconnect, in seconds
  reconnect.max.time = 60

  # Automatic recovery: time between two connection attempts, in seconds
  reconnect.interval = 1

  # Processing Threads: number of threads running tasks in this node
  #processing.threads = 1

  # Other JVM options added to the java command line when the node is started as
  # a subprocess. Multiple options are separated by spaces
  jppf.jvm.options = -server -Xmx256m
## Client and administration console configuration
### Server discovery
By default, JPPF clients are configured to automatically discover active servers on the network. This mechanism works in the same way as for the nodes, and uses the same configuration properties, except for the discovery timeout:

  # Enable or disable automatic discovery of JPPF drivers
 jppf.discovery.enabled = true

  # UDP multicast group to which drivers broadcast their connection parameters
 jppf.discovery.group = 230.0.0.1
  # UDP multicast port to which drivers broadcast their connection parameters
 jppf.discovery.port = 11111

  # IPv4 address inclusion patterns
  jppf.discovery.include.ipv4 =

  # IPv4 address exclusion patterns
  jppf.discovery.exclude.ipv4 =

  # IPv6 address inclusion patterns
  jppf.discovery.include.ipv6 =

  # IPv6 address exclusion patterns
  jppf.discovery.exclude.ipv6 =

A major difference is that, when discovery is enabled, the client does not stop attempting to find one or more servers. A client can also connect to multiple servers, and will effectively connect to every server it discovers on the network.

A client can also create mutliple connections to each discovered server, effectively creating a connection pool that can be used for concurrent job submissions. The size of the connection pools is configured with the following property:

  # connection pool size for each discovered server; defaults to 1 (single connection)
  jppf.pool.size = 5

Each server connection has an assigned name, following the pattern: “driver-<n>[-<p>]”, where n is a driver number, in order of discovery, and the optional p is the connection number, if the defined connection pool size is greater than 1.

For instance:

- if we defined jppf.pool.size = 1, the first discovered driver will have 1 connection named “driver-1”
- if we defined jppf.pool.size = 2, the first discovered driver will have 2 connections named “driver-1-1” and “driver-1-2”

The inclusion and exclusion pattern definitions work exactly in the same way as for the node confiugration. Please refer to section 4.4.1 for more details.
### Manual network configuration
As we have seen, a JPPF client can connect to multiple drivers. The first step will this be to name these drivers:

  # space-separated list of drivers this client may connect to
  # defaults to “default-driver”
 jppf.drivers = driver-1 driver-2

Then for each driver, we will define the connection and behavior attributes, including:

Connection to the JPPF server

  # host name, or ip address, of the host the JPPF driver is running on
 driver-1.jppf.server.host = localhost
 # port number for the class server that performs remote class loading
 driver-1.class.server.port = 11111
 # port number the clients / applications connect to
 driver-1.app.server.port = 11112

Here, driver-1.class.server.port and driver-1.app.server.port must have the same value as the corresponding properties class.server.port and app.server.port defined in the server configuration.

Connection pool size

  # size of the pool of connections to this driver
  driver-1.jppf.pool.size = 5

This allows the creation of a connection pool with a specific size for each server we connect to, whereas all pools would have the same size when server discovery is enabled.

Priority

  # assigned driver priority
  driver-1.priority = 10

The priority assigned to a server connection enables the defintion of a fallback strategy for the client. In effect, the client will always use connections that have the highest priority. If the connection with the server is interrupted, then the client we use connections with the next highest priority in the remaining accessible server connection pools.

Connection to the management server

  # management host for this driver
  driver-1.jppf.management.host = localhost
  # management port for this driver
  driver-1.jppf.management.port = 11198

This will allow direct access to the driver's JMX server using the client APIs, unless the client configuration property jppf.management.enabled is set to false.
### Recovery and failover
As for the nodes, when the connection to a server is interrupted, the client will automatically attempt to reconnect to the same server. This is configured as follows, with the default values:

  # number of seconds before the first reconnection attempt
 reconnect.initial.delay = 1
 # time after which the system stops trying to reconnect, in seconds
 # a value of zero or less means it never stops
  reconnect.max.time = 60
 # time between two connection attempts, in seconds
 reconnect.interval = 1

With these values, we have configured the recovery mechanism such that it will attempt to reconnect to the server after a 1 second delay, for 60 seconds and with connection attemps at 1 second intervals.
### Local execution
It is possible for a client to execute jobs locally (i.e. in the client JVM) rather than by submitting them to a server. This feature allows taking advantage of muliple CPUs or cores on the client machine, while using the exact same APIs as for a distributed remote execution. I can also be used for local testing and debugging before performing the “real-life” execution of a job.

Local execution is disabled by default. To enable it, set the following configuration property:

  # enable local job execution; defaults to false
 jppf.local.execution.enabled = true

Local execution uses a pool of threads, whose size is configured as follows:

  # number of threads to use for local execution
 # the default value is the number of CPUs or cores available to the JVM
 jppf.local.execution.threads = 4

It is also possible to mix local and remote execution. This will happen whenever the client is connected to a server and has local execution enabled. In this case, the JPPF client uses an adaptive load-balancing alogrithm to balance the workload between local execution and node-side execution.
### Full client configuration file (default values)
  # list of drivers this client may connect to
  jppf.drivers = driver-1 driver-2

  # host name, or ip address, of the host the JPPF driver is running on
  driver-1.jppf.server.host = localhost
  # port number for the class server that performs remote class loading
  driver-1.class.server.port = 11111
  # port number the clients / applications connect to
  driver-1.app.server.port = 11112

  # priority given to the driver connection
  driver-1.priority = 10

  # host name for the management server
  driver-1.jppf.management.host = localhost
  # port number for the management server
  driver-1.jppf.management.port = 11198

  # configuration for connection driver-2
  driver-2.jppf.server.host = my.host.com
  driver-2.class.server.port = 11121
  driver-2.app.server.port = 11122
  driver-2.jppf.management.port = 12003
  driver-2.priority = 10

  # enable/disable automatic discovery of JPPF drivers
  jppf.discovery.enabled = true
  # UDP multicast group to which drivers broadcast their connection parameters
  jppf.discovery.group = 230.0.0.1
  # UDP multicast port to which drivers broadcast their connection parameters
  jppf.discovery.port = 11111

  # automatic recovery: number of seconds before the first reconnection attempt
  reconnect.initial.delay = 1
  # time after which the system stops trying to reconnect, in seconds
  reconnect.max.time = 60
  # automatic recovery: time between two connection attempts, in seconds
  reconnect.interval = 1